## Slide 1: TRILL OAM use of CFM
Tissa Senevirathne (Cisco)
tsenevir@cisco.com

## Slide 2: Motivation
Common OAM architecture and protocol suite between SDOs
  Not limited to TRILL, but potential use in other overlay protocols
Single toolkit for customers
  Savings in training
  Savings in OPEX (more efficient troubleshooting)
Increase CFM footprint to areas that it has not been widely used so far
Reduced R&D time and hence faster time to market

## Slide 3
MEP for TRILL RBridge
MEP for 802.1 bridge
MIP for 802.1 bridge
MD Level 0 … 7
TRILL
MD Level 0…7
MD Level 0…7
802.1 device
802.1 device
TRILL device
TRILL device
TRILL device
Nested MP Interaction
MIP for TRILL RBridge
802.1 customer
MD Levels
Link MD Levels

## Slide 4: Ask from IEEE 8021
Allocate 4 Opcodes
  See Section 8.2 of ref-3
    Path Trace Reply
    Path Trace Message
    Multicast Tree verification Reply
    Multicast Tree verification Message
Allocate block of 32 TLVs for IETF specific information
  See section 8.4.2 of ref-3

## Slide 5: MIB Layer
TRILL OAM MIB is implemented as an augmentation to CFM MIB
  Allows easy implementation of nested OAM

## Slide 6: References for TRILL OAM
Requirement RFC 6905
Framework draft-ietf-trill-oam-framework-04
Fault Management draft-ietf-trill-oam-fm-01
MIB draft-ietf-trill-oam-mib-00
Loss and Delay Measurement draft-ietf-trill-loss-delay-00