| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Text Proposed of Symbol Structure for HR-Network OFDMA PHY |
| Date Submitted | 2011-05-09 |
| Source(s) | Liru Lu (Alina), Xin Zhang, Masayuki Oodo, Ming-Tuo Zhou, Vinh Dien Hoang, Hiroshi Harada NICT | E-mail: liru@nict.com.sg; zhangxin@nict.com.sg; moodo@nict.go.jp; mingtuo@nict.com.sg; hvdien@nict.com.sg; harada@nict.go.jp |
| Re: | Call for Comments for 802.16n AWD |
| Abstract | In this contribution, we propose text of symbol structure for 802.16n OFDMA PHY. |
| Purpose | To discuss and adopt the proposed text in the 802.16n draft Text |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Copyright Policy | The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Text Proposed of Symbol Structure for HR-Network OFDMA PHY

Liru Lu (Alina), Xin Zhang, Masayuki Oodo

Ming-Tuo Zhou, Vinh Dien Hoang, Hiroshi Harada

NICT

# 1. Introduction

In Doc. IEEE 802.16n-10/0048, section 6.2.4 specifies the requirement on Uplink Heavy Data Service. The following symbol structure is proposed for HR-Network OFDMA PHY in achieving this function requirement.

# 2. Proposed Symbol Structure in OFDMA PHY

An OFDMA system requires the information of wireless channel for recovering of data based on estimated channel parameters. The subcarriers in each OFDMA symbol are allocated for data and pilot signals. The pilot signals received are used to estimate channel delay profiles by comparing with original pilot messages sent at the transmitter of the system. The obtained channel profile is used for channel equalization and to combat multipath frequency selective fading. For a large communication range, the maximum channel delay spread is 10ms. A typical OFDMA system, such as IEEE 802.16e OFDMA system, is unable to combat long delay profile when it is operating at 1.25 and 5 MHz bandwidths due to its short cyclic prefix length. The data rate offered by OFDMA system is also not enough for supporting high data rate applications such video streaming.

For the downlink and uplink OFDMA symbol structures defined in wireless standards IEEE 802.16e, the allocation of symbols for uplink transmission follows a tile structure which is defined as (4 subcarriers) * (3 OFDM symbols). The pilot pattern of downlink system follows cluster structure. 4 pilot symbols are included for each cluster which is form by (14 subcarriers) * (2 OFDM symbols). The ratio of data and pilots is 2:1 and 6:1 for uplink and downlink respectively. The overhead is high and the system is unable to support high data rate applications such as high definition TV which requires not less than 7Mbps uplink transmission rate.

In this document, an optimized OFDMA symbol structure is proposed to reduce the overhead and combat the long propagation delay profile in particularly for the channel band 170 to 205 MHz Public Broadband Network Systems and other OFDMA based wireless communications system. The symbol structure is defined by positioning the data and pilot subcarriers in each OFDMA symbol by adopting the tile structure in Figures 247a and 249a for downlink and uplink systems, respectively. By means of provided OFDMA symbol structure, the system data rate can be increased by nearly 30% for the same level of SNR and the packet overhead is reduced to 1/7.

# 3. Text Proposal for IEEE 802.16n AWD

Xxx

Note:

The text in BLACK color: the existing text in AWD

The text in RED color: the removal of existing AWD text

The text in BLUE color: the new text added to the AWD

[-------------------------------------------------Start of Text Proposal---------------------------------------------------]

8. Physical layer (PHY)

8.4 WirelessMAN-OFDMA PHY

8.4.1 Introduction

Insert the following contents to section 8.4.1 on Page 694 at the end of 2nd paragraph

For WirelessMAN-OFDMA PHY specified for public broadband with operating frequency from 170 to 205MHz, channel bandwidth is limited to 5MHz. The corresponding OFDMA PHY mode is named PBB mode. The FFT size of 1024 and 512 shall be supported in PBB mode of OFDMA PHY.

[-------------------------------------------------End of Text Proposal----------------------------------------------------]