| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Enhancements for WirelessMAN-OFDMA Study Report Draft |
| Date Submitted | 2011-01-08 |
| Source(s) | Zheng Yan-Xiu ITRI | E-mail: zhengyanxiu@itri.org.tw |
| Re: | none |
| Abstract | Proposed material for the WirelessMAN-OFDMA study report |
| Purpose | For adoption into the WirelessMAN-OFDMA Study Report |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the �Source(s)� field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Enhancements for WirelessMAN-OFDMA Study Report Draft

I.  Introduction

This contribution proposes content for inclusion into the introduction to 802.16 for inclusion into the Enhancements for WirelessMAN-OFDMA Study Report.

II. Proposed Edits to Enhancements for WirelessMAN-OFDMA Study Report

Table of Contents

1	Introduction	2

1.1	User experience between WiMAX and LTE	3

1.2	Counter Strategies for WiMAX	3

1.3	Migration to IEEE 802.16m	4

1.4	Network deployment support for WirelessMAN-OFDMA	4

1.5	Power saving	4

1.6	VoIP efficiency	4

2	802.16 Standards Impact	5

2.1	MAC Layer Changes needed	5

2.2	Physical Layer Changes needed	5

3	Recommendations	5

1	Introduction

The SUCCESS of IEEE 802.16m relies on the SUCCESS of WirelessMAN-OFDMA. The SUCCESS of WirelessMAN-OFDMA relies on more competitive WirelessMAN-OFDMA product than LTE product. This study report reveals some facts of current WirelessMAN-OFDMA. WirelessMAN-OFDMA is competitive but the bandwidth of WiMAX product is narrower than that of the LTE product. The users may view WirelessMAN-OFDMA outdating technology and embrace LTE. However, WirelessMAN-OFDMA provides better spectrum efficiency to operators from market point of view. WirelessMAN-OFDMA should succeed but enhancement is necessary with backward compatible migration.

This study report also indicates the forward compatibility for the enhancement supporting migration from WirelessMAN-OFDMA to IEEE 802.16m. Several important enhancements to WiMAX operators could be considered for WirelessMAN-OFDMA and higher bandwidth utilization for operator with capital expenditure could be achieved.

1.1	User experience between WiMAX and LTE

LTE provides impressive user experience comparing to the WiMAX. Refer to field results in TeliaSonera’s network, it renders download speeds of up to 59.1 Mbps and upload speeds hitting as high as 18.2 Mbps. The average speed of the network was also very impressive: 33.4 Mbps down, and 12.7 Mbps up. In Taiwan, Chunghwa Telecom’s LTE experimental trial also rendered download speed of up to 45Mbps and upload speed of up to 20Mbps. The average downlink speed of the network was around 20 to 25Mbps.

The truth is that impressive results do not provide edge to LTE operators. TeliaSonera uses 40 MHz of spectrum in the 2.6 GHz band and peak spectrum efficiency is 1.48 bits/sec/Hz in downlink and 0.445 bits/sec/Hz in uplink. Chunghwa Telecom applies 20MHz of spectrum to provide 2.25bits/sec/Hz in downlink and 1bit/sec/Hz in uplink. UQ uses 10MHz of spectrum and peak spectrum efficiency is 4bits/sec/Hz in downlink and 1bit/sec/Hz in uplink. The truth is that WirelessMAN-OFDMA has outperformed current LTE product.

End users only care their product instead of technology itself. We should remember one thing that �end users have no knowledge to differentiate them both and they only want to have the same user experience�. So, datacomm works as long as their QoS is good. LTE claims edge through high speed and the WiMAX can not claim such advantage due to 10MHz spectrum and loses to LTE

1.2	Counter Strategies for WiMAX

From user experience point of view, wider bandwidth support is killing feature to all WiMAX operators to prevail their LTE competitors. There are couple strategies for WiMAX operators to take their advantage in return.

20MHz support is a straightforward methodology for current WiMAX operators. However, 10MHz and 20MHz WiMAX system can not co-exist in the same carrier. Therefore, operator would never sacrifice their existing users to please small amount of high end users. In fact, current data rate can support most existing applications.

IEEE 802.16m provides better performance than WirelessMAN-OFDMA but same issue occurs. Although IEEE 802.16m can co-exist with WirelessMAN-OFDMA, the product and vendors are not ready. If we consider co-carrier deployment, the resource of IEEE 802.16m can not be used for user camping on WirelessMAN-OFDMA system. It implies lower data rate for users served in WirelessMAN-OFDMA system. It decreases user experience. However, early stage will not have many IEEE 802.16m users. It further decreases user experience. If WiMAX operator applies green zone for IEEE 802.16m, it wastes more resource for scarce IEEE 802.16m users. 3G upgradaton from GSM has shown that WiMAX operator has to pay huge amount of money to teach their end users to upgrade their WiMAX. Another consideration is that longer time is necessary for product stability.

Multicarrier is a simple approach for operator to find a balance between cost and spectrum efficiency. WiMAX operator does not need new air interface but upgrade their base station processing capability. Low end and high end users can share the same spectrum. Chip, base station and network are mature. WiMAX Operator does not have to run the risk of unstable network. Multicarrier is safe for WiMAX operator to provide double or triple throughput to end users and compete with their LTE operators.

1.3	Migration to IEEE 802.16m

WirelessMAN-OFDMA and IEEE 802.16m has a big gap and a migration support is also necessary for WirelessMAN-OFDMA. During the IEEE 802.16m development, we have developed several supports for IEEE 802.16m user to share the same resource in WirelessMAN-OFDMA region but we don’t have support for WirelessMAN-OFDMA user to share resource in IEEE 802.16m region. Since IEEE 802.16m is the next step of WirelessMAN-OFDMA, we could transplant some features and designs from IEEE 802.16m to WirelessMAN-OFDMA and ease some burden of migration. Forward compatibility could be considered for the enhancement.

1.4	Network deployment support for WirelessMAN-OFDMA

WirelessMAN-OFDMA allows frequency reuse 1 deployments but most of the commercial networks are deployed in frequency reuse 3. WiMAX network can apply FFR based technique to realize frequency reuse 1. However, the inter-cell interference in frequency reuse 1 scenario results in MAP and traffic performance degradation especially in cell edge areas. Therefore, Current WiMAX deployment generally applies frequency reuse 3 to improve the cell edge performance in dense population area, cell-edge users would suffer significant throughput degradation and decrease user experience.

Since WirelessMAN-OFDMA and LTE are both OFDMA system, same issues occur for both systems. However, current LTE deployment applies frequency resue 1. When number of users becomes larger and the network still can sustain, this absolutely harms WirelessMAN-OFDMA market. WirelessMAN-OFDMA may need solution for inter-cell interference control in case of LTE supporting frequency resue 1 scenario without performance degradation. In fact, LTE absolutely should support frequency reuse 1 and otherwise HSPA+ outperform LTE from operator’s point of view.

1.5	Power saving

In current WirelessMAN-OFDMA network, power consumption is a serious issue for user experience. We believe users would be very angry when their mobile phone out of energy. For telecom, user would have serious concern of their charging due to billing strategy counting by time. For datacomm, user would use their mobile every moment under flat rate. In other words, WiMAX device may have to sustain for 5 or 10 hours. Further optimization should be considered as well.

1.6	VoIP efficiency

VoIP efficiency support is an important requirement IEEE 802.16. For current wireless communication, voice is still the most profitable business. More users utilize VoIP, more profit to operators. We may rely on IEEE 802.16m’s experience and copy for WirelessMAN-OFDMA.

2	802.16 Standards Impact

2.1		MAC Layer Changes needed

2.2		Physical Layer Changes needed

3	Recommendations