| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Explanation and corrections on Figure 157a and 157b |
| Date Submitted | 2008 – 01- 14 |
| Source(s) | Shashikant Maheshwari, Adrian Boariu, Yousuf Saifullah, Haihong Zheng Nokia Siemens Networks | Voice : +1 972 839 1878 E-Mail : Shashi.maheshwari@nsn.com |
| Re: | In response to the call for comments on the IEEE 802.16j D2 |
| Abstract | In this document we propose some explanation and corrections on figures 157a and 157b |
| Purpose | Discussion and Adoption in the IEEE 802.16j Draft |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Explanation and Corrections on Figure 157a and 157b

# Introduction

Figure 157a describes the example of initial transmission of DL HARQ for centralized scheduling and 157b describes the example of retransmission of DL HARQ for centralized scheduling. However, there is no corresponding text specified in IEEE 802.16j/D2 to explain those figures.

Following proposed specification text provide the explanation for figures 157a and 157b and also see the corrections for the figures 157a and 157b.

# Proposed Specification Text

[Insert following text at line 35 Page 132]

In this example, we consider that all HARQ bursts are transmitted to 3 hop away MSs (i.e. MSs attached to RS2 and RS3). Similar procedure is applicable for MSs who are attached at different hop-depth.

In Figure 157a, MR-BS schedules 5 HARQ bursts for 3 hop away MSs. One of the burst (burst # 2) is assumed to be failed on 1st relay link. It is shown on the arrow as x(2). Similarly other HARQ bursts are failed on other links (access /relay links) and corresponding failed HARQ burst is shown on the relevant arrow.  RS1 failed to receive HARQ burst #2 therefore it will replace the CID in the corresponding HARQ MAP IE with its own Basic CID and at the time of UL ACK reporting, it suppose to send code C1 for that burst. Same procedure is applied at RS2 and RS3. While forwarding the ACK/NAK to super-ordinate RS/MR-BS, RS will perform Cx operation and send encoded ACK/NAK.

[Change figure 157a as shown in following figure]

[Insert following text at line 31 Page 133]

Figure 157b describes the HARQ retransmission along with new transmission. Retransmission is only performed on the failed link and onwards while the ACK/NAK reporting for the retransmission burst is sent back to MR-BS.

MR-BS schedule transmission of new burst (6, 7 and 8) and also retransmit burst #2 which was failed on 1st hop (see frame N in figure 157b).

RS1 has to forward all four burst along with 2 retransmitted burst (#1 and #4) witch were failed at 2nd hop (see frame N+1 in figure 157b), therefore RS1 transmit 6 burst in total.

Assume out of 6, 3 bursts are meant for RS2 and other 3 bursts are meant for RS3. RS2 transmit total 4 HARQ bursts, 3 burst received from RS1 and one retransmitted burst (#3) similarly RS3 transmit 4 HARQ bursts, 3 received from RS1 and one retransmitted burst (#5) (see frame N+2 in figure 157a).

In frame N+3, MS sends the ACK/NAK.

In frame N+4, RSs will transmit the ACK/NAK for the burst received from super-ordinate RS in the order it has received.  However, RSs will transmit the UL ACK/NAK for the retransmitted burst in the separate region indicated by “Retx_ACKCH_offset” in the HARQ_ACKCH_region_allocation_for_Relay_Data IE.

For RS2, one HARQ burst was retransmitted (#3) therefore ACK/NAK for it will be reported in the separate region indicated by “Retx_ACKCH_offset” in the HARQ_ACKCH_region_allocation_for_Relay_Data IE.

For RS3, one HARQ burst was retransmitted (#5) therefore ACK/NAK for it will be reported in the separate region indicated by “Retx_ACKCH_offset” in the HARQ_ACKCH_region_allocation_for_Relay_Data IE.

RS1 will receive ACK/NAK for the burst it has transmitted along with the ACK/NAK for the retransmitted burst from RS2 and RS3.  RS1 shall peform the Cx operation and relay the ACK/NAK of retransmitted burst to super-ordinate station. It shall also append its own ACK/NAK of retransmitted burst.

[Change figure 157b as shown in following figure]