| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Codebook Evaluation for IEEE802.16m SU-/MU-MIMO |
| Date Submitted | 2008-09-12 |
| Source(s) | Jaewan Kim, Wookbong Lee, Bin-Chul Ihm LG Electronic Inc. LG R&D Complex, 533 Hogye-1dong, Dongan-gu, Anyang, 431-749, Korea | Voice: +82-31-450-1883 E-mail: lgjohnkim@lge.com wbong@lge.com bcihm@lge.com |
| Re: | In response to TGm Call for comments 802.16m-08/040 for session 58 |
| Abstract | This contribution provides performance comparison of several codebook candidates |
| Purpose | Discussion |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Codebook Evaluation for IEEE802.16m SU-/MU-MIMO

Jaewan Kim, Wookbong Lee and Bin-Chul Ihm

LG Electronics

Introduction

In the previous Kobe meeting, it has been agreed that IEEE 802.16e based codebook and/or DFT based codebook will be used for the CL-MIMO in the IEEE802.16m system. In this contribution, we have compared the performances of IEEE802.16e codebook and DFT based codebooks for further discussion.

# SLS Evaluation Results of Proposed codebooks

Several kinds of codebook scheme have been proposed for the application of IEEE802.16m CL-MIMO. In this contribution, three codebooks, IEEE 802.16e codebook [1], phase-adapted DFT codebook [2], DFT based codebook [3], have been evaluated.

Table 1. shows 4Tx closed loop single user MIMO (CL-SU-MIMO) performance. As you can see, IEEE 802.16e codebook seems to be more proper in uncorrelated channel with about 5% gain over other two DFT based codebooks for SU-MIMO. But it has the almost same performance as DFT-based codebooks with antenna spacing of 4. Moreover, it is worse than other codebooks in case of 0.5. Phase-adapted DFT codebook shows the best performance in case of 0.5with 4.2% relative gain.

Table 1 Performance comparison of 4Tx SU-MIMO

| Antenna spacing | Spectral Efficiency (SE) / Cell-edge User’s Throughput (CT) | 16e based codebook | DFT based codebook |
| --- | --- | --- | --- |
|  |  | IEEE 802.16e codebook (6bit) | Phase-adapted DFT codebook (4bit) | DFT based codebook in [3] (4bit) |
| Zero Correlation | SE | 0% | -5.6% | -4.8% |
|  | CT | 0% | -8.3% | -6% |
| 4 | SE | 0% | -0.8% | -2% |
|  | CT | 0% | 1.1% | -1% |
| 0.5 | SE | 0% | 4.2% | 2.3% |
|  | CT | 0% | 8.7% | 5.5% |

Table 2. shows 4Tx closed loop multi user MIMO (CL-MU-MIMO) performance with ZFBF algorithm. As you can see phase-adapted DFT codebook has the best performance among three codebooks. It has obtained about 3.9% (4case) and 12% (0.5 case) relative gain over IEEE 802.16e codebook, respectively. We can find out from the results that phase-adapted DFT codebook is the most suitable for MU-MIMO.

Table 2 Performance comparison of 4Tx MU-MIMO

| Antenna spacing | Spectral Efficiency (SE) / Cell-edge User’s Throughput (CT) | 16e based codebook | DFT based codebook |
| --- | --- | --- | --- |
|  |  | IEEE 802.16e codebook (6bit) | Phase-adapted DFT codebook (4bit) | DFT based codebook in [3] (4bit) |
| 4 | SE | 0% | 3.9% | 2.6% |
|  | CT | 0% | 5.2% | 3.4% |
| 0.5 | SE | 0% | 12% | 6.4% |
|  | CT | 0% | 14.4% | 8.4% |

# Conclusion

IEEE 802.16e codebook and DFT based codebooks have shown almost the same performance in SU-MIMO except for the case of uncorrelated channel. Phase-shifted DFT codebook has shown the best performance regardless of channel scenario in MU-MIMO.

In general, MU-MIMO performs better than SU-MIMO. So, when we compare codebooks, we should focus on MU-MIMO performance comparison.

However, we should be very careful when we decide IEEE 802.16m codebook. First we need to decide how many codebooks (single or multiple) and how many codebook entities (4bit, 6bit or else) will be used.

# Reference

P80216Rev2/D7, Section 8.4.5.4.10.15 MIMO feedback for Tx beamforming

C802.16m-08/983, LGE, “Codebook issues in 16m CL-SU-MIMO.”

C802.16m- 08/1187, Samsung, “Evaluation of CL SU and MU-MIMO codebooks.”

# Simulation Assuptions

Table 3 Basic simulation assumption

| Parameter | Assumption |
| --- | --- |
| OFDM parameters | 10 MHz (1024 subcarriers) |
| Channelization | LLRU |
| Number of total RUs | 48 |
| Number of PRUs in a subband One PMI and CQI per a subband | 4 |
| Channel Models | Extended Ped-B |
| Mobile Speed (km/h) | 3 km/h |
| Number of MCS level | 24 QPSK 1/8, QPSK 1/6, QPSK 1/4, QPSK 1/3, QPSK 3/7, QPSK 1/2, QPSK 5/9, QPSK 5/8, QPSK 7/10, QPSK 3/4, 16QAM4/9, 16QAM1/2, 16QAM13/24, 16QAM5/8, 16QAM2/3, 16QAM3/4, 16QAM5/6, 64QAM3/5, 64QAM5/8, 64QAM17/25, 64QAM3/4, 64QAM5/6, 64QAM9/10, 64QAM14/15 |
| Channel Code | CTC |
| Antenna configuration | 4 transmitter, 2 receiver => [4Tx, 2Rx] |
| MIMO receiver | Linear Minimum Mean Squared Error (LMMSE) |
| Channel Estimation | Perfect channel estimation |

Table 4 System parameter assumption

| Parameter | Assumption |
| --- | --- |
| Cellular Layout | Hexagonal grid, 19 cell sites, wrap-around, 3 sectors per site |
| Distance-dependent path loss | L=130.19 + 37.6log10(R), R in kilometers |
| Inter site distance | 1.5km |
| Penetration loss | 10dB |
| Shadowing standard deviation | 8 dB |
| Shadowing correlation | Between cells | 0.5 |
|  | Between sectors | 1.0 |
| Antenna pattern (horizontal) (For 3-sector cell sites with fixed antenna patterns) | = 70 degrees, Am = 20 dB |
| Total BS TX power | 46dBm |
| Minimum distance between MS and cell | 35 meters |
| Target block error rate | 10 % |
| HARQ | Chase combining with maximum retransmission 4, Asynchronous HARQ |
| OFDM symbols per subframe | 6 |
| Scheduling Criterion | Proportional Fair |
| Users per sector | 10 |
| Link Mapping | RBIR |
| Other Cell interference | 8 dominant interferers |
| CQI feedback delay | 3 subframes |
| CQI, PMI feedback method | Whole 12 subband |
| CQI, PMI feedback period | Every frame |
| Rank feedback period | Every Superframe |
| Channel Scenario | Mandatory Scenario (Zero correlated channel and Spatially correlated channel : 4 and 0.5antenna spacing) |