| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Ranging Code Design for IEEE 802.16m |
| Date Submitted | 2008-5-12 |
| Source(s) | Kuhn-Chang Lin, Tina D.-H. Huang, and Yu T. Su NCTU/ MediaTek Inc. Yih-Shen Chen, Pei-Kai Liao, I-Kang Fu and Paul Cheng MediaTek Inc. | Voice: E-mail: tony.cm95g@nctu.edu.tw ytsu@mail.nctu.edu.tw Paul.Cheng@mediatek.com |
| Re: | IEEE 802.16m-08/016, “Call for Contributions on Project 802.16m System Description Document (SDD)”. In response to the following topics: • Uplink Control Structure |
| Abstract | The contribution proposes a single OFDM symbol based ranging code design and the associated channel assignment scheme for OFDMA systems. Our design allows an efficient initial ranging method which is capable of detecting single and multiple ranging codes, estimating the corresponding timing offsets and power levels without the aid of side information such as SNR or SINR. |
| Purpose | For 802.16m discussion and adoption |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Ranging Code Design for IEEE 802.16m

Kuhn-Chang Lin, Tina D.-H. Huang, and Yu T. Su

NCTU/MediaTek Inc.

Yih-Shen Chen, Pei-Kai Liao, I-Kang Fu and Paul Cheng

MediaTek Inc.

- Introduction

The initial uplink synchronization procedure refers to the process in which ranging subscriber stations (RSSs) adjust their transmission time instants and transmission powers according to the ranging response sent by the target base station (BS) so that the corresponding ranging waveforms are received by the BS synchronously, i.e., they are aligned with the mini-slot boundary of the BS clock, and with almost identical power. A ranging process includes initial ranging and periodic ranging. The ranging signal specified in IEEE 8-2.16e suffers from unsatisfactory initial timing estimation performance when there are multiple initial ranging requests, even if the strengths of individual incoming ranging signals and the noise power level are known. Estimation of the strengths of multiple incoming ranging signals, however, is very difficult, if not impossible, during an initial ranging period.

This contribution proposes a new family of ranging codes and the corresponding channel assignment scheme (CAS) which enables a BS to detect multiple RSS signals and estimate the corresponding timing offsets and powers. Our design uses only one OFDM symbol and gives robust, excellent multi-user detection and timing estimation performance. Compared with the performance of existing works, our ranging code design and its detection method yield much improved performance and greater immunity against the interference from multi-users and frequency selective fading. Side information such as noise power level and signal-to-interference ratio is not needed.

Any RSS who wants to communicate with the BS shall activate an initial ranging process. Periodic ranging is needed to cope with the time-variant nature of a mobile environment. This contribution focuses on the initial ranging process only but an extension to periodic ranging would be straightforward.

2. Review of Related Works

In an IEEE 802.16e-based OFDMA system, a RSS senses a BS, accomplishes downlink synchronization and acquires uplink transmission parameters. Then, it chooses one of the available frequency-domain ranging codes randomly and transmits its ranging symbol twice over two consecutive OFDM symbol intervals with BPSK modulation on the ranging channel in a randomly chosen ranging time-slot. When a BS receives the ranging symbols from several RSSs, it must be able to detect and identify these ranging codes. After separating colliding codes, the BS will extract the timing information and the associated power for each RSS. The BS then broadcast a ranging response to notify all active RSSs that they should adjust to the corresponding time-slots. The ranging response contains not only the adjustment information (e.g. timing and power adjustments) but also the status information (e.g. success, retransmission). Before receiving the success notification, each RSS should adapt its power and timing to satisfy the corresponding adjustment instruction at each iteration. The ranging process shall continue until being notified otherwise.

There are a few investigations [2]-[5] on the initial ranging for the IEEE 802.16e standard [1] or general OFDMA systems. These works fall into two major categories. The first category [2], [3] is based on the ranging codes of [1]. In [2], a frequency domain correlator bank is used to detect the multi-user ranging codes by comparing the correlators' outputs with a fixed threshold. Since the output statistic is a function of the multi-user interference, which in turn depends on the number of RSSs, the cross-correlations of the ranging codes used, and the corresponding power and noise levels, a fixed detection threshold would not be able to provide robust performance. Fu and Minn [3] suggested using an adaptive threshold for a time-domain correlator bank and, as expected, obtained a better performance.

The second category [4], [5] proposes ranging code structures other than that defined by [1]. Zhuang et al. [4] partitions all active RSSs into different groups. Each group is given its specific and non-overlapping subchannels, consisting of consecutive adjacent subcarriers, such that the multiple-period ranging signals from different groups will not interfere with each other within an observation window of a single OFDM symbol. Furthermore, the number of subcarriers within a subchannel is equal to the code duration. As consecutive subcarriers are assigned to an user, diversity is lacking. Frequency-selective fading and propagation delay variation of RSSs increase the ranging complexity and degrade the performance. Fu, Li and Minn [5] suggests an interleaved channel assignment scheme (CAS) to overcome the major drawbacks of the above approache. However, their method requires that multiple-symbol ranging code be used.

The rest of this contribution is organized as follows. The ensuing section describes system models and our channel assignment scheme. Our ranging signal design is presented in Section 4, and proposed ranging method is introduced in Section 5. Simulation results and discussions are reported in Section 6. Finally, conclusions are given in Section 7.

Notation:  denotes the floor operation.  represents  modulo .  and  denote transpose and Hermitian operations

- Channel assignment and system description

The same number of subcarriers as that specified in [1] are used for the proposed ranging code structure so that a fair comparison can be made. The proposed frequency domain interleaved-subband channel assignment scheme (IS-CAS) is shown in Fig. 1. Subcarriers are divided into  groups with each group having  subbands and each subband consisting of  consecutive subcarriers such that each group can support a maximum of  RSSs. The bandwidth of a subband is less than the coherent bandwidth to ensure the channel gain of each subcarrier within a subband is approximately the same. On the other hand, the subbands of a group are interleaved so that the frequency spacing between subbands, , is larger than the coherent bandwidth to guarantee that channel responses of subbands are uncorrelated and diversity gain is achieved at the receiving end.

Let  be the set of indices of the subcarriers allocated to the th group and denote by  the th RSS in the th group which employs the frequency domain ranging code

. The frequency domain ranging signal  for  is defined as

where  and  is the relative amplitude of .

Consider an operation scenario in which different RSSs are randomly distributed over the coverage of a BS such that their ranging signals arrive at the BS asynchronously. The maximum transmission delay  (samples) equals to the round-trip propagation delay between the BS and a RSS at the boundary of the cell. To avoid inter subcarrier interference (ICI) and inter symbol interference (ISI), the length of the cyclic prefix (CP), , must be larger than the sum of  and the maximum delay spread among all uplink ranging channels  (samples). With the CP inserted, the time domain ranging signal for  is given by

Assuming the uplink channels remain static within a symbol duration and ignoring the presence of noise for the moment, we express the received ranging waveform  for  as

where  are the associated channel tap weights. The received signal at the BS thus become

where  are independent and identical distributed (i.i.d.) complex circular symmetric Gaussian random variables with zero mean and variance .

As shown in Fig. 2, within an observation window of width  samples, the received signal has contributions from each RSS ranging waveform of at least a complete -sample OFDMA symbol period and that, after discrete Fourier transform, the resulting frequency domain signal is ISI-free.

Fig. 1. Interleaved-subband channel assignment scheme for the case,  and =6.

Fig. 2. Time-domain relationships of various arriving RSS signals within a BS observation window.

- Proposed Ranging Signal Structure

The maximum supported RSSs in one group, M, is set to be . In practice,  is usually larger than 2, hence a proper choice of  is needed to ensure M > 2. Let  be the lowest subcarrier index allocated for the ranging codes and for  define

Every BS broadcasts its seed in downlink subframe. Let  be the extended (or shortened) seed of the targeted BS, which has been acquired in the previous downlink subframe and  be a constant modulus number. Then the ranging code for  is defined by

where  and the code symbol in the th subcarrier of the th subband is

The multiplication of  by  is equivalent to phase-rotating the prototype sequence (vector)  by the pseudo-random sequence (vector) . The modification term  therefore serve the purpose of PAPR reduction just like the sequences used in selective mapping. In our design, however, the prototype sequence is known once the BS seed (or ID) is given. Hence the corresponding optimal (phase) rotation vector can be predetermined. It can be broadcasted along side the BS seed or be stored in mobile stations. In contrast to the CDMA codes used in 16e, the above ranging codes have simpler structure and are easier to generate.

Such an arrangement also ensures that the overall frequency-domain phase shifts of all RSSs in the same group are non-overlapping over the interval , where , if . Hence, the RSSs in the same group can be detected and decoupled easily without using multiple OFDM symbols, giving a better rate and throughput performance. For convenience of reference, the proposed ranging signal (6)-(7) with its channel assignment scheme will be referred to as the frequency-domain interleaved polyphase (FDIP) code.

- Ranging method

Let the timing estimation error for  be denoted by . It was found [8] that whenever ,  results in only a cyclic phase shift of the received OFDMA symbol. But if  is outside , then the orthogonality among subcarriers is lost and ICI will arise. Our estimate thus assume that the timing offset  for  is equal to the sum of the transmission delay and the channel group delay. When a RSS receives the timing offset estimate from the BS, it adjusts its timing accordingly and retransmit its ranging code with both cyclic prefix and postfix to avoid loss of orthogonality.

The structure of the FDIP code and the assumption that the subband bandwidth is smaller than the uplink channel's coherent bandwidth imply that the channel gains within a subband are related by

where .

Denoted by   the received frequency domain signal within the th group after removing the BS seed  (see eq.(7)) and define the  matrix  by

and the  matrix

where

and the diagonal matrix

Then we have

where  is a matrix of i.i.d. complex white Gaussian variables with zero mean and variance  and  is given by

with =.

5.1. Multi-user Ranging Signal Detection and Timing Offset Estimation

The covariance matrix of  defined by

is a Hermitian matrix whose eigenvalues values are non-negative. Let  be the  eigenvalues of  in descending order. When there are  RSSs in the th group, , we have  basis vectors which span the null space  and can be obtained by performing singular value decomposition (SVD) of . An estimate  of the timing offset associated with  corresponds to one of the largest  local maximum of

where .

The vector  which represents the delay estimates of the delays of the active RSSs in the th group is obtained by using the received samples in one OFDMA symbol and following the steps given below.

1. Arrange the received frequency domain samples in matrix form . Set  equal .

2. Apply SVD to  to find the  matrix .

3. Find the largest  peaks of (15) to estimate  for  RSSs. Check the  peaks' values with the threshold, . If there exist  peaks below the threshold,  and go back to the step 2.

5.2. Power Estimation

Rewriting (12) as

where  and  is obtained by replacing the delays in (10) by their estimated version . The LS estimate  can be obtained by

where . The power of the th RSS in the th group can be represented as

where  denote the row vector in  corresponding to the th RSS in the th group. Note that neither channel knowledge nor noise spectrum density are required in the proposed algorithm.

- Simulation Results

6.1. System parameters and assumptions

The OFDMA system parameter values used in the simulations and reported in this section are the same as those defined in [1] and [9]. The uplink bandwidth is 10 MHz, and the subcarrier spacing is 10.9375 KHz. The number of subcarriers used for initial ranging is 144. For the proposed ranging structure =6, =6, =4 and =140. The modified ITU Vehicular A channel model with 24 paths is used and the sampling interval, , is 89.285 ns. The number of sample-spaced channel taps, , is set to be 30. We consider a cell size of radius 5 km so that the round-trip delay =33.34  = 373 samples.  samples is assumed to satisfy the condition . Each group can support  RSSs, where =2. Thus the maximum number of RSSs in one time slot is equal to 8. The speed of each RSS is 120 km/hr and carrier frequency is 2.5 GHz, hence the normalized residual frequency offsets of RSSs are assumed to be i.i.d. within the range [-0.05,0.05]. Some or all of the following RSS distributions are considered in each figure. They are (i) 1 RSS, (ii) 2 RSSs in 1 group, (iii) 2 RSSs in 2 groups, (iv) 4 RSSs in 4 groups, (v) 4 RSSs in 2 groups and (vi) 8 RSSs within one ranging time-slot.

6.2. PAPR control performance

The rotation (mapping) vector  consists of a sequence of constant mudulus numbers that rotates the phases of the prototype code symbols ; see (7). Elements of a binary rotation vector are BPSK signals, i.e., , and those of a quatermary rotation vector are drawn from the QPSK constellation, i.e., . We calculate the mean and standard deviation of the crest factor by averaging over all possible BS seeds.  Fig. 3. shows that increasing the constellation size of  reduces the PAPR or the crest factor of a ranging code. However, either the downlink overhead or the mobile terminates’ storage requirement will increase accordingly.

Fig. 3. Crest factor reduction by using binary and quaternary rotation vectors.

6.3. Multi-User detection performance

Fig. 4 shows the probability of correct detection () performance versus average SNR. It can be seen that  is close to 1 even if SNR is as small as -10 dB. The performance degrades sightly if there are two RSSs in the same group. When SNR is larger than -7 dB, the performance loss is less than 0.005. Obviously, the performance of the proposed ranging signal and algorithm is insensitive to the RSSs' interference and residual frequency offsets.

Fig. 5 plots the probability of false alarm () as a function of the average SNR. We find that at high SNR, the RSSs in the different groups do not cause an increase of false alarm probability even if the residual frequency offset is nonzero. At lower SNR, the false alarm probability for the case when there is only one RSS per group will be higher than that if there are more than one RSS in each group due to the use of the same group of subcarriers. Both signal and null spaces are influenced by strong noise. When the SNR exceeds 5 dB, the noise effect becomes insignificant. However, even if SNR is smaller than 5 dB, the false alarm probability is always less than 0.02

Fig. 4. Detection probability performance as a function of average SNR.

Fig. 5. Probability of false alarm as a function of the average SNR.

6.4. Performance of the timing estimate

Fig. 6 shows the performance of timing jitter, defined as the root mean squared error of the timing offset estimator, as a function of the average SNR for various RSS distributions. In each simulation run, the transmission delays are taken randomly from the interval . It can be observed that one RSS in one group yields better performance than two RSSs in one group. The performance loss, however, is but one sampling interval. After each RSS has adjusted its timing offset, the BS can increase the number of RSSs in one group to support more RSSs provided that the dimension of the null space is larger than one.

Fig. 6. Timing jitter behavior as a function of the average SNR.

6.5. Power estimator performance

Fig. 7 shows the normalized MSE performance of our power estimation scheme as a function of average SNR. The performance of the power estimate is rather insensitive to the number of RSSs and suffers little or no performance loss in the presence of a residual frequency offset. The MSE curves flatten out at high SNR's due to the limitation of the approximation (8).

Fig. 7. Normalized MSE performance of the proposed power estimate.

7. Conclusions

We propose a single OFDM symbol based ranging signal design called FDIP code for initial ranging process in an IEEE802.16m-based OFDMA system. The FDIP code makes it possible to devise a ranging algorithm that needs no information about the noise power spectrum density nor powers of active RSSs. Our ranging scheme is based on the idea of projecting the received multiple ranging signals onto the null space and can also be extended for use in periodic ranging process in an OFDMA system. The simulation results demonstrate that the proposed method is more robust to multipath fading and multiuser interference than those using the frequency domain CDMA ranging codes used by IEEE802.16e. Not only multiple initial ranging waveforms can be detected and separated but their individual timing offsets and power levels can be accurately estimated.

References

IEEE LAN/MAN Standard Committee, ``Air Interface for Fixed and Mobile Broadband Wireless Access Systems," IEEE 802.16e-2005.

J. Krinock, M. Singh, A. Lonkar, L. Fung and C.-C. Lee, ``Comments on OFDMA ranging scheme described in IEEE 802.16ab01/01r1," document IEEE 802.abs-01/24.

X. Fu, and H. Minn, ``Initial uplink synchronization and power control (ranging process) for OFDMA system," in  Proc. Globecomm 2004, pp. 3999 - 4003.

X. Zhuang, K. Baum, V. Nangia, and M. Cudak ``Ranging improvement for 802.16e OFDMA PHY," document IEEE 802.16e-04/143r1.

X. Fu, Y. Li, and H. Minn, ``A New Ranging Method for OFDMA Systems,"  IEEE Trans. Wireless Commun, vol. 6, no. 2, pp. 659 - 669, February 2007.

R. O. Schmidt, ``Multiple emitter location and signal parameter estimation," in  Proc. RADC spectral Estimation Workship, 1979, pp. 243 - 258.

Z. Cao, U. Tureli, and Y. D. Yao, ``Deterministic Multiuser Carrier-Frequency Offset Estimation for Interleaved OFDMA Uplink,"  Tran. commun, vol. 52, no. 9, pp. 1585 - 1594, September 2004.

M. Morelli, C.-C. Jay Kuo, and M. O. Pun, ``Synchronization techniques for orthogonal frequency division multiple access (OFDMA): A tutorial review," Proceedings of the IEEE, vol. 95, no. 7, pp. 1394 - 1427, July 2007.

IEEE 802.16 Broadband Wireless Access Working Group, ``Draft IEEE 802.16m Evaluation Methodology," IEEE 802.16m-07/037r1.