| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Change Request for Section 11.5.3.1: Unicast Pilot Pattern in 802.16m SDD |
| Date Submitted | 2009-02-27 |
| Source(s) | Philip V. Orlik, Ramesh Annavajjala, Amine Maaref, Zhifeng (Jeff) Tao, Simon Pun, Jinyun Zhang Mitsubishi Electric Research Lab Toshiyuki Kuze Mitsubishi Electric Corp | Voice: 617-621-{7558, 7518, 7570, 7595} Fax: 617-621-7550 {porlik, annavajjala, maaref, tao,mpun ,jzhang}@merl.com Voice: +81-467-41-2885 Fax: +81-467-41-2486 Kuze.Toshiyuki@ah.MitsubishiElectric.co.jp |
| Re: | Change Request to 802.16m SDD (802.16m-08/003r7) - Target topic: “11.5.3.1 Unicast Pilot Pattern ”. |
| Abstract | This contribution proposes pilot patterns for 8 transmit antennas for Section 11.5.3.1 Unicast Pilot Pattern in the current 802.16m SDD (802.16m-08/003r7). |
| Purpose | For 802.16m discussion and adoption |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Change Request for

Section 11.5.3.1: Unicast Pilot Pattern in 802.16m SDD

Phil Orlik, Ramesh Annavajjala, Amine Maaref, Zhifeng (Jeff) Tao, Simon Pun, Jinyun Zhang

Mitsubishi Electric Research Labs

Toshiyuki Kuze

Mitsubishi Electric Corp

# Introduction

The IEEE 802.16m Systems Description Document (SDD) [1] provides support for up to 8 antennas at the transmitter for downlink transmission at the advanced base-station (ABS). With this setup, the number of receiver antennas at the advanced mobile-station (AMS) can be either 2 or 4 or 8. Unfortunately, the pilot pattern for 8 transmitter antennas at the ABS is still unspecified for channel estimation purposes. In this contribution, we present pilot pattern design for ABS with 8 transmitter antennas.

# Proposed Scheme

Our resource block size is 18 consecutive subcarriers over sub-frame duration of 6 consecutive OFDM symbols. In [1], pilot patterns for up to 4 transmit antennas are presented. The following is our pilot pattern for 8 transmit antenna ABS. From Fig. 1, the pilot overhead per transmit antenna is 5.55%. Here, Pj denotes the pilot for antenna j. Ignoring the pilots (P5, P6, P7, P8), our pilot pattern reduces to that of the Type-B pilot pattern in [1] with common-mode or dedicated pilots.

Figure 1: Pilot pattern for 8 transmit antennas

# Proposed Text

Modify the existing text in [1] as follows: Existing text is shown in black, whereas the proposed text is shown in red.

:

[-------------------------------------------------Start of Text Proposal---------------------------------------------------]

11.5.3.1 Unicast Pilot Pattern

11.5.3.1.1 Pilot patterns for 8 transmi- antenna ABS

With 8 antennas at the ABS for transmission, the following pilot pattern shall be used.

In the above Figure, Pj denotes the pilot subcarrier for the jth transmit antenna.

[-------------------------------------------------End of Text Proposal----------------------------------------------------]

# Reference

[1] Shkumbin Hamiti, “The Draft IEEE 802.16m System Description Document”, IEEE 802.16m-08/003r7