| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text for the IEEE 802.16m Amendment on Multi-Radio Coexistence |
| Date Submitted | 2009-03-02 |
| Source(s) | Jing Zhu and Aran Bergman Intel Corporation | +1-503-2647073 jing.z.zhu@intel.com *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | “802.16m AWD”: Target topic: “8.x IEEE 802.16m Air-Interface Protocol Structure: Multi-Radio Coexistence”. |
| Abstract | Proposed text for multi-radio coexistence in the draft P802.16m amendment |
| Purpose | Discussion and adoption by TGm |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Text for the IEEE 802.16m Amendment on Multi-Radio Coexistence

Jing Zhu and Aran Bergman

Intel Corporation

# Introduction

The contribution proposes the text on multi-radio coexistence for 802.16m amendment. The proposed text is developed so that it can be readily combined with IEEE P802.16 Rev2/D9 [1], it is compliant to the 802.16m SRD [2] and the 802.16m SDD [3], and it follows the style and format guidelines in [4].

# References

[1] IEEE P802.16 Rev2/D9, “Draft IEEE Standard for Local and Metropolitan Area Networks: Air Interface 
for Broadband Wireless Access”

[2] IEEE 802.16m-07/002r8, “802.16m System Requirements”

[3] IEEE 802.16m-08/003r7, “The Draft IEEE 802.16m System Description Document”

[4] IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment”

4. Abbreviation and acronyms

CLC: 	Co-Located Coexistence

### 15.2.x Multi-Radio Coexistence

### 15.2.x.1 Co-Located Coexistence (CLC) Class

AMS conducts pre-negotiated periodic absences from the serving ABS, and the time pattern of such periodic absence is referred by ABS and AMS as Co-Located Coexistence (CLC) class.

Terminologies used in this section:

- CLC active interval: the consecutive subframes where the AMS’s allocations are prohibited

- CLC active ratio: the time ratio of CLC active intervals to CLC active period of a CLC class

- CLC active period: the time interval of the active pattern of a CLC class repeating

There are three types of CLC classes, and they differ from each other in terms of the unit of CLC active period and the owner of the starting time.

- For Type I CLC class, the time unit of CLC active period is microsecond, and the AMS determines the starting time of the class.

- For Type II CLC class, the time unit of CLC active period is frame, and the serving ABS determines the starting time of the class.

- For Type III CLC class, there is only one active interval, using second as the time unit, and the serving ABS determines the starting time of the class.

- For all three types, the AMS determines CLC active interval, ratio, and period.

Type I CLC class is recommended for non-802.16 radio activity that has stringent timing requirements or/and can not align with frame boundary. Otherwise, Type II CLC class is recommended for better scheduling flexibility. Type III CLC class is recommended for continuous non-802.16 radio activity that lasts long time.

Support of all three types of CLC classes is mandatory for ABS, and optional for AMS.

The serving ABS manages each type of CLC class with the following three limits:

- Ri: maximum CLC active ratio (%)

- Ti: maximum CLC active interval (frame)

- Ni: maximum number of active CLC classes of the type

Here i is set to 1, 2, and 3 to indicate Type I, II, and III CLC class, respectively.

ABS may include the CLC Limits TLV in REG-RSP to indicate the limits for Type-I and Type-II, and they shall be set according to Table XXX. If not specified in REG-RSP, all three limits shall assume the lower-bound values in Table XXX.

Table XXX: CLC limits

|  | Ni | Ri | Ti |
| --- | --- | --- | --- |
| Type-I | 1 | 5% | 1 (5ms) |
| Type-II | 1 | 30% | 8 (40ms) |
| Type-III | 1 | 1% | 3 second |

The serving ABS shall not schedule Assignment IE (MAP), data, and HARQ feedback of the AMS’s allocations in the CLC active interval of an active CLC class. Whether only DL or only UL or both are prohibited depends on the configuration of the CLC class indicated in the MOB_CLC_REQ. The default is both DL and UL allocations are prohibited.

The ABS and AMS should set the starting time of a CLC class appropriately to prevent its CLC active interval from overlapping with SFH (super-frame header) as much as possible. If the AMS detects that there has been a change in the ABS after the end of a CLC active interval, it shall locally cancel all its active CLC classes and performs network entry with the new ABS. Or if the AMS detects a changed GCCC, the AMS shall continue reception until receiving the corresponding updated information regardless of the configurations of the currently active CLC classes. In this case, the AMS does not cancel its active CLC classes.

When the allocation of data or HARQ feedback due to synchronous HARQ retransmission overlaps with a CLC active interval, if the CLC active interval is equal to or shorter than 5ms, ABS and AMS shall cancel the allocation locally, and ABS shall reschedule it after the end of the CLC active interval. The allocation for future retransmission shall be synchronously scheduled according to the rescheduled allocation. Otherwise, if the CLC active interval is longer than 5ms, the current allocation shall remain unchanged.

- Fig. XXX explains how it works. Wherein, the pre-allocated 1st retransmission falls in a CLC active interval, and the serving ABS reschedules it to next available subframe. The static time relevance to the initial transmission is no longer valid, and the serving ABS sends new MAP information to notify AMS where the rescheduled allocation is. Then, the serving ABS synchronously schedules the 2nd retransmission according to the rescheduled 1st retransmission.

Fig. XXX: Rescheduling for Synchronous HARQ to Avoid CLC Active Interval

When the allocation of initial transmission due to group scheduling overlaps with a CLC active interval, if the CLC active interval is equal to or shorter than 5ms, ABS shall reschedule it after the end of the CLC active interval. Otherwise, if the CLC active interval is longer than 5ms, the current allocation shall remain unchanged.

The parameters for CLC class (settings) are specified as follows:

-- Fi: start frame number (frame)

-- fi: start time offset (subframe), not applicable to Type III

-- ai: time duration of CLC active intervals in each period (subframe for Type I and II, second for Type III)

-- bi: time duration of CLC active period (microsecond for Type I, frame for Type II), not applicable to Type III

Here, i is set to 1, 2, and 3 to indicate Type I, II, and III CLC class respectively.

The start frame number indicates in which frame the first CLC active period starts.

The start time offset indicates the number of subframes before which the first CLC active period starts in a frame.

The following parameters are needed in addition to Ni, Ri, and Ti in determining whether a CLC class meets the CLC limits:

-- ni: number of currently active CLC classes of the type for the requesting AMS

-- t: time duration of a type-1 subframe (microsecond)

-- s: latency limit (millisecond)

-- d: latency margin (millisecond)

The latency limit indicates the minimum value of the Maximum Latency parameter of all active service flows of the requesting AMS. The latency margin provides additional time for meeting the Maximum Latency requirement of all active service flows of the requesting AMS, and shall be set to 10ms.

The serving ABS shall consider a Type-I or Type-II CLC class of the AMS as meeting the CLC limits, if all following conditions are met, and as violating the CLC limits, if any of the following conditions is not met.

- (mod(ai, 8) x t x 0.001+ floor (ai/8) x 5 ) / (bi x pi)  Ri    (p1 = 0.001, p2 = 5)

- ceil(ai/8) x 5  min(Ti x 5, s – d)

- ni < Ni

The serving ABS shall consider a Type-III CLC class as meeting the CLC limits, if all following conditions are met, and as violating the CLC limits, if any of the following conditions is not met.

- a3  3 seconds

- n3 < 1

- The AMS only has Best-Effort service flows active

The serving ABS shall accept a request from the AMS to activate a CLC class, and honor it (i.e. not unsolicited deactivate or change it after activation) if the CLC class meets the CLC limits. The serving ABS may reject the request, or deactivate an active CLC class, if the CLC class violates the CLC limits.

The AMS may request to activate one or several Type I or/and Type II CLC classes by transmitting MOB_CLC-REQ after Basic Capability Negotiation (SBC-REQ/RSP). If the AMS wants to activate Type III CLC class, it shall only transmit MOB_CLC-REQ in the connected state. After the currently active Type III CLC class ends, the AMS shall wait for at least 5 min to request another one.

The serving ABS shall response with MOB_CLC-RSP within 20ms after receiving MOB_CLC-REQ. An active CLC class shall remain active until it has been deactivated by the AMS no matter whether the AMS is in active mode, sleep mode, or scanning mode. The AMS may skip scanning operation in a scan interval if it overlaps with a CLC active interval. The AMS and the serving ABS shall locally deactivate all CLC classes after the AMS enters idle state.

The AMS shall locally suspend all active CLC classes during handover, and resume them with the new serving ABS after the handover is completed.

The AMS shall wait for at least 100ms to transmit another MOB_CLC-REQ, after it has transmitted a MOB_CLC-REQ successfully.

The AMS shall wait for at least 1 second to transmit another MOB_CLC-REQ, after it has received a MOB_CLC-RSP successfully.

If the serving ABS receives MOB_CLC-REQ after the starting time of the requested Type I or II CLC class, the serving ABS shall still consider the CLC class as valid and starting at the beginning of the next CLC active period.

If the AMS receives MOB_CLC-RSP after the starting time of a Type I or II CLC class that it activates, the AMS shall still consider the CLC class as active and starting at the beginning of the next CLC active period. If the class is Type III, the AMS shall still consider the CLC class as active, starting immediately, and ending at beginning of the frame with the frame number equal to F3 + a3 x 200.

[Editor’s comment: detailed specifications on CLC Limits TLV and MOB_CLC-REQ/RSP will be included in the future contributions]