| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed contents of the Quick Access Message in the bandwidth request procedure |
| Date Submitted | 2009-03-02 |
| Source(s) | Jaehyuk Jang Hwasun Yoo Rakesh Taori Jung Je Son Samsung Electronics | E-mail: jack.jang@samsung.com *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | IEEE 802.16m-09/0012 Call for Contributions on Project 802.16m AWD Regarding SDD section 10.10 QoS |
| Abstract | This contribution proposes detailed contents of the Quick Access Message used in the bandwidth request procedure |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed contents of the Quick Access Message in the bandwidth request procedure

Jaehyuk Jang, Hwasun Yoo, Rakesh Taori, Jung Je Son

Samsung Electronics

# Introduction

Current SDD [1] describes an optional 3-step quick access procedure in section 11.9.2.5. But, the contents of the quick access message are not defined in the SDD. This contribution proposes detailed contents of the Quick Access Message which is used in the optional 3-step bandwidth request procedure.

# Proposed contents of the Quick Access Message

Figure 1 Proposed bandwidth request procedure using the quick access message

Figure 1 describes proposed bandwidth request procedure using the quick access message. An AMS optionally sends a message for the quick access to an ABS. The message contains full station identifier of the MS (STID) (12 bits length) and predefined BR size (4 bits length).

By using STID, an BS can use unicast normal A-MAP in response of the quick access message, and additional identifier (such as BW request ID) does not have to be introduced.

Due to lack of the PHY container, it is hard for an MS to describe both BR size and QoS info in the remaining fields. In case that 4 bits are available, an MS can only describe 16 cases as maximum. Therefore, the optional 3-step procedure should be limited to specific services to describe both BR size and QoS info for the bandwidth request. Following packets could be examples of specific services.

  - time-urgent MAC management messages including standalone header

  - VoIP packets (ertPS BR)

  - Time-urgent packets (video)

  - RoHC feedback header

  - TCP ACK

And, this predefined BR size should be negotiable using specific MAC management message (TBD).

# Propose Amendment Text

Add the text below to the relevant section.

15.2.X Bandwidth allocation and request mechanisms

15.2.X.1 Optional 3-step quick access procedure

The fields of the quick access message are defined in Table X

Table X – The quick access message fields

| Name | Length (bit) | Description |
| --- | --- | --- |
| STID | 12 | Station Identifier. |
| Predefined BR Size | 4 | Predefined bandwidth request size. The index of specific services for UL bandwidth request. The index is negotiable using the XXX message. |

# Reference

    - IEEE 802.16m-08/003r7, “802.16m System Description Document (SDD)”