| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Text Modifications on the Section 15.3.8 UL Physical Structure to be consistent with the Section 15.3.5 DL Physical Structure for the IEEE 802.16m Amendment |
| Date Submitted | 2009-03-02 |
| Source(s) | HanGyu Cho, Jin Sam Kwak E-mail : hgcho@lge.com LG Electronics |
| Re: | “802.16m AWD”: IEEE 802.16m-09/0012. ”Call for Contribution on Project 802.16m Amendment Working Document (AWD) Content” Target topic: Call for Comments on Amendment Working Document |
| Abstract | The contribution proposes the text of uplink physical structure section (15.3.8) to be included in the 802.16m amendment. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Text Modifications on the Section 15.3.8 UL Physical Structure to be consistent with the Section 15.3.5 DL Physical Structure for the IEEE 802.16m Amendment

HanGyu Cho, Jin Sam Kwak

LG Electronics

# 1. Introduction

This contribution proposes the text modifications on the section 15.3.8 UL Physical Structure to be consistent with the Section 15.3.5 DL Physical Structure for the IEEE 802.16m Amendment.

# 2. Motivation and Purpose

- In the Dallas meeting in January, subband partitioning rule and CRU/DRU allocation rule have been decided and included in the updated Amendment Working Document IEEE802.16m-09/0010 only in the section 15.3.5 DL Physical Structure.

- Generally, there is no technical reason we have different subband partitioning rule and CRU/DRU allocation rule for DL and UL.

- Moreoever, current AWD which only has subband partitioning equation in DL and different CRU/DRU allocation rules in DL and UL confuses 16m members.

- This contribution suggests the text modifications on the Section 15.3.8 UL Physical Structure to be consistent with the Section 15.3.5 DL Physical Structure.

# 3. Text proposal for inclusion in the 802.16m amendment

----------------------------------------------------------- Text Start---------------------------------------------------------

Adopt only the modified text in below.

## Advanced Air Interface

### Physical Layer

#### Uplink Physical Structure

##### Multi-Cell Resource Mapping

###### Subband Partitioning

The physical PRUs are first divided into subbands and minibands; a subband comprises N1 adjacent PRUs and a miniband N2 adjacent PRUs, where N1=4 and N2=1. Subbands are suitable for frequency selective allocations as they provide a continuous allocation of PRUs in frequency. Minibands are suitable for frequency diverse allocation and are permuted in frequency.

The number of subbands is denoted by KSB. The number of PRUs allocated to subbands is LSB = N1*KSB. A 5-bit (TBD) field called Uplink Subband Allocation Count (USAC) determines the value of KSB. The USAC is transmitted in the BCH. The remaining PRUs are allocated to minibands. The number of minibands in an allocation is denoted by KMB. The number of PRUs allocated to minibands is LMB = N2*KMB. The total number of PRUs is NPRU = LSB + LMB.

The PRUs are partitioned and reordered into two groups of subband PRUs, PRUSB, and miniband PRUs, PRUMB. The set of PRUSB is numbered from 0 to (LSB-1) and the set of PRUMB from 0 to (LMB-1).

Equation (188) defines the mapping of PRUs into PRUSB s. Equation (190) defines the mapping of PRUs to PRUMBs. Figure 407 illustrates the PRU to PRUSB s and PRUMB s mapping for a 5 MHz bandwidth with USAC equal to 3.

; 							(188)

where

.   (189)

,                              (190)

where

(191)

##### Cell-Specific Resource Mapping

###### CRU/DRU Allocation

The partition between CRUs and DRUs is done on a sector specific basis. [4]-bit uplink subband-based CRU allocation size (UCASSB,i) field is sent in the BCH for each allocated frequency partition. UCASSB,i indicates the number of allocated subband-based CRUs for partition FPi in the unit of subband size. And [6]-bit uplink miniband-based CRU allocation size (UCASMB) is sent in the BCH only for partition FP0, which indicates the number of allocated miniband-based CRUs for partition FP0.

The number of CRUs in each frequency partition is denoted by LCRU,FPi., where

(xxx)

The number of DRUs in each frequency partition is denoted by LDRU,FPi, where

LDRU,FPi = UFPSi*N2 - LCRU,FPi   for 0 ≤ i < UFPCT

The mapping of PRUFPi to CRUFPi is given by

where .  is the CRU/DRU-allocation sequence (TBD), and .

The mapping of PRUFPi to DRUFPi is given by

where . is the sequence which is obtained by renumbering the remainders of the PRUs, which are not allocated for CRU, from 0 to LDRU,FPi-1.

------------------------------------------------------------Text End---------------------------------------------------------