| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | A-A-MAP Group Size Indication in Non-User Specific A-MAP IE (AWD-15.3.6) |
| Date Submitted | 2009-07-yy |
| Source(s) | Ping Wang Yi Hsuan Hujun Yin Intel Corporation | ping.wang@intel.com yi.hsuan@intel.com hujun.yin@intel.com |
| Re: | Category: AWD comments / Area: Chapter 15.3.6 (DL-CTRL) “Comments on AWD 15.3.6 DL-CTRL” |
| Abstract | The contribution proposes the A-MAP group size indication in non-user specific A-MAP IE. |
| Purpose | To be discussed by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

A-A-MAP Group Size Indication in Non-User Specific A-MAP

Ping Wang, Yi Hsuan, and Hunjun Yin

Intel Corporation

# 1. Introductions

MCS {1/2, 1/4} or {1/2, 1/8} on A-A-MAP have already been agreed according to the latest IEEE 802.16m meeting in May, 2009, wherein the A-A-MAP resource allocation may be tabulated and indicated in the Non-user specific A-MAP IE.

This contribution proposes how to generate the A-A-MAP resource allocation indication table in non-user specific A-MAP IE in 15.3.6.5.2.1 in the 802.16m AWD [1]. The following design considerations were taken into account in the proposed scheme.

- One A-A-MAP size shall be supported;

- 5, 10, 20MHz system bandwidth can be included into the same one indication table in case of the non-FFR A-A-MAP and the FFR A-A-MAP, respectively.

- The maximum number of MLRUs for A-A-MAP is 48, which is about 50% [=(48/2)/96] of one OFDM symbol at 20MHz bandwidth.

- The resource allocation tables for A-A-MAP can be divided as following:

  - MCS (1/2, 1/4) is used for the non-FFR A-A-MAP region, which are the combinations of [1, 2] MLRUs;

  - MCS (1/2, 1/8) is used for the non-FFR A-A-MAP region, which are the combinations of [1, 4] MLRUs;

  - MCS (1/2) is used for the FFR Reuse 3 A-A-MAP region, and MCS (1/2, 1/4) is used for in the FFR Reuse 1 A-A-MAP region, which are the combinations of [1, 1, 2] MLRUs;

  - MCS (1/2) is used for the FFR Reuse 3 A-A-MAP region, and MCS (1/2, 1/8) is used for in the FFR Reuse 1 A-A-MAP region, which are the combinations of [1, 1, 4] MLRUs;

- Only 8 bit signaling overhead is used for the A-A-MAP resource allocation indication in the non-user specific A-A-MAP IE; So some combinations of MLRUs for A-A-MAP have to be removed according to the following considerations:

  - Non-occupied resources on A-A-MAP may be used for the data transmission;

  - Non-occupied resources not adjacent to the data transmission in the A-A-MAP region are wasted as few as possible by limiting the MLRU values for the different MCS in the A-A-MAP region.

# 2. Unconstrained A-A-MAP Resource Allocation Indication in Non-user Specific A-MAP IE

Table 1 lists the signaling overhead of the unconstrained resource indication when assuming that the total number of MLRUs on A-A-MAP can be 12, 24, and 48 for 5, 10, 20 MHz system bandwidth.

Table 1: Signaling Overhead of Unconstrained A-A-MAP Resource Indication

| Bandwidth | 5MHz | 10MHz | 20MHz |
| --- | --- | --- | --- |
| Number of MLRU Overhead on A-A-MAP | 12 | 24 | 48 |
| Number of Combinations on MCS (1/2, 1/4) on non-FFR A-A-MAP | 49 (ceil(log2(49))=6 bits) | 169 (ceil(log2(169))=8 bits) | 625 (ceil(log2(625))= 10 bits) |
| Number of Combinations on MCS (1/2, 1/8) on non-FFR A-A-MAP | 28 (ceil(log2(28))=5 bits) | 91 (ceil(log2(91))= 7 bits) | 325 (ceil(log2(325))= 9 bits) |
| Number of Combinations on MCS (1/2) for FFR Reuse 3 A-A-MAP and (1/2, 1/8) for FFR Reuse 1 A-A-MAP | 152 (ceil(log2(152))=8 bits) | 861 (ceil(log2(861))= 10 bits) | 5681 (ceil(log2(5681))= 13 bits) |
| Number of Combinations on Coding Set (1/2) and (1/2, 1/4) for FFR | 252 (ceil(log2(252))=8 bits) | 1547 (ceil(log2(1527))= 12 bits) | 10725 (ceil(log2(10725))= 14 bits) |

It can be seen that the signaling overhead of the A-A-MAP resource allocation indication is very large, especially for the higher system bandwidth such as 20MHz. So it is necessary to reduce the above-mentioned signaling overhead for A-A-MAP in the non-user specific A-MAP IE.

# 3. Constrained A-A-MAP Resource Allocation Indication in Non-user Specific A-MAP IE

In order to reduce the signaling overhead of the A-A-MAP resource indication in non-user specific A-MAP IE, some constraints shall be made:

- Only 8-bit signaling overhead is used for the A-A-MAP resource allocation indication in the non-user specific A-MAP IE, which means that some combinations of MLRUs for A-A-MAP have to be removed;

- Non-occupied resources not adjacent to the data transmission in the A-A-MAP region are wasted as few as possible by limiting the MLRU values for the different MCS in the A-A-MAP region, which shall be further clarified in the subsequent examples.

## Resource allocation Indication Table of MLRUs for MCS (1/2, 1/4) on non-FFR A-A-MAP

MCS (1/2, 1/4) on non-FFR A-A-MAP shall consume the [1, 2] MLRUs with one A-A-MAP size. Below describes how to generate the resource allocation indication for A-A-MAP to meet the resource waste as few as possible:

Wherein Ntotal () is the total number of MLRUs for A-A-MAP; N1 () is the number of 1 MLRU for A-A-MAP; N2 () is the number of 2 MLRUs for A-A-MAP.

Non-occupied MLRUs in the 2 MLRU region by A-A-MAP shall be wasted due to be separated by the 1 MLRU region by A-A-MAP from the data transmission. In order to reduce the waste as few as possible, such the restrictions can be made:

- N1 in the 1 MLRU (MCS = 1/2) region may be [1:2:48];

- N2 in the 2 MLRU (MCS = 1/4) region may be [1:1:24];

The total number of [1, 2] MLRU combination from the above restrictions are 276, which is still larger than the requirement of 8-bit signaling overhead. Below is the further removing operation:

WhereinΔis the removing step and below are the index of the [1,2] MLRU combinations to be retained:

[2:14,16:28,30:42,44:56,58:70,72:84,86:98,100:112,114:126,128:140,142:154,156:168,170:182,184:196, 198:210,212:224,226:238,240:252,254:266,268:276],which is illustrated in Table 2.

It can be seen that the maximum number of wasted resources in the 2 MLRU (MCS=1/4) region are 0 MLRUs (MCS = 1/2) and that the maximum number of extra blind-detection in the 1 MLRU region are 1.

Table 2: 8-Bit Resource Allocation Indication of MLRUs for MCS (1/2, 1/4) on the non-FFR A-A-MAP at 5, 10, and 20MHz

| Index | Number of 1 MLRUs (MCS = 1/2) | Number of 2 MLRUs (MCS = 1/4) | Total Number of MLRUs | Number of Blind-Detection on A-A-MAP |
| --- | --- | --- | --- | --- |
| 1 | 3 | 1 | 5 | 4 |
| 2 | 5 | 1 | 7 | 6 |
| 3 | 7 | 1 | 9 | 8 |
| 4 | 9 | 1 | 11 | 10 |
| 5 | 11 | 1 | 13 | 12 |
| 6 | 13 | 1 | 15 | 14 |
| 7 | 15 | 1 | 17 | 16 |
| 8 | 17 | 1 | 19 | 18 |
| 9 | 19 | 1 | 21 | 20 |
| 10 | 21 | 1 | 23 | 22 |
| 11 | 23 | 1 | 25 | 24 |
| 12 | 25 | 1 | 27 | 26 |
| 13 | 27 | 1 | 29 | 28 |
| 14 | 31 | 1 | 33 | 32 |
| 15 | 33 | 1 | 35 | 34 |
| 16 | 35 | 1 | 37 | 36 |
| 17 | 37 | 1 | 39 | 38 |
| 18 | 39 | 1 | 41 | 40 |
| 19 | 41 | 1 | 43 | 42 |
| 20 | 43 | 1 | 45 | 44 |
| 21 | 45 | 1 | 47 | 46 |
| 22 | 1 | 2 | 5 | 3 |
| 23 | 3 | 2 | 7 | 5 |
| 24 | 5 | 2 | 9 | 7 |
| 25 | 7 | 2 | 11 | 9 |
| 26 | 9 | 2 | 13 | 11 |
| 27 | 13 | 2 | 17 | 15 |
| 28 | 15 | 2 | 19 | 17 |
| 29 | 17 | 2 | 21 | 19 |
| 30 | 19 | 2 | 23 | 21 |
| 31 | 21 | 2 | 25 | 23 |
| 32 | 23 | 2 | 27 | 25 |
| 33 | 25 | 2 | 29 | 27 |
| 34 | 27 | 2 | 31 | 29 |
| 35 | 29 | 2 | 33 | 31 |
| 36 | 31 | 2 | 35 | 33 |
| 37 | 33 | 2 | 37 | 35 |
| 38 | 35 | 2 | 39 | 37 |
| 39 | 37 | 2 | 41 | 39 |
| 40 | 41 | 2 | 45 | 43 |
| 41 | 43 | 2 | 47 | 45 |
| 42 | 1 | 3 | 7 | 4 |
| 43 | 3 | 3 | 9 | 6 |
| 44 | 5 | 3 | 11 | 8 |
| 45 | 7 | 3 | 13 | 10 |
| 46 | 9 | 3 | 15 | 12 |
| 47 | 11 | 3 | 17 | 14 |
| 48 | 13 | 3 | 19 | 16 |
| 49 | 15 | 3 | 21 | 18 |
| 50 | 17 | 3 | 23 | 20 |
| 51 | 19 | 3 | 25 | 22 |
| 52 | 21 | 3 | 27 | 24 |
| 53 | 25 | 3 | 31 | 28 |
| 54 | 27 | 3 | 33 | 30 |
| 55 | 29 | 3 | 35 | 32 |
| 56 | 31 | 3 | 37 | 34 |
| 57 | 33 | 3 | 39 | 36 |
| 58 | 35 | 3 | 41 | 38 |
| 59 | 37 | 3 | 43 | 40 |
| 60 | 39 | 3 | 45 | 42 |
| 61 | 41 | 3 | 47 | 44 |
| 62 | 1 | 4 | 9 | 5 |
| 63 | 3 | 4 | 11 | 7 |
| 64 | 5 | 4 | 13 | 9 |
| 65 | 7 | 4 | 15 | 11 |
| 66 | 11 | 4 | 19 | 15 |
| 67 | 13 | 4 | 21 | 17 |
| 68 | 15 | 4 | 23 | 19 |
| 69 | 17 | 4 | 25 | 21 |
| 70 | 19 | 4 | 27 | 23 |
| 71 | 21 | 4 | 29 | 25 |
| 72 | 23 | 4 | 31 | 27 |
| 73 | 25 | 4 | 33 | 29 |
| 74 | 27 | 4 | 35 | 31 |
| 75 | 29 | 4 | 37 | 33 |
| 76 | 31 | 4 | 39 | 35 |
| 77 | 33 | 4 | 41 | 37 |
| 78 | 35 | 4 | 43 | 39 |
| 79 | 39 | 4 | 47 | 43 |
| 80 | 1 | 5 | 11 | 6 |
| 81 | 3 | 5 | 13 | 8 |
| 82 | 5 | 5 | 15 | 10 |
| 83 | 7 | 5 | 17 | 12 |
| 84 | 9 | 5 | 19 | 14 |
| 85 | 11 | 5 | 21 | 16 |
| 86 | 13 | 5 | 23 | 18 |
| 87 | 15 | 5 | 25 | 20 |
| 88 | 17 | 5 | 27 | 22 |
| 89 | 19 | 5 | 29 | 24 |
| 90 | 21 | 5 | 31 | 26 |
| 91 | 23 | 5 | 33 | 28 |
| 92 | 27 | 5 | 37 | 32 |
| 93 | 29 | 5 | 39 | 34 |
| 94 | 31 | 5 | 41 | 36 |
| 95 | 33 | 5 | 43 | 38 |
| 96 | 35 | 5 | 45 | 40 |
| 97 | 37 | 5 | 47 | 42 |
| 98 | 1 | 6 | 13 | 7 |
| 99 | 3 | 6 | 15 | 9 |
| 100 | 5 | 6 | 17 | 11 |
| 101 | 7 | 6 | 19 | 13 |
| 102 | 9 | 6 | 21 | 15 |
| 103 | 11 | 6 | 23 | 17 |
| 104 | 13 | 6 | 25 | 19 |
| 105 | 17 | 6 | 29 | 23 |
| 106 | 19 | 6 | 31 | 25 |
| 107 | 21 | 6 | 33 | 27 |
| 108 | 23 | 6 | 35 | 29 |
| 109 | 25 | 6 | 37 | 31 |
| 110 | 27 | 6 | 39 | 33 |
| 111 | 29 | 6 | 41 | 35 |
| 112 | 31 | 6 | 43 | 37 |
| 113 | 33 | 6 | 45 | 39 |
| 114 | 35 | 6 | 47 | 41 |
| 115 | 1 | 7 | 15 | 8 |
| 116 | 3 | 7 | 17 | 10 |
| 117 | 5 | 7 | 19 | 12 |
| 118 | 9 | 7 | 23 | 16 |
| 119 | 11 | 7 | 25 | 18 |
| 120 | 13 | 7 | 27 | 20 |
| 121 | 15 | 7 | 29 | 22 |
| 122 | 17 | 7 | 31 | 24 |
| 123 | 19 | 7 | 33 | 26 |
| 124 | 21 | 7 | 35 | 28 |
| 125 | 23 | 7 | 37 | 30 |
| 126 | 25 | 7 | 39 | 32 |
| 127 | 27 | 7 | 41 | 34 |
| 128 | 29 | 7 | 43 | 36 |
| 129 | 31 | 7 | 45 | 38 |
| 130 | 33 | 7 | 47 | 40 |
| 131 | 3 | 8 | 19 | 11 |
| 132 | 5 | 8 | 21 | 13 |
| 133 | 7 | 8 | 23 | 15 |
| 134 | 9 | 8 | 25 | 17 |
| 135 | 11 | 8 | 27 | 19 |
| 136 | 13 | 8 | 29 | 21 |
| 137 | 15 | 8 | 31 | 23 |
| 138 | 17 | 8 | 33 | 25 |
| 139 | 19 | 8 | 35 | 27 |
| 140 | 21 | 8 | 37 | 29 |
| 141 | 23 | 8 | 39 | 31 |
| 142 | 25 | 8 | 41 | 33 |
| 143 | 27 | 8 | 43 | 35 |
| 144 | 31 | 8 | 47 | 39 |
| 145 | 1 | 9 | 19 | 10 |
| 146 | 3 | 9 | 21 | 12 |
| 147 | 5 | 9 | 23 | 14 |
| 148 | 7 | 9 | 25 | 16 |
| 149 | 9 | 9 | 27 | 18 |
| 150 | 11 | 9 | 29 | 20 |
| 151 | 13 | 9 | 31 | 22 |
| 152 | 15 | 9 | 33 | 24 |
| 153 | 17 | 9 | 35 | 26 |
| 154 | 19 | 9 | 37 | 28 |
| 155 | 21 | 9 | 39 | 30 |
| 156 | 23 | 9 | 41 | 32 |
| 157 | 27 | 9 | 45 | 36 |
| 158 | 29 | 9 | 47 | 38 |
| 159 | 1 | 10 | 21 | 11 |
| 160 | 3 | 10 | 23 | 13 |
| 161 | 5 | 10 | 25 | 15 |
| 162 | 7 | 10 | 27 | 17 |
| 163 | 9 | 10 | 29 | 19 |
| 164 | 11 | 10 | 31 | 21 |
| 165 | 13 | 10 | 33 | 23 |
| 166 | 15 | 10 | 35 | 25 |
| 167 | 17 | 10 | 37 | 27 |
| 168 | 19 | 10 | 39 | 29 |
| 169 | 21 | 10 | 41 | 31 |
| 170 | 25 | 10 | 45 | 35 |
| 171 | 27 | 10 | 47 | 37 |
| 172 | 1 | 11 | 23 | 12 |
| 173 | 3 | 11 | 25 | 14 |
| 174 | 5 | 11 | 27 | 16 |
| 175 | 7 | 11 | 29 | 18 |
| 176 | 9 | 11 | 31 | 20 |
| 177 | 11 | 11 | 33 | 22 |
| 178 | 13 | 11 | 35 | 24 |
| 179 | 15 | 11 | 37 | 26 |
| 180 | 17 | 11 | 39 | 28 |
| 181 | 19 | 11 | 41 | 30 |
| 182 | 21 | 11 | 43 | 32 |
| 183 | 25 | 11 | 47 | 36 |
| 184 | 1 | 12 | 25 | 13 |
| 185 | 3 | 12 | 27 | 15 |
| 186 | 5 | 12 | 29 | 17 |
| 187 | 7 | 12 | 31 | 19 |
| 188 | 9 | 12 | 33 | 21 |
| 189 | 11 | 12 | 35 | 23 |
| 190 | 13 | 12 | 37 | 25 |
| 191 | 15 | 12 | 39 | 27 |
| 192 | 17 | 12 | 41 | 29 |
| 193 | 19 | 12 | 43 | 31 |
| 194 | 21 | 12 | 45 | 33 |
| 195 | 23 | 12 | 47 | 35 |
| 196 | 3 | 13 | 29 | 16 |
| 197 | 5 | 13 | 31 | 18 |
| 198 | 7 | 13 | 33 | 20 |
| 199 | 9 | 13 | 35 | 22 |
| 200 | 11 | 13 | 37 | 24 |
| 201 | 13 | 13 | 39 | 26 |
| 202 | 15 | 13 | 41 | 28 |
| 203 | 17 | 13 | 43 | 30 |
| 204 | 19 | 13 | 45 | 32 |
| 205 | 21 | 13 | 47 | 34 |
| 206 | 1 | 14 | 29 | 15 |
| 207 | 3 | 14 | 31 | 17 |
| 208 | 5 | 14 | 33 | 19 |
| 209 | 9 | 14 | 37 | 23 |
| 210 | 11 | 14 | 39 | 25 |
| 211 | 13 | 14 | 41 | 27 |
| 212 | 15 | 14 | 43 | 29 |
| 213 | 17 | 14 | 45 | 31 |
| 214 | 19 | 14 | 47 | 33 |
| 215 | 1 | 15 | 31 | 16 |
| 216 | 3 | 15 | 33 | 18 |
| 217 | 5 | 15 | 35 | 20 |
| 218 | 7 | 15 | 37 | 22 |
| 219 | 9 | 15 | 39 | 24 |
| 220 | 11 | 15 | 41 | 26 |
| 221 | 13 | 15 | 43 | 28 |
| 222 | 17 | 15 | 47 | 32 |
| 223 | 1 | 16 | 33 | 17 |
| 224 | 3 | 16 | 35 | 19 |
| 225 | 5 | 16 | 37 | 21 |
| 226 | 7 | 16 | 39 | 23 |
| 227 | 9 | 16 | 41 | 25 |
| 228 | 11 | 16 | 43 | 27 |
| 229 | 13 | 16 | 45 | 29 |
| 230 | 15 | 16 | 47 | 31 |
| 231 | 1 | 17 | 35 | 18 |
| 232 | 3 | 17 | 37 | 20 |
| 233 | 5 | 17 | 39 | 22 |
| 234 | 7 | 17 | 41 | 24 |
| 235 | 11 | 17 | 45 | 28 |
| 236 | 13 | 17 | 47 | 30 |
| 237 | 1 | 18 | 37 | 19 |
| 238 | 3 | 18 | 39 | 21 |
| 239 | 5 | 18 | 41 | 23 |
| 240 | 7 | 18 | 43 | 25 |
| 241 | 9 | 18 | 45 | 27 |
| 242 | 11 | 18 | 47 | 29 |
| 243 | 1 | 19 | 39 | 20 |
| 244 | 3 | 19 | 41 | 22 |
| 245 | 5 | 19 | 43 | 24 |
| 246 | 7 | 19 | 45 | 26 |
| 247 | 9 | 19 | 47 | 28 |
| 248 | 3 | 20 | 43 | 23 |
| 249 | 5 | 20 | 45 | 25 |
| 250 | 7 | 20 | 47 | 27 |
| 251 | 1 | 21 | 43 | 22 |
| 252 | 3 | 21 | 45 | 24 |
| 253 | 5 | 21 | 47 | 26 |
| 254 | 1 | 22 | 45 | 23 |
| 255 | 3 | 22 | 47 | 25 |
| 256 | 1 | 23 | 47 | 24 |

## Resource Allocation Indication Table of MLRUs for MCS (1/2, 1/8) on non-FFR A-A-MAP

MCS (1/2, 1/8) on non-FFR A-A-MAP shall consume the [1, 4] MLRUs with one A-A-MAP size. Below describes how to generate the resource allocation indication for A-A-MAP to meet the resource waste as few as possible:

Wherein Ntotal () is the total number of MLRUs for A-A-MAP; N1 () is the number of 1 MLRU for A-A-MAP; N2 () is the number of 4 MLRUs for A-A-MAP.

Non-occupied MLRUs in the 4 MLRU region by A-A-MAP shall be wasted due to be separated by the 1 MLRU region by A-A-MAP from data transmission. In order to reduce the waste as few as possible, such the restrictions can be made:

- N1 in the 1 MLRU (MCS = 1/2) region may be [1:1:48];

- N2 in the 4 MLRU (MCS = 1/8) region may be [1:1:12];

The total number of [1, 4] MLRU combination from the above restrictions are 264, which is still larger than the requirement of 8-bit signaling overhead. Below is the further removing operation:

Wherein Δis the removing step and below are the index of the [1,4] MLRU combinations to be retained: [1:31, 33:64, 66:97, 99:130,132:163, 165:196,198:229, 231:262, 264]), which is illustrated in Table 3.

It can be seen that the maximum number of wasted resources in the 4 MLRU (MCS=1/8) region are 0 MLRUs and that the maximum number of extra blind-detection in the 1 MLRU (MCS=1/2) region are 1.

Table 3: 8-bits Resource Allocation Indication of MLRUs for MCS (1/2, 1/8) on the non-FFR A-A-MAP at 5, 10, 20MHz BW

| Index | Number of 1 MLRUs (MCS =1/2) | Number of 4 MLRUs (MCS = 1/8) | Total Number of MLRUs | Number of Blind-Detection on A-A-MAP |
| --- | --- | --- | --- | --- |
| 1 | 1 | 1 | 5 | 2 |
| 2 | 2 | 1 | 6 | 3 |
| 3 | 3 | 1 | 7 | 4 |
| 4 | 4 | 1 | 8 | 5 |
| 5 | 5 | 1 | 9 | 6 |
| 6 | 6 | 1 | 10 | 7 |
| 7 | 7 | 1 | 11 | 8 |
| 8 | 8 | 1 | 12 | 9 |
| 9 | 9 | 1 | 13 | 10 |
| 10 | 10 | 1 | 14 | 11 |
| 11 | 11 | 1 | 15 | 12 |
| 12 | 12 | 1 | 16 | 13 |
| 13 | 13 | 1 | 17 | 14 |
| 14 | 14 | 1 | 18 | 15 |
| 15 | 15 | 1 | 19 | 16 |
| 16 | 16 | 1 | 20 | 17 |
| 17 | 17 | 1 | 21 | 18 |
| 18 | 18 | 1 | 22 | 19 |
| 19 | 19 | 1 | 23 | 20 |
| 20 | 20 | 1 | 24 | 21 |
| 21 | 21 | 1 | 25 | 22 |
| 22 | 22 | 1 | 26 | 23 |
| 23 | 23 | 1 | 27 | 24 |
| 24 | 24 | 1 | 28 | 25 |
| 25 | 25 | 1 | 29 | 26 |
| 26 | 26 | 1 | 30 | 27 |
| 27 | 27 | 1 | 31 | 28 |
| 28 | 28 | 1 | 32 | 29 |
| 29 | 29 | 1 | 33 | 30 |
| 30 | 30 | 1 | 34 | 31 |
| 31 | 31 | 1 | 35 | 32 |
| 32 | 33 | 1 | 37 | 34 |
| 33 | 34 | 1 | 38 | 35 |
| 34 | 35 | 1 | 39 | 36 |
| 35 | 36 | 1 | 40 | 37 |
| 36 | 37 | 1 | 41 | 38 |
| 37 | 38 | 1 | 42 | 39 |
| 38 | 39 | 1 | 43 | 40 |
| 39 | 40 | 1 | 44 | 41 |
| 40 | 41 | 1 | 45 | 42 |
| 41 | 42 | 1 | 46 | 43 |
| 42 | 43 | 1 | 47 | 44 |
| 43 | 44 | 1 | 48 | 45 |
| 44 | 1 | 2 | 9 | 3 |
| 45 | 2 | 2 | 10 | 4 |
| 46 | 3 | 2 | 11 | 5 |
| 47 | 4 | 2 | 12 | 6 |
| 48 | 5 | 2 | 13 | 7 |
| 49 | 6 | 2 | 14 | 8 |
| 50 | 7 | 2 | 15 | 9 |
| 51 | 8 | 2 | 16 | 10 |
| 52 | 9 | 2 | 17 | 11 |
| 53 | 10 | 2 | 18 | 12 |
| 54 | 11 | 2 | 19 | 13 |
| 55 | 12 | 2 | 20 | 14 |
| 56 | 13 | 2 | 21 | 15 |
| 57 | 14 | 2 | 22 | 16 |
| 58 | 15 | 2 | 23 | 17 |
| 59 | 16 | 2 | 24 | 18 |
| 60 | 17 | 2 | 25 | 19 |
| 61 | 18 | 2 | 26 | 20 |
| 62 | 19 | 2 | 27 | 21 |
| 63 | 20 | 2 | 28 | 22 |
| 64 | 22 | 2 | 30 | 24 |
| 65 | 23 | 2 | 31 | 25 |
| 66 | 24 | 2 | 32 | 26 |
| 67 | 25 | 2 | 33 | 27 |
| 68 | 26 | 2 | 34 | 28 |
| 69 | 27 | 2 | 35 | 29 |
| 70 | 28 | 2 | 36 | 30 |
| 71 | 29 | 2 | 37 | 31 |
| 72 | 30 | 2 | 38 | 32 |
| 73 | 31 | 2 | 39 | 33 |
| 74 | 32 | 2 | 40 | 34 |
| 75 | 33 | 2 | 41 | 35 |
| 76 | 34 | 2 | 42 | 36 |
| 77 | 35 | 2 | 43 | 37 |
| 78 | 36 | 2 | 44 | 38 |
| 79 | 37 | 2 | 45 | 39 |
| 80 | 38 | 2 | 46 | 40 |
| 81 | 39 | 2 | 47 | 41 |
| 82 | 40 | 2 | 48 | 42 |
| 83 | 1 | 3 | 13 | 4 |
| 84 | 2 | 3 | 14 | 5 |
| 85 | 3 | 3 | 15 | 6 |
| 86 | 4 | 3 | 16 | 7 |
| 87 | 5 | 3 | 17 | 8 |
| 88 | 6 | 3 | 18 | 9 |
| 89 | 7 | 3 | 19 | 10 |
| 90 | 8 | 3 | 20 | 11 |
| 91 | 9 | 3 | 21 | 12 |
| 92 | 10 | 3 | 22 | 13 |
| 93 | 11 | 3 | 23 | 14 |
| 94 | 12 | 3 | 24 | 15 |
| 95 | 13 | 3 | 25 | 16 |
| 96 | 15 | 3 | 27 | 18 |
| 97 | 16 | 3 | 28 | 19 |
| 98 | 17 | 3 | 29 | 20 |
| 99 | 18 | 3 | 30 | 21 |
| 100 | 19 | 3 | 31 | 22 |
| 101 | 20 | 3 | 32 | 23 |
| 102 | 21 | 3 | 33 | 24 |
| 103 | 22 | 3 | 34 | 25 |
| 104 | 23 | 3 | 35 | 26 |
| 105 | 24 | 3 | 36 | 27 |
| 106 | 25 | 3 | 37 | 28 |
| 107 | 26 | 3 | 38 | 29 |
| 108 | 27 | 3 | 39 | 30 |
| 109 | 28 | 3 | 40 | 31 |
| 110 | 29 | 3 | 41 | 32 |
| 111 | 30 | 3 | 42 | 33 |
| 112 | 31 | 3 | 43 | 34 |
| 113 | 32 | 3 | 44 | 35 |
| 114 | 33 | 3 | 45 | 36 |
| 115 | 34 | 3 | 46 | 37 |
| 116 | 35 | 3 | 47 | 38 |
| 117 | 36 | 3 | 48 | 39 |
| 118 | 1 | 4 | 17 | 5 |
| 119 | 2 | 4 | 18 | 6 |
| 120 | 3 | 4 | 19 | 7 |
| 121 | 4 | 4 | 20 | 8 |
| 122 | 5 | 4 | 21 | 9 |
| 123 | 6 | 4 | 22 | 10 |
| 124 | 7 | 4 | 23 | 11 |
| 125 | 8 | 4 | 24 | 12 |
| 126 | 9 | 4 | 25 | 13 |
| 127 | 10 | 4 | 26 | 14 |
| 128 | 12 | 4 | 28 | 16 |
| 129 | 13 | 4 | 29 | 17 |
| 130 | 14 | 4 | 30 | 18 |
| 131 | 15 | 4 | 31 | 19 |
| 132 | 16 | 4 | 32 | 20 |
| 133 | 17 | 4 | 33 | 21 |
| 134 | 18 | 4 | 34 | 22 |
| 135 | 19 | 4 | 35 | 23 |
| 136 | 20 | 4 | 36 | 24 |
| 137 | 21 | 4 | 37 | 25 |
| 138 | 22 | 4 | 38 | 26 |
| 139 | 23 | 4 | 39 | 27 |
| 140 | 24 | 4 | 40 | 28 |
| 141 | 25 | 4 | 41 | 29 |
| 142 | 26 | 4 | 42 | 30 |
| 143 | 27 | 4 | 43 | 31 |
| 144 | 28 | 4 | 44 | 32 |
| 145 | 29 | 4 | 45 | 33 |
| 146 | 30 | 4 | 46 | 34 |
| 147 | 31 | 4 | 47 | 35 |
| 148 | 32 | 4 | 48 | 36 |
| 149 | 1 | 5 | 21 | 6 |
| 150 | 2 | 5 | 22 | 7 |
| 151 | 3 | 5 | 23 | 8 |
| 152 | 4 | 5 | 24 | 9 |
| 153 | 5 | 5 | 25 | 10 |
| 154 | 6 | 5 | 26 | 11 |
| 155 | 7 | 5 | 27 | 12 |
| 156 | 8 | 5 | 28 | 13 |
| 157 | 9 | 5 | 29 | 14 |
| 158 | 10 | 5 | 30 | 15 |
| 159 | 11 | 5 | 31 | 16 |
| 160 | 13 | 5 | 33 | 18 |
| 161 | 14 | 5 | 34 | 19 |
| 162 | 15 | 5 | 35 | 20 |
| 163 | 16 | 5 | 36 | 21 |
| 164 | 17 | 5 | 37 | 22 |
| 165 | 18 | 5 | 38 | 23 |
| 166 | 19 | 5 | 39 | 24 |
| 167 | 20 | 5 | 40 | 25 |
| 168 | 21 | 5 | 41 | 26 |
| 169 | 22 | 5 | 42 | 27 |
| 170 | 23 | 5 | 43 | 28 |
| 171 | 24 | 5 | 44 | 29 |
| 172 | 25 | 5 | 45 | 30 |
| 173 | 26 | 5 | 46 | 31 |
| 174 | 27 | 5 | 47 | 32 |
| 175 | 28 | 5 | 48 | 33 |
| 176 | 1 | 6 | 25 | 7 |
| 177 | 2 | 6 | 26 | 8 |
| 178 | 3 | 6 | 27 | 9 |
| 179 | 4 | 6 | 28 | 10 |
| 180 | 5 | 6 | 29 | 11 |
| 181 | 6 | 6 | 30 | 12 |
| 182 | 7 | 6 | 31 | 13 |
| 183 | 8 | 6 | 32 | 14 |
| 184 | 9 | 6 | 33 | 15 |
| 185 | 10 | 6 | 34 | 16 |
| 186 | 11 | 6 | 35 | 17 |
| 187 | 12 | 6 | 36 | 18 |
| 188 | 13 | 6 | 37 | 19 |
| 189 | 14 | 6 | 38 | 20 |
| 190 | 15 | 6 | 39 | 21 |
| 191 | 16 | 6 | 40 | 22 |
| 192 | 18 | 6 | 42 | 24 |
| 193 | 19 | 6 | 43 | 25 |
| 194 | 20 | 6 | 44 | 26 |
| 195 | 21 | 6 | 45 | 27 |
| 196 | 22 | 6 | 46 | 28 |
| 197 | 23 | 6 | 47 | 29 |
| 198 | 24 | 6 | 48 | 30 |
| 199 | 1 | 7 | 29 | 8 |
| 200 | 2 | 7 | 30 | 9 |
| 201 | 3 | 7 | 31 | 10 |
| 202 | 4 | 7 | 32 | 11 |
| 203 | 5 | 7 | 33 | 12 |
| 204 | 6 | 7 | 34 | 13 |
| 205 | 7 | 7 | 35 | 14 |
| 206 | 8 | 7 | 36 | 15 |
| 207 | 9 | 7 | 37 | 16 |
| 208 | 10 | 7 | 38 | 17 |
| 209 | 11 | 7 | 39 | 18 |
| 210 | 12 | 7 | 40 | 19 |
| 211 | 13 | 7 | 41 | 20 |
| 212 | 14 | 7 | 42 | 21 |
| 213 | 15 | 7 | 43 | 22 |
| 214 | 16 | 7 | 44 | 23 |
| 215 | 17 | 7 | 45 | 24 |
| 216 | 18 | 7 | 46 | 25 |
| 217 | 19 | 7 | 47 | 26 |
| 218 | 20 | 7 | 48 | 27 |
| 219 | 1 | 8 | 33 | 9 |
| 220 | 2 | 8 | 34 | 10 |
| 221 | 3 | 8 | 35 | 11 |
| 222 | 4 | 8 | 36 | 12 |
| 223 | 5 | 8 | 37 | 13 |
| 224 | 7 | 8 | 39 | 15 |
| 225 | 8 | 8 | 40 | 16 |
| 226 | 9 | 8 | 41 | 17 |
| 227 | 10 | 8 | 42 | 18 |
| 228 | 11 | 8 | 43 | 19 |
| 229 | 12 | 8 | 44 | 20 |
| 230 | 13 | 8 | 45 | 21 |
| 231 | 14 | 8 | 46 | 22 |
| 232 | 15 | 8 | 47 | 23 |
| 233 | 16 | 8 | 48 | 24 |
| 234 | 1 | 9 | 37 | 10 |
| 235 | 2 | 9 | 38 | 11 |
| 236 | 3 | 9 | 39 | 12 |
| 237 | 4 | 9 | 40 | 13 |
| 238 | 5 | 9 | 41 | 14 |
| 239 | 6 | 9 | 42 | 15 |
| 240 | 7 | 9 | 43 | 16 |
| 241 | 8 | 9 | 44 | 17 |
| 242 | 9 | 9 | 45 | 18 |
| 243 | 10 | 9 | 46 | 19 |
| 244 | 11 | 9 | 47 | 20 |
| 245 | 12 | 9 | 48 | 21 |
| 246 | 1 | 10 | 41 | 11 |
| 247 | 2 | 10 | 42 | 12 |
| 248 | 3 | 10 | 43 | 13 |
| 249 | 4 | 10 | 44 | 14 |
| 250 | 5 | 10 | 45 | 15 |
| 251 | 6 | 10 | 46 | 16 |
| 252 | 7 | 10 | 47 | 17 |
| 253 | 8 | 10 | 48 | 18 |
| 254 | 1 | 11 | 45 | 12 |
| 255 | 2 | 11 | 46 | 13 |
| 256 | 4 | 11 | 48 | 15 |

## Resource allocation Indication Table of MLRUs for MCS (1/2) on FFR Reuse 3 A-A-MAP and (1/2, 1/8) on FFR Reuse 1 A-A-MAP

MCS (1/2) on FFR Reuse 3 A-A-MAP and (1/2, 1/8) on FFR Reuse 1 A-A-MAP shall consume the [1, 1, 4] MLRUs with one A-A-MAP size. Below describes how to generate the resource allocation indication for A-A-MAP to meet the resource waste as few as possible:

Wherein Ntotal () is the total number of MLRUs for A-A-MAP; N1 () is the number of 1 MLRU for FFR A-A-MAP Reuse 3; N2 () is the number of 1 MLRUs for FFR A-A-MAP Reuse 1; N3 () is the number of 4 MLRUs for FFR A-A-MAP Reuse 1.

Non-occupied MLRUs in the 4 MLRU region by FFR Reuse 1 A-A-MAP shall be wasted due to be separated by the 1 MLRU region by A-A-MAP from data transmission. In order to reduce the waste as few as possible, such the restrictions can be made:

- N1 in the 1 MLRU (MCS = 1/2) region in FFR Reuse 3 A-A-MAP may be [1:4:48];

- N2 in the 1 MLRU (MCS = 1/2) region in FFR Reuse 1 A-A-MAP may be [1:4:48];

- N3 in the 4 MLRU (MCS = 1/8) region in FFR Reuse 1 A-A-MAP may be [1:1:12];

The total number of [1, 1, 4] MLRU combination from the above restrictions are 276, which is still larger than the requirement of 8-bit signaling overhead. Below is the further removing operation:

WhereinΔis the removing step and below are the index of the [1,1,4] MLRU combinations to be retained:

[2:9,11:19,21:28,30:38,40:47,49:57,59:66,68:76,78:85,87:95,97:104,106:114,116:123,125:133,135:142, 144:152,154:162,164:171,173:181,183:190,192:200,202:209,211:219,221:228,230:238,240:247,249:257, 259:266,268:276,278:286],which is illustrated in Table 3.

It can be seen that the maximum number of extra blind detections in the 1 MLRU (MCS=1/2) region in FFR Reuse 3 A-A-MAP are 3, that the maximum number of waste resources in the 4 MLRU (MCS=1/8) region in FFR Reuse 1 A-A-MAP are 0 MLRUs, and that the maximum number of extra blind-detection in the 1 MLRU (MCS=1/2) region in FFR Reuse 1 A-A-MAP are 3.

Table 4: 8-bits Resource Allocation Indication of MLRUs for MCS (1/2) in FFR Reuse 3 A-A-MAP and (1/2, 1/8) in FFR Reuse 1 A-A-MAP at 5, 10, 20MHz BW

| Index | Number of 1 MLRU (MCS = 1/2) | Number of 1 MLRU (MCS = 1/2) | Number of 4 MLRUs (MCS = 1/8) | Total Number of MLRUs | Number of Blind-Detection on A-A-MAP |
| --- | --- | --- | --- | --- | --- |
| 1 | 5 | 1 | 1 | 10 | 7 |
| 2 | 9 | 1 | 1 | 14 | 11 |
| 3 | 13 | 1 | 1 | 18 | 15 |
| 4 | 17 | 1 | 1 | 22 | 19 |
| 5 | 21 | 1 | 1 | 26 | 23 |
| 6 | 25 | 1 | 1 | 30 | 27 |
| 7 | 29 | 1 | 1 | 34 | 31 |
| 8 | 33 | 1 | 1 | 38 | 35 |
| 9 | 41 | 1 | 1 | 46 | 43 |
| 10 | 1 | 5 | 1 | 10 | 7 |
| 11 | 5 | 5 | 1 | 14 | 11 |
| 12 | 9 | 5 | 1 | 18 | 15 |
| 13 | 13 | 5 | 1 | 22 | 19 |
| 14 | 17 | 5 | 1 | 26 | 23 |
| 15 | 21 | 5 | 1 | 30 | 27 |
| 16 | 25 | 5 | 1 | 34 | 31 |
| 17 | 29 | 5 | 1 | 38 | 35 |
| 18 | 37 | 5 | 1 | 46 | 43 |
| 19 | 1 | 9 | 1 | 14 | 11 |
| 20 | 5 | 9 | 1 | 18 | 15 |
| 21 | 9 | 9 | 1 | 22 | 19 |
| 22 | 13 | 9 | 1 | 26 | 23 |
| 23 | 17 | 9 | 1 | 30 | 27 |
| 24 | 21 | 9 | 1 | 34 | 31 |
| 25 | 25 | 9 | 1 | 38 | 35 |
| 26 | 33 | 9 | 1 | 46 | 43 |
| 27 | 1 | 13 | 1 | 18 | 15 |
| 28 | 5 | 13 | 1 | 22 | 19 |
| 29 | 9 | 13 | 1 | 26 | 23 |
| 30 | 13 | 13 | 1 | 30 | 27 |
| 31 | 17 | 13 | 1 | 34 | 31 |
| 32 | 21 | 13 | 1 | 38 | 35 |
| 33 | 25 | 13 | 1 | 42 | 39 |
| 34 | 29 | 13 | 1 | 46 | 43 |
| 35 | 5 | 17 | 1 | 26 | 23 |
| 36 | 9 | 17 | 1 | 30 | 27 |
| 37 | 13 | 17 | 1 | 34 | 31 |
| 38 | 17 | 17 | 1 | 38 | 35 |
| 39 | 21 | 17 | 1 | 42 | 39 |
| 40 | 25 | 17 | 1 | 46 | 43 |
| 41 | 1 | 21 | 1 | 26 | 23 |
| 42 | 5 | 21 | 1 | 30 | 27 |
| 43 | 13 | 21 | 1 | 38 | 35 |
| 44 | 17 | 21 | 1 | 42 | 39 |
| 45 | 21 | 21 | 1 | 46 | 43 |
| 46 | 1 | 25 | 1 | 30 | 27 |
| 47 | 5 | 25 | 1 | 34 | 31 |
| 48 | 9 | 25 | 1 | 38 | 35 |
| 49 | 13 | 25 | 1 | 42 | 39 |
| 50 | 17 | 25 | 1 | 46 | 43 |
| 51 | 1 | 29 | 1 | 34 | 31 |
| 52 | 9 | 29 | 1 | 42 | 39 |
| 53 | 13 | 29 | 1 | 46 | 43 |
| 54 | 1 | 33 | 1 | 38 | 35 |
| 55 | 5 | 33 | 1 | 42 | 39 |
| 56 | 9 | 33 | 1 | 46 | 43 |
| 57 | 1 | 37 | 1 | 42 | 39 |
| 58 | 5 | 37 | 1 | 46 | 43 |
| 59 | 1 | 41 | 1 | 46 | 43 |
| 60 | 5 | 1 | 2 | 14 | 8 |
| 61 | 9 | 1 | 2 | 18 | 12 |
| 62 | 13 | 1 | 2 | 22 | 16 |
| 63 | 17 | 1 | 2 | 26 | 20 |
| 64 | 21 | 1 | 2 | 30 | 24 |
| 65 | 25 | 1 | 2 | 34 | 28 |
| 66 | 29 | 1 | 2 | 38 | 32 |
| 67 | 33 | 1 | 2 | 42 | 36 |
| 68 | 37 | 1 | 2 | 46 | 40 |
| 69 | 5 | 5 | 2 | 18 | 12 |
| 70 | 9 | 5 | 2 | 22 | 16 |
| 71 | 13 | 5 | 2 | 26 | 20 |
| 72 | 17 | 5 | 2 | 30 | 24 |
| 73 | 21 | 5 | 2 | 34 | 28 |
| 74 | 25 | 5 | 2 | 38 | 32 |
| 75 | 29 | 5 | 2 | 42 | 36 |
| 76 | 33 | 5 | 2 | 46 | 40 |
| 77 | 5 | 9 | 2 | 22 | 16 |
| 78 | 9 | 9 | 2 | 26 | 20 |
| 79 | 13 | 9 | 2 | 30 | 24 |
| 80 | 17 | 9 | 2 | 34 | 28 |
| 81 | 21 | 9 | 2 | 38 | 32 |
| 82 | 25 | 9 | 2 | 42 | 36 |
| 83 | 29 | 9 | 2 | 46 | 40 |
| 84 | 1 | 13 | 2 | 22 | 16 |
| 85 | 5 | 13 | 2 | 26 | 20 |
| 86 | 13 | 13 | 2 | 34 | 28 |
| 87 | 17 | 13 | 2 | 38 | 32 |
| 88 | 21 | 13 | 2 | 42 | 36 |
| 89 | 25 | 13 | 2 | 46 | 40 |
| 90 | 1 | 17 | 2 | 26 | 20 |
| 91 | 5 | 17 | 2 | 30 | 24 |
| 92 | 9 | 17 | 2 | 34 | 28 |
| 93 | 13 | 17 | 2 | 38 | 32 |
| 94 | 21 | 17 | 2 | 46 | 40 |
| 95 | 1 | 21 | 2 | 30 | 24 |
| 96 | 5 | 21 | 2 | 34 | 28 |
| 97 | 9 | 21 | 2 | 38 | 32 |
| 98 | 13 | 21 | 2 | 42 | 36 |
| 99 | 17 | 21 | 2 | 46 | 40 |
| 100 | 1 | 25 | 2 | 34 | 28 |
| 101 | 5 | 25 | 2 | 38 | 32 |
| 102 | 9 | 25 | 2 | 42 | 36 |
| 103 | 1 | 29 | 2 | 38 | 32 |
| 104 | 5 | 29 | 2 | 42 | 36 |
| 105 | 9 | 29 | 2 | 46 | 40 |
| 106 | 1 | 33 | 2 | 42 | 36 |
| 107 | 5 | 33 | 2 | 46 | 40 |
| 108 | 1 | 37 | 2 | 46 | 40 |
| 109 | 1 | 1 | 3 | 14 | 5 |
| 110 | 5 | 1 | 3 | 18 | 9 |
| 111 | 13 | 1 | 3 | 26 | 17 |
| 112 | 17 | 1 | 3 | 30 | 21 |
| 113 | 21 | 1 | 3 | 34 | 25 |
| 114 | 25 | 1 | 3 | 38 | 29 |
| 115 | 29 | 1 | 3 | 42 | 33 |
| 116 | 33 | 1 | 3 | 46 | 37 |
| 117 | 1 | 5 | 3 | 18 | 9 |
| 118 | 5 | 5 | 3 | 22 | 13 |
| 119 | 9 | 5 | 3 | 26 | 17 |
| 120 | 17 | 5 | 3 | 34 | 25 |
| 121 | 21 | 5 | 3 | 38 | 29 |
| 122 | 25 | 5 | 3 | 42 | 33 |
| 123 | 29 | 5 | 3 | 46 | 37 |
| 124 | 1 | 9 | 3 | 22 | 13 |
| 125 | 5 | 9 | 3 | 26 | 17 |
| 126 | 9 | 9 | 3 | 30 | 21 |
| 127 | 13 | 9 | 3 | 34 | 25 |
| 128 | 21 | 9 | 3 | 42 | 33 |
| 129 | 25 | 9 | 3 | 46 | 37 |
| 130 | 1 | 13 | 3 | 26 | 17 |
| 131 | 5 | 13 | 3 | 30 | 21 |
| 132 | 9 | 13 | 3 | 34 | 25 |
| 133 | 13 | 13 | 3 | 38 | 29 |
| 134 | 17 | 13 | 3 | 42 | 33 |
| 135 | 21 | 13 | 3 | 46 | 37 |
| 136 | 1 | 17 | 3 | 30 | 21 |
| 137 | 9 | 17 | 3 | 38 | 29 |
| 138 | 13 | 17 | 3 | 42 | 33 |
| 139 | 17 | 17 | 3 | 46 | 37 |
| 140 | 1 | 21 | 3 | 34 | 25 |
| 141 | 5 | 21 | 3 | 38 | 29 |
| 142 | 9 | 21 | 3 | 42 | 33 |
| 143 | 13 | 21 | 3 | 46 | 37 |
| 144 | 1 | 25 | 3 | 38 | 29 |
| 145 | 5 | 25 | 3 | 42 | 33 |
| 146 | 1 | 29 | 3 | 42 | 33 |
| 147 | 5 | 29 | 3 | 46 | 37 |
| 148 | 1 | 33 | 3 | 46 | 37 |
| 149 | 1 | 1 | 4 | 18 | 6 |
| 150 | 5 | 1 | 4 | 22 | 10 |
| 151 | 9 | 1 | 4 | 26 | 14 |
| 152 | 13 | 1 | 4 | 30 | 18 |
| 153 | 17 | 1 | 4 | 34 | 22 |
| 154 | 25 | 1 | 4 | 42 | 30 |
| 155 | 29 | 1 | 4 | 46 | 34 |
| 156 | 1 | 5 | 4 | 22 | 10 |
| 157 | 5 | 5 | 4 | 26 | 14 |
| 158 | 9 | 5 | 4 | 30 | 18 |
| 159 | 13 | 5 | 4 | 34 | 22 |
| 160 | 17 | 5 | 4 | 38 | 26 |
| 161 | 21 | 5 | 4 | 42 | 30 |
| 162 | 25 | 5 | 4 | 46 | 34 |
| 163 | 5 | 9 | 4 | 30 | 18 |
| 164 | 9 | 9 | 4 | 34 | 22 |
| 165 | 13 | 9 | 4 | 38 | 26 |
| 166 | 17 | 9 | 4 | 42 | 30 |
| 167 | 21 | 9 | 4 | 46 | 34 |
| 168 | 1 | 13 | 4 | 30 | 18 |
| 169 | 5 | 13 | 4 | 34 | 22 |
| 170 | 9 | 13 | 4 | 38 | 26 |
| 171 | 17 | 13 | 4 | 46 | 34 |
| 172 | 1 | 17 | 4 | 34 | 22 |
| 173 | 5 | 17 | 4 | 38 | 26 |
| 174 | 9 | 17 | 4 | 42 | 30 |
| 175 | 13 | 17 | 4 | 46 | 34 |
| 176 | 1 | 21 | 4 | 38 | 26 |
| 177 | 5 | 21 | 4 | 42 | 30 |
| 178 | 9 | 21 | 4 | 46 | 34 |
| 179 | 1 | 25 | 4 | 42 | 30 |
| 180 | 1 | 29 | 4 | 46 | 34 |
| 181 | 1 | 1 | 5 | 22 | 7 |
| 182 | 5 | 1 | 5 | 26 | 11 |
| 183 | 9 | 1 | 5 | 30 | 15 |
| 184 | 13 | 1 | 5 | 34 | 19 |
| 185 | 17 | 1 | 5 | 38 | 23 |
| 186 | 21 | 1 | 5 | 42 | 27 |
| 187 | 25 | 1 | 5 | 46 | 31 |
| 188 | 5 | 5 | 5 | 30 | 15 |
| 189 | 9 | 5 | 5 | 34 | 19 |
| 190 | 13 | 5 | 5 | 38 | 23 |
| 191 | 17 | 5 | 5 | 42 | 27 |
| 192 | 21 | 5 | 5 | 46 | 31 |
| 193 | 1 | 9 | 5 | 30 | 15 |
| 194 | 5 | 9 | 5 | 34 | 19 |
| 195 | 9 | 9 | 5 | 38 | 23 |
| 196 | 13 | 9 | 5 | 42 | 27 |
| 197 | 1 | 13 | 5 | 34 | 19 |
| 198 | 5 | 13 | 5 | 38 | 23 |
| 199 | 9 | 13 | 5 | 42 | 27 |
| 200 | 13 | 13 | 5 | 46 | 31 |
| 201 | 1 | 17 | 5 | 38 | 23 |
| 202 | 5 | 17 | 5 | 42 | 27 |
| 203 | 9 | 17 | 5 | 46 | 31 |
| 204 | 1 | 21 | 5 | 42 | 27 |
| 205 | 1 | 25 | 5 | 46 | 31 |
| 206 | 1 | 1 | 6 | 26 | 8 |
| 207 | 5 | 1 | 6 | 30 | 12 |
| 208 | 9 | 1 | 6 | 34 | 16 |
| 209 | 13 | 1 | 6 | 38 | 20 |
| 210 | 17 | 1 | 6 | 42 | 24 |
| 211 | 21 | 1 | 6 | 46 | 28 |
| 212 | 1 | 5 | 6 | 30 | 12 |
| 213 | 5 | 5 | 6 | 34 | 16 |
| 214 | 13 | 5 | 6 | 42 | 24 |
| 215 | 17 | 5 | 6 | 46 | 28 |
| 216 | 1 | 9 | 6 | 34 | 16 |
| 217 | 5 | 9 | 6 | 38 | 20 |
| 218 | 9 | 9 | 6 | 42 | 24 |
| 219 | 13 | 9 | 6 | 46 | 28 |
| 220 | 1 | 13 | 6 | 38 | 20 |
| 221 | 5 | 13 | 6 | 42 | 24 |
| 222 | 1 | 17 | 6 | 42 | 24 |
| 223 | 5 | 17 | 6 | 46 | 28 |
| 224 | 1 | 21 | 6 | 46 | 28 |
| 225 | 1 | 1 | 7 | 30 | 9 |
| 226 | 5 | 1 | 7 | 34 | 13 |
| 227 | 9 | 1 | 7 | 38 | 17 |
| 228 | 13 | 1 | 7 | 42 | 21 |
| 229 | 17 | 1 | 7 | 46 | 25 |
| 230 | 1 | 5 | 7 | 34 | 13 |
| 231 | 9 | 5 | 7 | 42 | 21 |
| 232 | 13 | 5 | 7 | 46 | 25 |
| 233 | 1 | 9 | 7 | 38 | 17 |
| 234 | 5 | 9 | 7 | 42 | 21 |
| 235 | 9 | 9 | 7 | 46 | 25 |
| 236 | 1 | 13 | 7 | 42 | 21 |
| 237 | 5 | 13 | 7 | 46 | 25 |
| 238 | 1 | 17 | 7 | 46 | 25 |
| 239 | 5 | 1 | 8 | 38 | 14 |
| 240 | 9 | 1 | 8 | 42 | 18 |
| 241 | 13 | 1 | 8 | 46 | 22 |
| 242 | 1 | 5 | 8 | 38 | 14 |
| 243 | 5 | 5 | 8 | 42 | 18 |
| 244 | 9 | 5 | 8 | 46 | 22 |
| 245 | 1 | 9 | 8 | 42 | 18 |
| 246 | 5 | 9 | 8 | 46 | 22 |
| 247 | 1 | 13 | 8 | 46 | 22 |
| 248 | 5 | 1 | 9 | 42 | 15 |
| 249 | 9 | 1 | 9 | 46 | 19 |
| 250 | 1 | 5 | 9 | 42 | 15 |
| 251 | 5 | 5 | 9 | 46 | 19 |
| 252 | 1 | 9 | 9 | 46 | 19 |
| 253 | 1 | 1 | 10 | 42 | 12 |
| 254 | 5 | 1 | 10 | 46 | 16 |
| 255 | 1 | 5 | 10 | 46 | 16 |
| 256 | 1 | 1 | 11 | 46 | 13 |

## Resource allocation Indication Table of MLRUs for MCS (1/2) on FFR Reuse 3 A-A-MAP and (1/2, 1/4) on FFR Reuse 1 A-A-MAP

MCS (1/2) on FFR Reuse 3 A-A-MAP and (1/2, 1/4) on FFR Reuse 1 A-A-MAP shall consume the [1, 1, 2] MLRUs with one A-A-MAP size. Below describes how to generate the resource allocation indication for A-A-MAP to meet the resource waste as few as possible:

Wherein Ntotal () is the total number of MLRUs for A-A-MAP; N1 () is the number of 1 MLRU for FFR A-A-MAP Reuse 3; N2 () is the number of 1 MLRUs for FFR A-A-MAP Reuse 1; N3 () is the number of 2 MLRUs for FFR A-A-MAP Reuse 1.

Non-occupied MLRUs in the 2 MLRU region by FFR Reuse 1 A-A-MAP shall be wasted due to be separated by the 1 MLRU region by A-A-MAP from data transmission. In order to reduce the waste as few as possible, such the restrictions can be made:

- N1 in the 1 MLRU (MCS = 1/2) region in FFR Reuse 3 A-A-MAP may be [1:5:48];

- N2 in the 1 MLRU (MCS = 1/2) region in FFR Reuse 1 A-A-MAP may be [1:4:48];

- N3 in the 2 MLRU (MCS = 1/4) region in FFR Reuse 1 A-A-MAP may be [1:2:24];

The total number of [1, 1, 2] MLRU combination from the above restrictions are 276, which is still larger than the requirement of 8-bit signaling overhead. Below is the further removing operation:

Then below is the index to be retained: [2:13,15:27,29:41,43:55,57:69,71:82,84:96,98:110,112:124,126:138, 140:151,153:165,167:179,181:193,195:207,209:220,222:234,236:248,250:262,264:276], which is illustrated in Table 4.

It can be seen that the maximum number of extra blind detections in the 1 MLRU (MCS=1/2) region in FFR Reuse 3 A-A-MAP are 4, that the maximum number of waste resources in the 2 MLRU (MCS=1/4) region in FFR Reuse 1 A-A-MAP are 2 MLRUs, and that the maximum number of extra blind-detection in the 1 MLRU (MCS=1/2) region in FFR Reuse 1 A-A-MAP are 3.

Table 5: 8-bits Resource Allocation Indication of MLRUs for MCS (1/2) in FFR Reuse 3 A-A-MAP and (1/2, 1/4) in FFR Reuse 1 A-A-MAP at 5, 10, 20MHz BW

| Index | Number of 1 MLRU (MCS = 1/2) | Number of 1 MLRU (MCS = 1/2) | Number of 2 MLRU (MCS = 1/4) | Total Number of MLRUs | Number of Blind-Detection on A-A-MAP |
| --- | --- | --- | --- | --- | --- |
| 1 | 6 | 1 | 1 | 9 | 8 |
| 2 | 11 | 1 | 1 | 14 | 13 |
| 3 | 16 | 1 | 1 | 19 | 18 |
| 4 | 21 | 1 | 1 | 24 | 23 |
| 5 | 26 | 1 | 1 | 29 | 28 |
| 6 | 31 | 1 | 1 | 34 | 33 |
| 7 | 36 | 1 | 1 | 39 | 38 |
| 8 | 41 | 1 | 1 | 44 | 43 |
| 9 | 1 | 5 | 1 | 8 | 7 |
| 10 | 6 | 5 | 1 | 13 | 12 |
| 11 | 11 | 5 | 1 | 18 | 17 |
| 12 | 16 | 5 | 1 | 23 | 22 |
| 13 | 26 | 5 | 1 | 33 | 32 |
| 14 | 31 | 5 | 1 | 38 | 37 |
| 15 | 36 | 5 | 1 | 43 | 42 |
| 16 | 41 | 5 | 1 | 48 | 47 |
| 17 | 1 | 9 | 1 | 12 | 11 |
| 18 | 6 | 9 | 1 | 17 | 16 |
| 19 | 11 | 9 | 1 | 22 | 21 |
| 20 | 16 | 9 | 1 | 27 | 26 |
| 21 | 21 | 9 | 1 | 32 | 31 |
| 22 | 26 | 9 | 1 | 37 | 36 |
| 23 | 31 | 9 | 1 | 42 | 41 |
| 24 | 36 | 9 | 1 | 47 | 46 |
| 25 | 1 | 13 | 1 | 16 | 15 |
| 26 | 11 | 13 | 1 | 26 | 25 |
| 27 | 16 | 13 | 1 | 31 | 30 |
| 28 | 21 | 13 | 1 | 36 | 35 |
| 29 | 26 | 13 | 1 | 41 | 40 |
| 30 | 31 | 13 | 1 | 46 | 45 |
| 31 | 1 | 17 | 1 | 20 | 19 |
| 32 | 6 | 17 | 1 | 25 | 24 |
| 33 | 11 | 17 | 1 | 30 | 29 |
| 34 | 16 | 17 | 1 | 35 | 34 |
| 35 | 21 | 17 | 1 | 40 | 39 |
| 36 | 26 | 17 | 1 | 45 | 44 |
| 37 | 1 | 21 | 1 | 24 | 23 |
| 38 | 6 | 21 | 1 | 29 | 28 |
| 39 | 16 | 21 | 1 | 39 | 38 |
| 40 | 21 | 21 | 1 | 44 | 43 |
| 41 | 1 | 25 | 1 | 28 | 27 |
| 42 | 6 | 25 | 1 | 33 | 32 |
| 43 | 11 | 25 | 1 | 38 | 37 |
| 44 | 16 | 25 | 1 | 43 | 42 |
| 45 | 21 | 25 | 1 | 48 | 47 |
| 46 | 1 | 29 | 1 | 32 | 31 |
| 47 | 6 | 29 | 1 | 37 | 36 |
| 48 | 11 | 29 | 1 | 42 | 41 |
| 49 | 16 | 29 | 1 | 47 | 46 |
| 50 | 1 | 33 | 1 | 36 | 35 |
| 51 | 6 | 33 | 1 | 41 | 40 |
| 52 | 1 | 37 | 1 | 40 | 39 |
| 53 | 6 | 37 | 1 | 45 | 44 |
| 54 | 1 | 41 | 1 | 44 | 43 |
| 55 | 1 | 45 | 1 | 48 | 47 |
| 56 | 1 | 1 | 3 | 8 | 5 |
| 57 | 6 | 1 | 3 | 13 | 10 |
| 58 | 11 | 1 | 3 | 18 | 15 |
| 59 | 16 | 1 | 3 | 23 | 20 |
| 60 | 21 | 1 | 3 | 28 | 25 |
| 61 | 26 | 1 | 3 | 33 | 30 |
| 62 | 31 | 1 | 3 | 38 | 35 |
| 63 | 36 | 1 | 3 | 43 | 40 |
| 64 | 41 | 1 | 3 | 48 | 45 |
| 65 | 6 | 5 | 3 | 17 | 14 |
| 66 | 11 | 5 | 3 | 22 | 19 |
| 67 | 16 | 5 | 3 | 27 | 24 |
| 68 | 21 | 5 | 3 | 32 | 29 |
| 69 | 26 | 5 | 3 | 37 | 34 |
| 70 | 31 | 5 | 3 | 42 | 39 |
| 71 | 36 | 5 | 3 | 47 | 44 |
| 72 | 1 | 9 | 3 | 16 | 13 |
| 73 | 6 | 9 | 3 | 21 | 18 |
| 74 | 11 | 9 | 3 | 26 | 23 |
| 75 | 16 | 9 | 3 | 31 | 28 |
| 76 | 21 | 9 | 3 | 36 | 33 |
| 77 | 31 | 9 | 3 | 46 | 43 |
| 78 | 1 | 13 | 3 | 20 | 17 |
| 79 | 6 | 13 | 3 | 25 | 22 |
| 80 | 11 | 13 | 3 | 30 | 27 |
| 81 | 16 | 13 | 3 | 35 | 32 |
| 82 | 21 | 13 | 3 | 40 | 37 |
| 83 | 26 | 13 | 3 | 45 | 42 |
| 84 | 1 | 17 | 3 | 24 | 21 |
| 85 | 6 | 17 | 3 | 29 | 26 |
| 86 | 11 | 17 | 3 | 34 | 31 |
| 87 | 16 | 17 | 3 | 39 | 36 |
| 88 | 21 | 17 | 3 | 44 | 41 |
| 89 | 1 | 21 | 3 | 28 | 25 |
| 90 | 11 | 21 | 3 | 38 | 35 |
| 91 | 16 | 21 | 3 | 43 | 40 |
| 92 | 21 | 21 | 3 | 48 | 45 |
| 93 | 1 | 25 | 3 | 32 | 29 |
| 94 | 6 | 25 | 3 | 37 | 34 |
| 95 | 11 | 25 | 3 | 42 | 39 |
| 96 | 16 | 25 | 3 | 47 | 44 |
| 97 | 1 | 29 | 3 | 36 | 33 |
| 98 | 6 | 29 | 3 | 41 | 38 |
| 99 | 11 | 29 | 3 | 46 | 43 |
| 100 | 1 | 33 | 3 | 40 | 37 |
| 101 | 6 | 33 | 3 | 45 | 42 |
| 102 | 1 | 37 | 3 | 44 | 41 |
| 103 | 1 | 1 | 5 | 12 | 7 |
| 104 | 6 | 1 | 5 | 17 | 12 |
| 105 | 11 | 1 | 5 | 22 | 17 |
| 106 | 16 | 1 | 5 | 27 | 22 |
| 107 | 21 | 1 | 5 | 32 | 27 |
| 108 | 26 | 1 | 5 | 37 | 32 |
| 109 | 31 | 1 | 5 | 42 | 37 |
| 110 | 36 | 1 | 5 | 47 | 42 |
| 111 | 1 | 5 | 5 | 16 | 11 |
| 112 | 6 | 5 | 5 | 21 | 16 |
| 113 | 11 | 5 | 5 | 26 | 21 |
| 114 | 16 | 5 | 5 | 31 | 26 |
| 115 | 21 | 5 | 5 | 36 | 31 |
| 116 | 31 | 5 | 5 | 46 | 41 |
| 117 | 1 | 9 | 5 | 20 | 15 |
| 118 | 6 | 9 | 5 | 25 | 20 |
| 119 | 11 | 9 | 5 | 30 | 25 |
| 120 | 16 | 9 | 5 | 35 | 30 |
| 121 | 21 | 9 | 5 | 40 | 35 |
| 122 | 26 | 9 | 5 | 45 | 40 |
| 123 | 1 | 13 | 5 | 24 | 19 |
| 124 | 6 | 13 | 5 | 29 | 24 |
| 125 | 11 | 13 | 5 | 34 | 29 |
| 126 | 16 | 13 | 5 | 39 | 34 |
| 127 | 21 | 13 | 5 | 44 | 39 |
| 128 | 1 | 17 | 5 | 28 | 23 |
| 129 | 11 | 17 | 5 | 38 | 33 |
| 130 | 16 | 17 | 5 | 43 | 38 |
| 131 | 21 | 17 | 5 | 48 | 43 |
| 132 | 1 | 21 | 5 | 32 | 27 |
| 133 | 6 | 21 | 5 | 37 | 32 |
| 134 | 11 | 21 | 5 | 42 | 37 |
| 135 | 16 | 21 | 5 | 47 | 42 |
| 136 | 1 | 25 | 5 | 36 | 31 |
| 137 | 6 | 25 | 5 | 41 | 36 |
| 138 | 11 | 25 | 5 | 46 | 41 |
| 139 | 1 | 29 | 5 | 40 | 35 |
| 140 | 6 | 29 | 5 | 45 | 40 |
| 141 | 1 | 37 | 5 | 48 | 43 |
| 142 | 1 | 1 | 7 | 16 | 9 |
| 143 | 6 | 1 | 7 | 21 | 14 |
| 144 | 11 | 1 | 7 | 26 | 19 |
| 145 | 16 | 1 | 7 | 31 | 24 |
| 146 | 21 | 1 | 7 | 36 | 29 |
| 147 | 26 | 1 | 7 | 41 | 34 |
| 148 | 31 | 1 | 7 | 46 | 39 |
| 149 | 1 | 5 | 7 | 20 | 13 |
| 150 | 6 | 5 | 7 | 25 | 18 |
| 151 | 11 | 5 | 7 | 30 | 23 |
| 152 | 16 | 5 | 7 | 35 | 28 |
| 153 | 21 | 5 | 7 | 40 | 33 |
| 154 | 1 | 9 | 7 | 24 | 17 |
| 155 | 6 | 9 | 7 | 29 | 22 |
| 156 | 11 | 9 | 7 | 34 | 27 |
| 157 | 16 | 9 | 7 | 39 | 32 |
| 158 | 21 | 9 | 7 | 44 | 37 |
| 159 | 1 | 13 | 7 | 28 | 21 |
| 160 | 6 | 13 | 7 | 33 | 26 |
| 161 | 11 | 13 | 7 | 38 | 31 |
| 162 | 16 | 13 | 7 | 43 | 36 |
| 163 | 21 | 13 | 7 | 48 | 41 |
| 164 | 1 | 17 | 7 | 32 | 25 |
| 165 | 6 | 17 | 7 | 37 | 30 |
| 166 | 11 | 17 | 7 | 42 | 35 |
| 167 | 1 | 21 | 7 | 36 | 29 |
| 168 | 6 | 21 | 7 | 41 | 34 |
| 169 | 11 | 21 | 7 | 46 | 39 |
| 170 | 1 | 25 | 7 | 40 | 33 |
| 171 | 6 | 25 | 7 | 45 | 38 |
| 172 | 1 | 29 | 7 | 44 | 37 |
| 173 | 1 | 33 | 7 | 48 | 41 |
| 174 | 1 | 1 | 9 | 20 | 11 |
| 175 | 6 | 1 | 9 | 25 | 16 |
| 176 | 11 | 1 | 9 | 30 | 21 |
| 177 | 16 | 1 | 9 | 35 | 26 |
| 178 | 21 | 1 | 9 | 40 | 31 |
| 179 | 26 | 1 | 9 | 45 | 36 |
| 180 | 6 | 5 | 9 | 29 | 20 |
| 181 | 11 | 5 | 9 | 34 | 25 |
| 182 | 16 | 5 | 9 | 39 | 30 |
| 183 | 21 | 5 | 9 | 44 | 35 |
| 184 | 1 | 9 | 9 | 28 | 19 |
| 185 | 6 | 9 | 9 | 33 | 24 |
| 186 | 11 | 9 | 9 | 38 | 29 |
| 187 | 16 | 9 | 9 | 43 | 34 |
| 188 | 21 | 9 | 9 | 48 | 39 |
| 189 | 1 | 13 | 9 | 32 | 23 |
| 190 | 6 | 13 | 9 | 37 | 28 |
| 191 | 11 | 13 | 9 | 42 | 33 |
| 192 | 16 | 13 | 9 | 47 | 38 |
| 193 | 6 | 17 | 9 | 41 | 32 |
| 194 | 11 | 17 | 9 | 46 | 37 |
| 195 | 1 | 21 | 9 | 40 | 31 |
| 196 | 6 | 21 | 9 | 45 | 36 |
| 197 | 1 | 25 | 9 | 44 | 35 |
| 198 | 1 | 29 | 9 | 48 | 39 |
| 199 | 1 | 1 | 11 | 24 | 13 |
| 200 | 6 | 1 | 11 | 29 | 18 |
| 201 | 11 | 1 | 11 | 34 | 23 |
| 202 | 16 | 1 | 11 | 39 | 28 |
| 203 | 21 | 1 | 11 | 44 | 33 |
| 204 | 1 | 5 | 11 | 28 | 17 |
| 205 | 11 | 5 | 11 | 38 | 27 |
| 206 | 16 | 5 | 11 | 43 | 32 |
| 207 | 21 | 5 | 11 | 48 | 37 |
| 208 | 1 | 9 | 11 | 32 | 21 |
| 209 | 6 | 9 | 11 | 37 | 26 |
| 210 | 11 | 9 | 11 | 42 | 31 |
| 211 | 16 | 9 | 11 | 47 | 36 |
| 212 | 1 | 13 | 11 | 36 | 25 |
| 213 | 6 | 13 | 11 | 41 | 30 |
| 214 | 11 | 13 | 11 | 46 | 35 |
| 215 | 1 | 17 | 11 | 40 | 29 |
| 216 | 6 | 17 | 11 | 45 | 34 |
| 217 | 1 | 21 | 11 | 44 | 33 |
| 218 | 1 | 1 | 13 | 28 | 15 |
| 219 | 6 | 1 | 13 | 33 | 20 |
| 220 | 11 | 1 | 13 | 38 | 25 |
| 221 | 16 | 1 | 13 | 43 | 30 |
| 222 | 21 | 1 | 13 | 48 | 35 |
| 223 | 1 | 5 | 13 | 32 | 19 |
| 224 | 6 | 5 | 13 | 37 | 24 |
| 225 | 11 | 5 | 13 | 42 | 29 |
| 226 | 16 | 5 | 13 | 47 | 34 |
| 227 | 1 | 9 | 13 | 36 | 23 |
| 228 | 6 | 9 | 13 | 41 | 28 |
| 229 | 11 | 9 | 13 | 46 | 33 |
| 230 | 1 | 13 | 13 | 40 | 27 |
| 231 | 1 | 17 | 13 | 44 | 31 |
| 232 | 1 | 21 | 13 | 48 | 35 |
| 233 | 1 | 1 | 15 | 32 | 17 |
| 234 | 6 | 1 | 15 | 37 | 22 |
| 235 | 11 | 1 | 15 | 42 | 27 |
| 236 | 16 | 1 | 15 | 47 | 32 |
| 237 | 1 | 5 | 15 | 36 | 21 |
| 238 | 6 | 5 | 15 | 41 | 26 |
| 239 | 11 | 5 | 15 | 46 | 31 |
| 240 | 1 | 9 | 15 | 40 | 25 |
| 241 | 6 | 9 | 15 | 45 | 30 |
| 242 | 1 | 13 | 15 | 44 | 29 |
| 243 | 1 | 17 | 15 | 48 | 33 |
| 244 | 6 | 1 | 17 | 41 | 24 |
| 245 | 11 | 1 | 17 | 46 | 29 |
| 246 | 1 | 5 | 17 | 40 | 23 |
| 247 | 6 | 5 | 17 | 45 | 28 |
| 248 | 1 | 9 | 17 | 44 | 27 |
| 249 | 1 | 13 | 17 | 48 | 31 |
| 250 | 1 | 1 | 19 | 40 | 21 |
| 251 | 6 | 1 | 19 | 45 | 26 |
| 252 | 1 | 5 | 19 | 44 | 25 |
| 253 | 1 | 9 | 19 | 48 | 29 |
| 254 | 1 | 1 | 21 | 44 | 23 |
| 255 | 1 | 5 | 21 | 48 | 27 |
| 256 | 1 | 1 | 23 | 48 | 25 |

# Conclusions

The A-A-MAP resource allocation indication in non-user specific A-MAP IE has already proposed in this paper by removing some combinations of A-A-MAP resource allocations, which can be tabulated into three tables of MCS (1/2, 1/4) in the non-FFR A-A-MAP, (1/2, 1/8) in the non-FFR A-A-MAP, (1/2) in the FFR Reuse 3 A-A-MAP and (1/2, 1/8) in the FFR Reuse 1 A-A-MAP, (1/2) in the FFR Reuse 3 A-A-MAP and (1/2, 1/4) in the FFR Reuse 1 A-A-MAP, respectively.

# References

[1] P802.16m Amendment Working document, 802.16m-09/0010r2, June 1, 2009.