| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed AAI_NBR-REQ/ADV message format |
| Date Submitted | 2009-07-14 |
| Source(s) | Jaehyuk Jang, Jung Je Son, Rakesh Taori Samsung Electronics Jenhui Chen, Yu-Jen Lee, Chin-Yang Sheng, Woei-Hwa Tarn, Chih-Chieh Wang Chang Gung University Ying-Chuan Hsiao, Ming-Hung Tao ITRI | E-mail: jack.jang@samsung.com E-mail: jhchen@mail.cgu.edu.tw *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | IEEE 802.16m-09/0028r1: Call for Comments and Contributions on the AWD Section 15.2.5 AAI MAC Management Messages Section 15.2.5.4 AAI_NBR-ADV |
| Abstract | This contribution provides detailed message format of the AAI_NBR-REQ/ADV |
| Purpose | To be discussed and adopted by TGm |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed AAI_NBR-REQ/ADV message format

Jaehyuk Jang, Jung Je Son, Rakesh Taori
Samsung Electronics

Jenhui Chen, Yu-Jen Lee, Chin-Yang Sheng, Woei-Hwa Tarn, Chih-Chieh Wang
Chang Gung University

Ying-Chuan Hsiao, Ming-Hung Tao
ITRI

# Introduction

This contribution provides detailed message format of the AAI_NBR-REQ/ADV.

To support unicast neighbor advertisement message, we need to introduce new message, i.e., the AAI_NBR-REQ message in the MS side, so that an AMS can send the AAI_NBR-REQ message to request the AAI_NBR-ADV message.

And, detailed format of the AAI_NBR-ADV message is missing in the current AWD. The proposed AAI_NBR-ADV message can include information of neighbor legacy BSs as well as ABSs'. If this information is not included in the AAI_NBR-ADV message, MS must perform zone switch BEFORE performing handover only to get neighbor information. To reduce MS's complexity, it is desirable to provide all neighbor BSs information in the MZone even though size of the AAI_NBR-ADV message could be large.

# Proposed Text #1

Add following sections in the AWD.

----------------------------------------------------- Start of Proposed Text -----------------------------------------------------

15.2 Medium access control

15.2.5 AAI MAC Management Messages

15.2.5.XX AAI_NBR-REQ

An AMS sends AAI_NBR-REQ message to request the AAI_NBR-ADV message. The AAI_NBR-REQ message may include neighbor BS IDs. The AMS may send the AAI_NBR-REQ for requesting the fragments of AAI_NBR-ADV message. The AMS may send the AAI_NBR-REQ message when the AMS has no complete neighbor BSs list information included in the AAI_NBR-ADV message.

The AAI_NBR_REQ message shall include following parameters:

- Flag: this indicates the type of the AAI_NBR-REQ

  - 0b0: this requests the AAI_NBR-ADV for specific BSs

  - 0b1: this requests the missed fragments of AAI_NBR-ADV

If Flag == 0b0 following parameters shall be included in the AAI_NBR-REQ message:

- N_Neighbor_BS

  - Number of neighboring BS for the AAI_NBR-ADV message.

- Requested BS ID: 48 bits

If Flag == 0b1 following parameters shall be included in the AAI_NBR-REQ message:

- N_Fragments

  - Number of missed fragments indicated in the AAI_NBR-ADV messages.

- Fragment_Index

  - The index of fragment of the AAI_NBR-ADV messages.

------------------------------------------------------ End of Proposed Text ------------------------------------------------------