| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Cancellation of Carrier Management command |
| Date Submitted | 2010-03-04 |
| Source(s) | Peiying Zhu Bin Chen Jia Lin Junxian Mo Yanhong Wang Ronald Mao Huawei Technologies Co.,Ltd. | zhupeiying@huawei.com |
| Re: | Call for LB #31 on “ P802.16m/D4”: Target topic: “16.2.8.2.11.5.2” |
| Abstract | This contribution proposes Cancellation of Carrier Management command |
| Purpose | To be discussed and adopted by TGm for 802.16m LB#31. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Cancellation of Carrier Management command

Peiying Zhu, Bin Chen, Jia Lin, Junxian Mo, Yanhong Wang, Ronald Mao

Huawei Technologies Co.,Ltd.

# Introduction

AAI_CM-IND does not have a IE to indicate the process result of the corresponding AAI_CM-CMD, so that if it fail to perform the command in AAI_CM-CMD, the behavior is undefined. When the carrier status changes and the AMS does not report to ABS in time, this problem may happens. Anyway, such command shall need a way to handle unexpected issues and cancel the process.

The description of AAI_CM-IND is incorrect, which conflict with the procedure in the previous subclause, say, 16.2.8.2.11.1 Secondary Carrier Activation/De-activation and 16.2.8.2.11.2 Primary Carrier Change. In that two subclause, the AAI_CM-IND can be used for the notification for two purpose, say, Secondary Carrier Activation/De-activation and Primary Carrier Change, but in this subclause, it is just used for inform the ABS of the readiness of target carrier.

# References

[1] P802.16m DRAFT Amendment to IEEE Standard for Local and metropolitan area networks, P80216m/D4, Jan 2010.

# Text proposal for inclusion in the 802.16m AWD

< Modify the text in the section 16.2.8.2.11.5.2 in the page 247 from line 3 to 25.>

-------------------------------  Start of text proposal #1 --------------------------------------------

An AAI_CM-IND message shall be transmitted by an AMS to response to the corresponding AAI_CM-CMD from the ABS. For the responding to secondary carrier management command in the AAI_CM-CMD, the action code in the AAI_CM-IND shall be set to 0, while for primary carrier change command, it shall be set to 1. If the command is handled successfully, Action Result in the AAI_CM-IND shall be set to 1, otherwise it shall be set to 0.

The format of the AAI_CM-IND MAC control message is shown in Table 750—.

Table 750—AAI_CM-IND MAC Control Message Format

| Field | Size (Bit) | Description |
| --- | --- | --- |
| Control message type | 8 | AAI_CM-IND |
| Action code | 1 | 0: Secondary carrier management 1: Primary carrier change |
| Action Result | 1 | 0: Failure 1: Successful |

-------------------------------  End of text proposal #1 --------------------------------------------