| oProject | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Text Clean up for E-MBS Connection Establishment in IEEE 802.16m (16.9.2.1) |
| Date Submitted | 2010-05-11 |
| Source(s) | Nan Li Kaiying Lv Bo Sun Yang Liu ZTE Corporation | E-mail: lv.kaiying@zte.com.cn |
| Re: | LB31a / Chapter 16.9.2.1(E-MBS Connection Establishment) |
| Abstract | Text clean up for E-MBS Connection Establishment is proposed. |
| Purpose | To be discussed and adopted. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Text Clean up for E-MBS Connection Establishment in IEEE 802.16m

Nan Li, Kaiying Lv, Bo Sun,Yang Liu

ZTE Corporation

# 1. Introduction

Text about E-MBS connection Establishment in 802.16m/D5 is unclear and may cause confusion. This proposal provides editorial changes as well as small technical changes on E-MBS connection Establishment (16.9.2.1).

# 2. Text Proposal

======================== Start of Proposed Text =====================

[Change text in P827，Line 7，16.9.2.1 E-MBS Connection Establishment as follows:]

To discover E-MBS service, AMS will inform ABS of support of E-MBS transmission by AAI_REG-REQ message and the ABS will indicate if it supports any of E-MBS modes for that AMS through AAI_REG-RSP message. The basic E-MBS capability exchange in AAI_REG-REQ/RSP message is described in 16.2.3.7 and 16.2.3.8.

When an AMS registers for receiving multicast and broadcast services, the serving ABS or the AMS may initiate the DSA procedure for multicast and broadcast connections. Following the The AMS’s discovery and registration of the E-MBS services and registers with the serving ABS for receiving multicast and broadcast services through upper layer signaling which are outside the scope of this standard.

To prepare for subsequent E-MBS operation, the AMS obtains the E-MBS related configuration information receiving AAI_SCD message and AAI_E-MBS-CFG MAC Control message on the corresponding E-MBS carrier described in Table 974. The AMS learns the E-MBS_Zone_ID(s) to which the serving and neighboring ABS belongs through AAI_E-MBS_CFG message.

If E-MBS is supported by the AMS/ABS, support of DSx messaging for E-MBS flow establishment is mandatory on AMS/ABS. In addition the E-MBS flows may also be established optionally through upper layer signaling that is outside the scope of this specification.

The ABS or AMS may/shall initiate the DSA procedure with respect to multicast and broadcast connections. When supported, the The ABS sends DSA, DSC and DSD messaging respectively to establish, change and delete E-MBS service flows. shall be activated, changed or deleted through ABS/network Initiated DSA, DSC and DSD messaging respectively. The ABS initiated DSx messaging shall be supported and AMS initiated DSx may also be supported. In addition the E-MBS service flows may also be established optionally through upper layer signaling，which is outside the scope of this specification. When E-MBS services involve multiple flows the compact form of DSx with group parameter should be used to reduce overhead and signaling delay associated with E-MBS flow management.

The ABS sends the AAI-DSA-REQ/RSP to the AMS containing the relevant E-MBS/MBS parameters. The parameters sent will indicate to the AMS whether to listen to E-MBS on an AAI zone or to listen to MBS on a legacy MBS zone. It also includes E-MBS IDs and FIDs, E-MBS zone IDs, E-MBS carrier information (physical carrier index). Selective decoding of content is at the granularity of FID's.

…

============================== End of Proposed Text ========================