| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clarification on D-LBS Zone Location Beacon Transmission for Multiple Antenna Systems (16.8.3) |
| Date Submitted | 2010-09-08 |
| Source(s) | Alexey Khoryaev, Alexander Maltsev, Mikhail Shilov, Andrey Chervyakov, Gregory Morozov Intel Corporation | E-mails: alexey.khoryaev@intel.com alexander.maltsev@intel.com |
| Re: | Comments on IEEE P802.16m/D8 for IEEE 802.16 Working Group Sponsor Ballot Topic: LBS (Section 16.8.3) |
| Abstract | This contribution provides clarification on location beacon transmission for multiple antenna systems |
| Purpose | To be discussed and adopted by TGm for the next draft of the IEEE 802.16m amendment document. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clarification on D-LBS Zone Location Beacon Transmission for Multiple Antenna Systems

Alexey Khoryaev, Alexander Maltsev, 
Mikhail Shilov, Andrey Chervyakov, Gregory Morozov

Intel Corporation

Introduction

This contribution provides clarification of the D-LBS zone location beacon transmission for multiple antenna systems. The proposed text is developed so, that it is compliant to the IEEE 802.16m SRD [1] and the IEEE 802.16m SDD [2], and it follows the style and format guidelines in [3].

In accordance with the D8 of the IEEE 802.16m [4] the “SA-Preamble shall be used as a reference location beacon signal for transmission inside of D-LBS zone. The physical structure of the SA-Preamble signal transmitted by each ABS or ARS in the D-LBS zone shall be the same as defined in section 16.3.5.1.2”. For multiple antenna systems, the SA-Preamble sub-block sequences are interleaved on the number of antennas (see Figure 516 in [4]).  In addition to interleaving the antenna rotation is applied on a frame-by frame basis.

In the latest D8 of the IEEE 802.16m [4] for the transmission of location beacon in D-LBS zone (represented by the SA-Preamble sequence) the interleaving and antenna rotation patterns are undefined. In this contribution to clarify the location beacon transmission for multiple antenna systems it is proposed that location beacon shall be transmitted from the arbitrary single antenna of the multiple antenna system.

References

IEEE 802.16m-07/002r8, “802.16m System Requirements”

IEEE 802.16m-08/0034r2, “The Draft IEEE 802.16m System Description Document”

IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment”

IEEE P802.16m/D8, “Part 16: Air Interface for Fixed and Mobile Broadband Wireless Access Systems – DRAFT Amendment to IEEE Standard for Local and metropolitan area networks”

Proposed Text

Instruction to editor:

Black text: existing D8 text

Red and strike out text: to be deleted

Blue and underline text: to be added

=========================Start of Proposed Text 1 ==============================

[Note to Editor: Change the following text in section 16.8.3 Enhanced LBS Support on page 895 (line 49) as follows]

16.8.3.2 D-LBS zone location beacon signals

The SA-Preamble shall be used as a reference location beacon signal for transmission inside of D-LBS zone. The physical structure of the SA-Preamble signal transmitted by each ABS or ARS in the D-LBS zone shall be the same as defined in section 16.3.6.1.2 for given frame.  For systems with multiple transmit antennas the whole SA-Preamble sequence shall be transmitted from the arbitrary single antenna.

========================== End of Proposed Text 1 =============================