## Slide 1: Distributed Network Protection (DNP) architecture study
Maarten Vissers
2011-11-08
v2
v2: includes a few slides at the end illustrating segment protection

## Slide 2: Contents
Introduction 3
Legend 4
  High level models of PIP+CBP, PNP, PEP+CNP, CNP, CEP 5
  High level & basic models of IBBEB nodes 8
  High level & basic models of PEB/PB nodes 10
PBB/PBB-TE network with IBBEB nodes 12
  PBB Domain with restorable BVLAN Ethernet Connections (EC) 13
    BVLAN U for unprotected SVLAN ECs
    BVLAN A & B for protected SVLAN ECs
    Load sharing between portal nodes, BVLAN end point blocking
    Distributed Restorable BVLAN connected to DRNI
  PBB-TE Domain with protected TESI connections 17
    TESI U1,U2 for unprotected SVLAN ECs
    TESI A1,A2,A3 & B1,B2,B3 for protected SVLAN ECs
    Load sharing between portal nodes, TESI end point blocking
    Distributed TESI Protection connected to DRNI
  Port filtering entities location in CBP 22
  PBB Domain with G.8031 SNC protected SVLAN EC 24
  Compound view – BVLAN, TESI, SVLAN restoration/protection connected to DRNI 26
  Impact of single switch fabric? 31

## Slide 3: Introduction
The following slides focus on the distributed network protection (DNP) functionality and associated MAC addresses in the portal nodes of a DRNI protected Ethernet ENNI. These slides complement the “DRNI Data Plane Model I/II Comparison & MAC Address Values in DRNI” slides (axbq-vissers-drni-data-plane-model-I-and-II-comparison-1011-v00.pptx) .
The simplest DRNI configuration is assumed, including two nodes in a portal
A portal supports DRNI protected SVLAN ECs and unprotected SVLAN ECs (as per MEF requirement); unprotected SVLAN ECs are considered to be outside DNRI control
Network domain is assumed to be PBB/PBB-TE and portal nodes are IBBEB nodes, supporting restorable MP2MP BVLAN ECs and protected P2P TESIs
  Deployment of alternative network domain technologies (MPLS(TP), SDH, OTN) and portal nodes (TB) is addressed in a next version. In such TB nodes the B-Component and PIPs are replaced by MPLS(TP), SDH or OTN Network Ports connected to ‘MPLS LSP Relay’, ‘SDH VC-n Relay’ or ‘OTN ODUk Relay’ functions and MPLS(TP), SDH or OTN specific ‘provider network ports’.
MAC address requirement is investigated (to some extend) to understand which functions must use the PIP/CBP port’s EUI48 values, which functions may use these values and which functions must not use these values; further analysis is to be added in a next version

## Slide 4: Legend
The configurations in this presentation require the use of a more compact modelling method than provided by the 802.1Q models
For this reason the next slides present alternative presentations for the various XXP ports specified in 802.1Q
Those alternative presentations focus on the MEP, MIP and multiplexing/demultiplexing (MUX) functionality within those XXP ports and port pairs
The alternative presentation of the PIP-CBP port pair assumes the support of the basic functionality specified in clause 5.7/802.1Q, supporting single domain PBB networks with IB BEB and BCB nodes

## Slide 5: Legend
19.2/3/5
6.9, 9.5b
8.5
19.2
6.7
802.3
19.2/3/5
6.14
6.10
6.14
6.11, 9.5c
19.2/5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
19.2/3/5
6.14
6.10
6.14
6.11, 9.5c
19.2/5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
MUX
MUX
MUX
PIP
CBP
SVLAN MEP & MIP
BVLAN/TESI MEP
SVLAN to BVLAN/TESI muxes
BVLAN/TESI MEP
SVLAN MEP/MIP
SVLAN mux
19.2/3/5
6.9, 9.5b
8.5
19.2
6.7
802.3
PNP
MUX
BVLAN /TESI MEP & MIP
Link MEP
BVLAN/TESI to Link mux
Link MEP
BVLAN/TESI MEP/MIP
BVLAN mux
PHY MEP
W & P TESI MEPs
SVLAN mux & TESI protection switch
SVLAN MEP/MIP

## Slide 6: Legend
19.2/3/5
6.14
6.14
6.9, 9.5b
19.2/5
6.9, 9.5a
8.5
19.2/3/5
6.9, 9.5b
8.5
19.2
6.7
802.3
PEP
CNP
CVLAN MEP & MIP
SVLAN MEP
CVLAN to SVLAN mux
SVLAN MEP
CVLAN MEP/MIP
CVLAN mux
19.2/3/5
6.9, 9.5b
8.5
19.2
6.7
802.3
PNP
MUX
SVLAN MEP & MIP
Link MEP
SVLAN to Link mux
Link MEP
SVLAN MEP/MIP
SVLAN mux
PHY MEP
19.2/3/5
6.14
6.14
6.9, 9.5b
19.2/5
6.9, 9.5a
8.5
MUX

## Slide 7: Legend
19.2/3/5
6.9, 9.5b
8.5
19.2
6.7
802.3
19.2/3/5
6.9, 9.5b
8.5
19.2
6.7
802.3
CNP
MUX
SVLAN MEP & MIP
Link MEP
SVLAN to Link mux
Link MEP
SVLAN MEP/MIP
SVLAN mux
PHY MEP
6.9, 9.5a
8.5
19.2
6.7
802.3
CEP
Link MEP
CVLAN to Link mux
6.9, 9.5a
8.5
19.2
6.7
802.3
MUX
Link MEP
CVLAN mux
PHY MEP

## Slide 8: High level model of IBBEB nodes
SVLAN mux BVLAN/TESI MEP
BVLAN/TESI mux
Link MEP
Intra-DAS
Intra-DAS
ENNI
INNI
SVLAN EC Relay
BVLAN EC/TESI Relay
BVLAN/TESI MEP/MIP
SVLAN MEP/MIP
SVLAN MEP/MIP
Link MEP
SVLAN mux
BVLAN/TESI MEP

## Slide 9: Basic model of IBBEB nodes without illustrating intermediate MEP/MIP functions
BVLAN EC/TESI Relay
SVLAN EC Relay
Intra-DAS
Intra-DAS
ENNI
INNI

## Slide 10: High level model of PEB/PB nodes
Intra-DAS
ENNI
UNI
INNI
SVLAN EC Relay
SVLAN MEP/MIP
CVLAN mux
SVLAN MEP
CVLAN MEP/MIP
CVLAN EC Relay
SVLAN mux
Link MEP
SVLAN MEP/MIP
UNI
SVLAN MEP/MIP
Link MEP SVLAN mux
Link MEP CVLAN mux
Link MEP SVLAN mux
PEB functionality

## Slide 11: Basic model of PEB/PB nodes without illustrating intermediate MEP/MIP functions
Intra-DAS
ENNI
INNI
UNI
CVLAN EC Relay
UNI
SVLAN EC Relay
PEB functionality

## Slide 12: PBB/PBB-TE Network with IBBEB nodes
BVLAN EC/TESI Relay
SVLAN EC Relay
BVLAN EC/TESI Relay
SVLAN EC Relay
BVLAN EC/TESI Relay
BVLAN/TESI end points
Link end points
SVLAN EC Relay
INNI
ENNI
ENNI
Link end points
BVLAN/TESI end points
BVLAN/TESI end points
Link end points
Link end points
PBB, PBB-TE domain (note)

## Slide 13: PBB Domain with BVLAN ECs
BVLAN EC Relay
SVLAN EC Relay
BVLAN EC Relay
SVLAN EC Relay
BVLAN EC Relay
Intra-DAS BVLAN
Intra-Network BVLAN
Intra-DAS Link
INNI
SVLAN EC Relay
BVLAN B
Blocked BVLAN B endpoint
BVLAN B for protected SVLAN ECs has active endpoint at either the left, or the right portal node. The other BVLAN endpoint is blocked. The two BVLAN endpoints form one virtual endpoint.
B-MAC addresses of left & right BVLAN B endpoints is the same
BVLAN A
Blocked BVLAN A endpoint
BVLAN A for protected SVLAN ECs has active endpoint at either the right, or the left portal node. The other BVLAN endpoint is blocked. The two BVLAN endpoints form one virtual endpoint.
B-MAC addresses of left & right BVLAN A endpoints is the same
BVLAN U
BVLAN U for unprotected SVLAN ECs has active endpoints at left and right portal nodes.
B-MAC addresses of left & right BVLAN U endpoints is different
animated

## Slide 14: Load sharing at portal nodes
BVLAN A and B are used to support load sharing of protected SVLAN ECs by the two portal nodes
Under fault free conditions, 50% of the SVLAN EC traffic will pass through the left portal node to the ENNI and the other 50% will pass through the right portal node
  The figure in the previous slide illustrates that BVLAN A and B are both having an end point on the domain top edge node to illustrate load sharing. To support multipoint SVLAN ECs between any sub set of edge nodes it is typically necessary that a BVLAN is connected to all IB BEB nodes in a domain. BVLAN A and B most likely will have end points on each edge node as such. Note: For load balancing at the portal nodes, it is not necessary to distribute the SVLAN ECs in each edge node over both BVLAN A and B.
Unprotected SVLAN ECs can not be supported by BVLAN A or B due to blocking of BVLAN end point at one of the two portal nodes
QUESTION: How to block a BVLAN end point; i.e. prevent that BVLAN OAM generated on the CBP will enter the BVLAN Relay function?
BVLAN ECs are set up under MSTP/MVRP control. A/B are dynamic connections. MSTP/MVRP will restore BVLAN A/B ECs if it receives a trigger condition. Triggers are e.g. ‘active gateway failed’ and request from DRNI.

## Slide 15: Distributed Restorable BVLAN connected to DRNI
P
W
W
P
Half-DAS
B
A
Intra-DAS BVLAN
ENNI
ENNI
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U
Half-DAS
X
Right portal node failure or
ENNI + Intra-DAS BVLAN failure
Normal state, no failures
X
X
P
W
W
P
B
A
ENNI
ENNI
U
SVLAN EC Relay
SVLAN EC Relay
Half-DAS
Intra-DAS BVLAN
Half-DAS

## Slide 16: Distributed Restorable BVLAN connected to DRNI
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
Right ENNI failure
Intra-DAS BVLAN
ENNI
ENNI
Half-DAS
Half-DAS
X
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
Left ENNI failure
Intra-DAS BVLAN
ENNI
ENNI
Half-DAS
Half-DAS
X
P
W
W
P
B
A
U
P
W
W
P
B
A
U

## Slide 17: PBB-TE Domain with TESI connections
TESI Relay
SVLAN EC Relay
TESI Relay
SVLAN EC Relay
TESI Relay
Intra-DAS TESI
Intra-Network TESI
Intra-DAS Link
INNI
SVLAN EC Relay
W
P
W*
P
W
P*
TESI A1,A2,A3
A1
A2
A3
TESI A1,A2,A3 for protected SVLAN ECs has active protected endpoint at either the right, or the left portal node. The other protected TESI endpoint is blocked. The two protected TESI endpoints form one virtual protected endpoint.
Blocked TESI A protected endpoints
TESI A relay
ESP-MAC address of left & right TESI A endpoints is the same
W
P
W
P*
W*
P
TESI B1,B2,B3
B3
Blocked TESI B protected endpoints
TESI B relay
TESI B1,B2,B3 for protected SVLAN ECs has active protected endpoint at either the left, or the right portal node. The other protected TESI endpoint is blocked. The two protected TESI endpoints form one virtual protected endpoint.
ESP-MAC address of left & right TESI B endpoints is the same
B1
B2
U1
U2
TESI U1,U2
TESI U1,U2 for unprotected SVLAN ECs has active endpoints at left and right portal nodes.
ESP-MAC address of left & right TESI U endpoints is different
animated

## Slide 18: TESI W & P connection configurations
TESI Relay
TESI Relay
TESI Relay
W
P
W*
P
W
P*
A1
A2
A3
TESI A relay
ESP-VID Translation?
TESI A drop
TESI Relay
TESI Relay
TESI Relay
W
P
W*
P
W
P*
A1
A2
A3
TESI A relay ESP-VID Translation?
TESI A drop
W*
P
W
P*
W*
P
W
P*
Working TESI = A1
Protection TESI = A2+A3
Working TESI = A1+A3
Protection TESI = A2
DNP Control Protocol
DNP Control Protocol
@A
ESP-DA = @A, ESP-VID = a2
ESP-DA = @A, ESP-VID = a1
ESP-DA = @A, ESP-VID = a2
ESP-DA = @A, ESP-VID = a1
ESP-DA = @A, ESP-VID = a3 
ESP-VID = a4 
ESP-DA = @A, ESP-VID = a3 
ESP-VID = a4 
@A
@A
@A

## Slide 19: Load sharing at portal nodes
TESI A and B are used to support load sharing of protected SVLAN ECs by the two portal nodes
Under fault free conditions, 50% of the SVLAN EC traffic will pass through the left portal node to the ENNI and the other 50% will pass through the right portal node
  The figure in slide 17 illustrates that TESI A and B are both having an end point on the domain top edge node to illustrate load sharing. Note: For load balancing at the portal nodes, it is not necessary to that each edge node has a TESI A and B. For load balancing at portal nodes, some edge nodes may only have a TESI A and other edge nodes may only have a TESI B.
Unprotected SVLAN ECs can not be supported by TESI A or B due to blocking of TESI end point at one of the two portal nodes
QUESTION: How to block a TESI end point; i.e. prevent that TESI OAM generated on the CBP will enter the TESI Relay function?
TESI connections are set up under network management control. A1/B1 and A2/B2 are static connections. Adding A3/B3 allows portal nodes to control relay or drop of incoming TESI frames. A3/B3 should have third/forth ESP-VID value.

## Slide 20: Distributed TESI Protection connected to DRNI
W*
P
W
P*
W
P*
W*
P
Half-DAS
B3
B1
B2
A1
A2
A3
Intra-DAS TESI
ENNI
ENNI
P
W*
P*
W
B3
B1
B2
A1
A2
A3
W
P*
W*
P
ENNI
ENNI
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U1
U2
SVLAN EC Relay
SVLAN EC Relay
U1
U2
Half-DAS
Half-DAS
Intra-DAS TESI
Half-DAS
X
Right portal node failure or ENNI + Intra-DAS TESI failure
Normal state, no failures
X
X

## Slide 21: Distributed TESI Protection connected to DRNI
W*
P
W
P*
P*
W
P
W*
B3
B1
B2
A1
A2
A3
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U1
U2
Right ENNI failure
Intra-DAS TESI
ENNI
ENNI
Half-DAS
Half-DAS
X
W*
P
W
P*
P*
W
P
`W*
B3
B1
B2
A1
A2
A3
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U1
U2
Left ENNI failure
Intra-DAS TESI
ENNI
ENNI
Half-DAS
Half-DAS
X

## Slide 22: Port filtering entities
Figures 22-2 and 22-4 in 802.1Q illustrate the location of the port filtering entities in a bridge port. How to apply these specifications in the case of a CBP?

## Slide 23: Port filtering entities location in CBP?
19.2/3/5
6.14
6.10
6.14
6.11, 9.5c
19.2/5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
PIP
CBP
SVLAN MEP & MIP
BVLAN/TESI MEP
SVLAN to BVLAN/TESI muxes
19.2/3/5
Port filtering entities 8.6.1/2/4
SVLAN MEP & MIP
BVLAN EC/TESI Relay
SVLAN EC Relay
Port filtering entities 8.6.1/2/4
19.2/3/5
6.14
6.10
6.14
6.11, 9.5c
19.2/5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
19.2/3/5
Port filtering entities 8.6.1/2/4
Port filtering entities 8.6.1/2/4
19.2/3/5
6.14
6.10
6.14
19.2/5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
19.2/3/5
Port filtering entities 8.6.1/2/4
6.11, 9.5c
Port filtering entitIes 8.6.1/2/4
B
C
D
ISID
BSI Relay
ISID
ISID
ISID
ISID
BSI Relay
ISID
ISID
ISID
ISID
BSI Relay
ISID
ISID
ISID
Under normal circumstances, the CBPs are Edge Ports for the BVLAN Ethernet connections and TESI connections and port filtering should not be performed; i.e. fixed forwarding (correct?).
In a DRNI Portal with two nodes, BVLAN and TESI endpoints are duplicated (one in each portal node). Should port filtering be used to control which of the two endpoints is connected to a BVLAN/TESI? Or should we instead control the Port Map in the VLAN Registration Entry for BVLANs and the Filtering Entry for TESIs? Or other?
For case port filtering can be used, what is the location of the port filtering entries in the CBP: A, B, C, D or other? Port filtering may not be the right tool, as BVLAN/TESI MEP functions will generate OAM which is not blocked in case of locations B,C,D. BVLAN and TESI OAM generated by the CBP in the standby gateway node must be blocked.
19.2/3/5
6.14
6.10
6.14
6.11, 9.5c
19.2/5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
6.9
8.5
19.2/3/5
Port filtering entities 8.6.1/2/4
Port filtering entities 8.6.1/2/4
A
ISID
BSI Relay
ISID
ISID
ISID

## Slide 24: PBB Domain with G.8031 SNC protected SVLAN EC
BVLAN EC Relay
SVLAN EC Relay
BVLAN EC Relay
SVLAN EC Relay
BVLAN EC Relay
Intra-DAS BVLAN
Intra-Network BVLAN
Intra-DAS Link
INNI
SVLAN EC Relay
G.8031 SNC protected SVLAN EC has active endpoint at either the right, or the left portal node. The other SVLAN EC endpoint is disabled. The two SVLAN EC endpoints form one virtual endpoint.
SVLAN EC P is transported via BVLAN Ug. SVLAN EC W is transported via BVLAN Ub. SVLAN EC N is transported via the Intra-Network BVLAN.
Should S-MAC address of left & right SVLAN EC P/P* MEP be the same?
BVLAN Ub
SNCP
Half-DSS
BVLAN Ug
Half-DAS
Half-DSS
Half-DAS
W
P
W*
P
W
P*
SVLAN EC P
SVLAN EC W
Should S-MAC address of left & right SVLAN EC W/W* MEP be the same?
Intra-Network SVLAN EC N
DNP Control Protocol
The Half-DSS functions support the distribution of the SNCP endpoints.

## Slide 25: SNC protected SVLAN EC W & P configurations
SVLAN EC Relay
SVLAN EC Relay
Intra-Network BVLAN
SVLAN EC Relay
BVLAN Ub
SNCP
Half-DSS
BVLAN Ug
Half-DAS
Half-DSS
Half-DAS
W
P
W*
P
W
P*
SVLAN EC P
SVLAN EC W
Intra-Network SVLAN EC N
State 1:
Working SVLAN EC = EC W
Protection SVLAN EC = EC P + EC N
State 2:
Working SVLAN EC = EC W + EC N
Protection SVLAN EC = EC P
DNP Control Protocol
W*
P
W
P*
Half-DAS
Half-DAS
Half-DSS
Half-DSS
W*
P
W
P*
Half-DAS
Half-DAS
Half-DSS
Half-DSS
Disabled SVLAN MEP
Active SVLAN MEP
Active SVLAN MEP
Disabled SVLAN MEP
SVLAN EC relay
TESI A drop
SVLAN EC relay
SVLAN EC drop
SVLAN EC drop

## Slide 26: Compound view Normal state, no failures
BVLAN EC/TESI Relay
BVLAN EC/TESI Relay
P
W
W
P
Half-DAS
B
A
Intra-DAS
BVLAN or TESI
ENNI
ENNI
SVLAN EC Relay
SVLAN EC Relay
Ub
Half-DAS
hDTS
W*
P
hDTS
W*
P
B1
A2
hDTS
W
P*
hDTS
W
P*
B3
B2
A1
A3
U1
U2
hDSS
W*
P
Ug
hDSS
W
P*
hDTS: half-Distributed TESI protection Sublayer, hDSS: half-Distributed SNCP Sublayer

## Slide 27: Compound view Right ENNI failure
BVLAN EC/TESI Relay
BVLAN EC/TESI Relay
P
W
W
P
Half-DAS
B
A
Intra-DAS
BVLAN or TESI
ENNI
ENNI
SVLAN EC Relay
SVLAN EC Relay
Ub
Half-DAS
hDTS
W*
P
hDTS
W*
P
B1
A2
hDTS
W
P*
hDTS
W
P*
B3
B2
A1
A3
U1
U2
W*
P
Ug
W
P*
X
hDSS
hDSS
hDTS: half-Distributed TESI protection Sublayer, hDSS: half-Distributed SNCP Sublayer

## Slide 28: Compound view Right ENNI and Intra-DAS link failure (or right portal node failure)
BVLAN EC/TESI Relay
BVLAN EC/TESI Relay
P
W
W
P
Half-DAS
B
A
Intra-DAS
BVLAN or TESI
ENNI
ENNI
SVLAN EC Relay
SVLAN EC Relay
Ub
Half-DAS
hDTS
W*
P
hDTS
W*
P
B1
A2
hDTS
W
P*
hDTS
W
P*
B3
B2
A1
A3
U1
U2
W*
P
Ug
W
P*
X
X
hDSS
hDSS
hDTS: half-Distributed TESI protection Sublayer, hDSS: half-Distributed SNCP Sublayer

## Slide 29: Virtual BVLAN, TESI, SVLAN end points
BVLAN EC/TESI Relay
BVLAN EC/TESI Relay
P
W
W
P
Half-DAS
B
A
Intra-DAS
BVLAN or TESI
ENNI
ENNI
SVLAN EC Relay
SVLAN EC Relay
Ub
Half-DAS
hDTS
W*
P
hDTS
W*
P
B1
A2
hDTS
W
P*
hDTS
W
P*
B3
B2
A1
A3
U1
U2
hDSS
W*
P
Ug
hDSS
W
P*
Virtual BVLAN end point B
Virtual BVLAN end point A
Virtual protected TESI end point B
Virtual protected TESI end point A
Virtual SVLAN segment end point P
Virtual SVLAN segment end point W
Do end points within a virtual end point require a common MAC Address value? Expectation is: yes

## Slide 30: MAC Addresses at CBP/PIP ports
To be added…

## Slide 31: Impact of single switch fabric?
What will be the impact if an IBBEB has a single switch fabric, which supports both the BVLAN/TESI Relay function and the SVLAN Relay function?
BVLAN/TESI Relay
6.9, 9.5b
8.5
19.2
6.7
802.n
PIP
6.14
6.10
6.14
6.11, 9.5c
19.2/3/5
19.2/3/5
6.9, 9.5b
8.5
CBP
PNP
19.2/3/5
SVLAN Relay
BVLAN/TESI Relay
6.9, 9.5b
8.5
19.2
6.7
802.n
6.14
6.10
6.14
6.11, 9.5c
19.2/3/5
19.2/3/5
6.9, 9.5b
8.5
19.2/3/5
SVLAN Relay
Separate B- & S-VLAN fabrics
Combined B- & S-VLAN fabrics
(combined PNP/CBP/PIP)
BVLAN Relay supports MP BVLAN connectivity between two or more PNPs and one or more CBPs
The same connectivity within a IB-BEB with combined B- & S-VLAN Fabric
19.2
6.7
802.n
19.2/3/5
6.9, 9.5b
8.5
6.9, 9.5b
8.5
19.2
6.7
802.n
6.14
6.10
6.14
6.11, 9.5c
19.2/3/5
19.2/3/5
6.9, 9.5b
8.5
19.2/3/5
6.9, 9.5b
8.5
6.14
6.10
6.14
6.11, 9.5c
19.2/3/5
19.2/3/5
Fabric
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX

## Slide 32: Slides added in v2

## Slide 33: PBB-TE Domain with TESI segment protection
TESI Relay
TESI Relay
SVLAN EC Relay
TESI Relay
SVLAN EC Relay
Intra-DAS TESI
Intra-Network TESI
Intra-DAS Link
INNI
SVLAN EC Relay
animated
W
P
W*
P
W
P*
TESI A with segments A1,A2,A3
A1
A2
A3
TESI A1,A2,A3 for protected SVLAN ECs has active segment protected endpoint at either the right, or the left portal node. The other segment protected TESI endpoint is disabled and the associated TESI endpoint is blocked. The two segment protected TESI endpoints form one virtual segment protected endpoint.
Blocked TESI A endpoint
TESI A relay
ESP-MAC address of left & right TESI A endpoints is the same
Segment MEP disabled
W
P
W
P*
W*
P
TESI B with segments B1,B2,B3
B3
Blocked TESI B endpoint
TESI B relay
TESI B1,B2,B3 for protected SVLAN ECs has active segment protected endpoint at either the left, or the right portal node. The other segment protected TESI endpoint is is disabled and the associated TESI endpoint is blocked. The two segment protected TESI endpoints form one virtual segment protected endpoint.
ESP-MAC address of left & right TESI B endpoints is the same
B1
B2
Segment MEP disabled
U1
U2
TESI U1,U2
TESI U1,U2 for unprotected SVLAN ECs has active endpoints at left and right portal nodes.
ESP-MAC address of left & right TESI Ui endpoints is different

## Slide 34: Distributed TESI Segment Protection connected to DRNI
W*
P
W
P*
P*
W
P
W*
Half-DAS
B3
B1
B2
A1
A2
A3
Intra-DAS TESI
ENNI
ENNI
P
W*
P*
W
B3
B1
B2
A1
A2
A3
W
P*
W*
P
ENNI
ENNI
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U1
U2
SVLAN EC Relay
SVLAN EC Relay
U1
U2
Half-DAS
Half-DAS
Intra-DAS TESI
Half-DAS
Right portal node failure or ENNI + Intra-DAS TESI failure
Normal state, no failures
X
X
X

## Slide 35: Distributed TESI Segment Protection connected to DRNI
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U1
U2
Right ENNI failure
Intra-DAS TESI
ENNI
ENNI
Half-DAS
Half-DAS
X
Active Gateway
Standby Gateway
Active Gateway
Standby Gateway
SVLAN EC Relay
SVLAN EC Relay
U1
U2
Left ENNI failure
Intra-DAS TESI
ENNI
ENNI
Half-DAS
Half-DAS
X
W*
P
W
P*
P*
W
P
W*
B3
B1
B2
A1
A2
A3
W*
P
W
P*
P*
W
P
W*
B3
B1
B2
A1
A2
A3