## Slide 1: SRP Redundant Multipath Stream Selection (4) IEEE 802.1 AVB WG Sep 2011
Presented by: Philippe Klein, Broadcom
phkl-srp-stream-path-selection-0911-v01

## Slide 2: The Goals
Multipath streams to maximize bandwidth offered by the whole network topology
Stream Redundancy
T
B
B
B
B
L
L
T
B
B
B
B
L
L
Spanning Tree
B
B
B
B
L
L
T
MSRP Streams
Topology
Stream follows the spanning tree
Multi-path streams beyond spanning tree
Stream Redundancy

## Slide 3: Additional SRP Talker Advertise Attributes
New SRP Talker Advertise Attributes:
  Source Port Stream_subID (could either be the Talker ports or the first downstream bridge “splitting” the TA over multiple egress ports)
  Sequence ID (“easiest” option for loop protection; small counter is good enough)
  Link Cost (computed from multiple metrics, specific computation on a per profile base) or Link Metrics

## Slide 4: Additional SRP Talker Advertise Attributes (cont)
New SRP Talker Advertise Attributes:
  Stream Reference Counters:
    Stream Ref Count: indicates the number of TA with different source Port Stream_subID handled by the bridge for a given stream ID
    Port Ref Count: indicates the number of TA with different Stream_subID handled by a given port of the bridge for a given stream ID
    Propagates the highest reference counts along the path
    If a listener requires redundancy without single point of failure, it will select the TAs with a Stream Ref Count equal to 1. If such TAs are not received by the Listener, it indicates a network engineering issue for which the fix is beyond the scope of SRP.
    The same scheme applies for a single point of failure per “wire”

## Slide 5: Bridge’s TA Propagation
TAs are forwarded over every bridge’s egress port (regardless of their RSTP port state)
  Loop protection by blocking duplicated TAs based on sequence ID
  TAs could optionally not be forwarded on ports associated to a given spanning tree, allowing traffic separation between MSRP streams and “IT traffic”
Configurable bridge selection between same Stream TA based on:
  Stream SubID & Link Cost (configurable computation) / Metrics (configurable precedence between metrics)
  Lowest Stream Reference Count

## Slide 6: MSRP Stream Forwarding
MSRP Stream Paths created with the “multipath” MSRP TA/LR scheme presented in the previous slides will be loop free beyond Spanning Trees:
However to forward MSRP streams beyond these Spanning Trees without modifying current bridge implementations (which might first filter out ingress datagrams based on bridge’s port states), these streams could be associated to a “Dummy Spanning Tree” for which bridge ports will always be configured to “forwarding” state.

## Slide 7: Open Question
What is the effect of a change of the accumulated latency if the path is re-selected “on the fly” (i.e. a link fails and new spanning tree is established). Does the stream fails on any change ?
Is it possible to configure a threshold so that if a new path is re-selected “on the fly” the full registration does not need to take place again (in case of link failure, the upstream bridge to propagate the last stored TA on the ports of the “dummy SP”. The Listener could receive the TAs thru a different path with a different accumulated latency…) ?

## Slide 8
Thank you