## Slide 1
Starvation-free priority precedence Mick Seaman mickseaman@gmail.com
802.1Q provides options for transmission selection. All except for the ‘strict priority’ default require management control. This presentation describes a simple approach that does not require management and imposes a worse case delay on latency sensitive frames that is no worse than for ‘strict priority’ but removes the ‘starvation’ risk for lower priority frames.
Updated: allowing for PFC effects, ETS comparison, soliciting interest.

## Slide 2: Priority precedence – Algorithm1
As for simple strict priority:
Transmission queues per output port per traffic class
Received frames queued in reception order
FIFO queuing, prior to transmission
But:
The frame at the head of each output queue other than that of the highest priority is added to the tail of the next highest queue if (and once) higher priority queues currently contains no such promoted frame
Transmission only occurs from the highest priority queue
1 Andreas pointed out (off-line, last meeting) similarity to operating system process promotion for starvation avoidance.

## Slide 3: Priority precedence – PFC
PFC could pause transmission from traffic class Q+:
Algorithm as described (prior slide) would then pause transmission from lower priority Q, Q-, …
Need algorithm to be mis-configuration (whatever the source) proof
So, instead of promoting ‘the frame’:
Add a ‘marker’ to the higher priority queue, Q+.
When ‘marker’ reaches the head of Q+, transmit from the head of Q (which may be a marker, so from Q-, …)

## Slide 4: Priority precedence – Result
As for simple strict priority:
Transmission of any frame of priority P can be delayed by all previously queued frames of higher priority P+, by previously queued frame of priority P, and by one previously queued frame of lower priority P-.
Gain:
Worst-case delay is the same as for simple strict priority.
Avoids the well-known strict priority starvation issue.
Practical replacement for ETS, which is not delay calculation friendly.
Cost:
The expected/mean delay experienced by frames of priority P will be higher.