## Slide 1
PCF Time Bounded Services
Tim Phipps,
Symbionics

## Slide 2
Current Specification Status
Distributed Coordination Function (DCF)
  Yes
Point Coordination Function (PCF)
  Yes
Distributed Time Bounded Services (DTBS)
  Agreed in principle
PCF Time-Bounded Services (PCF TBS)
  No, Why not?...

## Slide 3
Alternatives
DTBS using Active Signalling
  Rejected because it would require an energy based CCA
DTBS using different Inter-Frame Spacings
  Long delays for asynchronous traffic to access medium
  Very inefficient with more than two priority levels
PCF TBS
  Similar to PCF asynchronous traffic

## Slide 4
Arguments For PCF TBS
In any situation in which a PCF is viable, PCF TBS will be viable also
Low average delay between packets on the air

## Slide 5
What is needed?
Connection ID in CF Up and CF Down packets
Request to be included on the polling list
  Similar to the mechanism used with asynchronous traffic

## Slide 6
AP Initiates Connection
AP requests a connection
  With a maximum payload and an assigned connection ID
STA grants connection
  With connection ID
  Can refuse by not responding

## Slide 7
STA Initiates Connection
STA requests a connection
  With a maximum payload
AP grants connection
  With assigned connection ID
  Can refuse by not responding

## Slide 8
Changes to Frame Formats
Data Frames
  For CF-Up and CF-Down the Duration field can be reused as a connection ID field.
    Duration field has no meaning in Contention Free Period
Management Frame Sub-Types
  Connection Request
  Connection Grant
  End Connection