## Slide 1
MAC Specification Issues
Tim Phipps,
Symbionics

## Slide 2
Weight Field and Timing Synchronisation
There are many references in 20b3 to a Weight field, but no specification of how it is used
A mechanism is needed for timing synchronisation
  Trivial in infrastructure networks
  More difficult in ad-hoc networks . . .

## Slide 3
Ad-Hoc Timing Synchronisation
Forming an ad-hoc network
Joining an ad-hoc network
Steady State ad-hoc network
Merging two ad-hoc networks

## Slide 4
Form an ad-hoc network
Covered by section 7.1.3.6 of 20b3
Set status to “Synchronised” and start beaconing
A small delay whilst this station checks that there is no existing network
  Then synchronised beaconing will start

## Slide 5
Join an Ad-Hoc Network
Covered by section 7.1.4
An unsynchronised station adopts a synchronised time-stamp and becomes synchronised itself
Start to send beacons

## Slide 6
Steady State Ad-hoc Network
All stations are synchronised and take it in turn to send beacons
Received time-stamps in beacons may not equal local value of time
Need a distributed, stable algorithm
Propose that
  Take the average
  New Time = (Old local time + Received time stamp) / 2

## Slide 7
Re-merging an Ad-hoc network
BSS IDs are unique
  Therefore, can only get two identical BSS IDs by a split
Re-merging may cause stations to change timing references by a large amount
  No clever algorithm can avoid this
Sleep-wake patterns will be disrupted
  Stations should not stay in power saving mode if they continue to miss beacon transmissions

## Slide 8
Conclusion
There is no benefit if stations transmit time-stamps (in beacons and probe responses) before they are synchronised
Synchronisation can be gained by adopting a time-stamp
Synchronisation can be maintained by sticking to an average value
  Re-merging of a split BSS can be achieved

## Slide 9
Estimate of Power Saving Status
In an infrastructure network an AP must track the Power Saving Status of Stations
  Probably possible
  The AP is Continuously Awake
In an ad-hoc network a Station must track the Power Saving Status of other Stations
  Probably not possible
  The Station is NOT (necessarily) Continuously Awake
  Errors will occur . . .

## Slide 10
Bad Estimate of PS Status
If the transmitter thinks that a receiver is awake it will continue to retry a packet . . .
If a receiver is not awake when a packet is transmitted, or retransmitted, it will fail and refail and refail and refail and . . .
Result:
  Every bad estimate will often result in the maximum number of retries followed by a failure

## Slide 11
Solution
Expect bad estimates of power saving status
Allow a station to change its estimate
Use failed retries as an indication of failure

## Slide 12
Probe Responder
To guarantee that a probe is received there must be at least one node awake in a network at any given time, this node is the probe responder
In an infrastructure network this must be the AP
In an ad-hoc network there must be at least one STA awake . . .

## Slide 13
Ad-hoc Network Probe Responses
The station that sent the last beacon stays awake
The station that (thinks it) sent the last beacon sends probe responses
  Note there may be more than one, if not perfect connectivity
No longer any need to cancel queued probe responses

## Slide 14
Motion (Synchronisation)
“That no station shall be allowed to transmit a time-stamp field before it is synchronised.
That unsynchronised stations may adopt a received time-stamp to become synchronised.
That timing synchronisation be maintained in an ad-hoc network by adjusting a synchronised timing reference to be the average of itself and any time-stamp received from another station in that network
That the weight field be removed from the specification”.

## Slide 15
Motion (Power Saving Status)
“That the estimated power saving state of another station is based on the power management information transmitted by that station and on additional information available locally (such as history of failed transmission attempts) which may be deemed relevant”.

## Slide 16
Motion (Probe Responder)
“That in an network there shall be at least one node that is awake at any given time to respond to probes.
In an ad-hoc network probe responses shall be sent by the station that sent the beacon.
Stations do not need to cancel a pending probe response transmission if they observe a successful probe response from another station in the same network”.