| Seq. # | Section number | your initials |
| --- | --- | --- |

Cmnt type

| E, e, T, t | Part of NO vote | Corrected Text/Comment | Rationale | Disposition/Rebuttal |
| --- | --- | --- | --- | --- |
|  | 8.1.3.3 | RMr | t |
| Else if the ESSID designates an ad hoc network, select an ad hoc BSSID.... | The ESSID ad hoc designation is not defined anywhere, and does not seem appropriate. |

8.4.1.1.1

8.4.2.1.1

8.4.3.1.1

| 8.4.4.1.14 | RMr |
| --- | --- |
|  | Change aPower_Management_State to aPower_Management_Mode. | Changes required to match with 8.2.1.2 (that defines aPower_Management_Mode). |
| 8.4.1.1.1 | RMr | T |

Add the following:

aPower_Mgt_Ability,

aCF_Aware

1.	Manufactures should have the ability to provide either power  saving STAs, or devices for which power saving is not applicable.

| 2. CF awareness is optional throughout the draft. |
| --- |
| 8.4.2.1.1 | RMr | T |

Add the following:

aPower_Mgt_Ability                GET,

| aCF_Aware GET, | Refer to my comment on 8.4.1.1.1 |
| --- | --- |
| 8.4.3.1.1 | RMr | T |

Add the following:

aPower_Mgt_Ability,

| aCF_Aware, | Refer to my comment on 8.4.1.1.1 |
| --- | --- |
| 8.4.4.1 | RMr | T |

Add two new subsections:

8.4.4.x.	aPower_Mgt_Ability

Power_Mgt_Ability ATTRIBUTE

WITH APPROPRIATE SYNTAX

Boolean;

BEHAVIOUR DEFINED AS

"True if this station has power saving ability, false otherwise.";

REGISTERED AS

{ iso(1) member-body(2) us(840) ieee802dot11(10036) SMT(0) attribute(7) power_mgt_ability(x) };

8.4.4.y.	aCF_Aware

CF_Aware ATTRIBUTE

WITH APPROPRIATE SYNTAX

boolean;

BEHAVIOUR DEFINED AS

"True if this station is contention-free aware, false otherwise.";

REGISTERED AS

{ iso(1) member-body(2) us(840) ieee802dot11(10036) SMT(0) attribute(7) cf_aware(y) };

|  | Refer to my comment on 8.4.1.1.1 |
| --- | --- |
| 8.4.4.1 | RMr | E |
| From subsection 18 onwards, replace the "###" notations in the REGISTERED AS paragraphs, with the appropriate numbering. |