## Slide 1
Authentication Letter Ballot comments Wim Diepstraten AT&T WCND Nieuwegein The Netherlands
IEEE P802.11
Wireless Access Method and Physical Layer Specification

## Slide 2
Authentication discussion
This document intends to analyse the functionality of the different authentication schemes that are currently defined in D2 draft, and tries to identify the differences in their characteristics
There are 3 authentication mechanisms defined:
  Open Authentication
  Shared Key authentication
  Propriatary authentication
Basic assumptions.
  The objective for the 802.11 authentication is simply used to bring the wireless link up to the assumed physical standard of a wired link (section 2.4.3.1 par 5)
    So “Open Authentication” that compares the STA address against a “Allowed List” does achieve this basic function.
    But a station could fraud to be another station by using its SA address.
  More sophisticated Authentication does only make sense when Privacy is used on all data traffic, so when WEP is on.
    otherwise stations can always fake to be an other station to send its information anyway.
  If WEP is not used, then a more sophisticated Authentication scheme does not prevent stations to fake identity.
  If a station does know the WEP key, then that is equivalent to a station being physically connected to the wired medium.
    So then we have achieved the spirit of the “Wired Equivelancy”.
So when WEP=on then knowledge of the WEP key does accomplish the “Wired Equivelancy”, and provide a level of implicit authentication.

## Slide 3
Authentication examples:
Open Sytem Authentication:
  Either no Authentication or
  AP can verify allowed membership against SA list.
  This makes sense with WEP = off.
  but does not protect against fake identity.
When WEP=on then knowledge of same key on both end is required to allow communication.
  So this is implicit authentication.
  If Station is not who he claims to be does not make any difference for privacy, because it has the key, so it can see all traffic.
So Implicit authentication makes a lot of sense from a privacy point of view.
  It does accomplish the “Wired Equivelancy” goal.

## Slide 4
Shared Key Authentication:
Shared Key Authentication:
  Needs WEP algorithm + Shared Key in Authentication phase.
    The same key is used for Privacy and Authentication (no separate key provisions in MIB).
  AP can do an additional membership check against SA list.
  Using Shared Key Authentication, without using WEP for data privacy does not make sense from privacy point of view. (We are not doing security but privacy).
So Shared Key Authentication does also rely on knowledge of the same key on both ends.
What is the value of Shared Key versus Open System Authentication when WEP is on???????
  So why bother?
Conclusion: Shared Key authentication is equivalent to Open System authentication, because they both depend on the knowledge of the same key on both ends.
Recommendation: Delete Shared Key Authentication method.

## Slide 5
Propriatary Authentication:
Propriatary algorithm possible.
  Can take relative long time depending on algorithm.
  Therefore desire for pre-authentication possibility.
  Station can be authenticated with multiple APs and Stations at the same time according to current scheme.
    This is basic requirement to allow pre-authentication.
There is a desire for support of other authentication methods.
  This is provided by the mechanism as currently defined.
  Although from a privacy point of view it does not provide additional protection when the WEP key is known.

## Slide 6
Maintaining Authentication State:
Stations need to be able to be authenticated with multiple stations at same time.
  Basicly to allow pre-authentication to prevent long propriatary authentication delays.
Currently each TA/RA pair must maintain a authentication state variable.
  Authentication is needed before any traffic can occur between a given station (TA/RA) pair.
  For an AP this is no problem, because it needs to maintain per station knowledge for all kind of purposes.
  For a Station in an IS this is default no problem, as long as all traffic is going via the AP (DS).
  In Ad-Hoc a Station does need to maintain State information for all stations it wants to communicate with.
  The same is true for a Station in an IS that wants to do direct S-to-S traffic, then it needs to maintain extra Authentication State information for each station that wants to communicate directly, in addition to the AP.
Effect of Authentication requirement for S-to-S.
  First transmission to a given station should be a Authentication handshake.
  If there is a mismatch between state information on both ends then traffic is dropped (although Acked), and there is no feedback about this occuring.
  Similar to suggested changes in AP, rules could be changed such that if such is detected, then a station has to do a deAuthenticate, to get state information on both ends in line.
  However do we need/want this complexity??
Authentication and WEP was there primarily to protect the DS, and to prevent to compromise the privacy of the existing wired network.
  For Ad-Hoc implicit authentication is achieved when WEP is used.
  This is more then sufficient for Ad-Hoc.

## Slide 7
Implicit Authentication in Ad-Hoc
Conclusion:
  Implicit Authentication is enough for Ad-Hoc.
  So no explicit authentication is needed.
  So no S-to-S state information needs to be maintained.
    which is an N to N problem.
  Complexity reduction for Stations.
  This is accomplished by allowing S-to-S traffic in State 1 of Figure 2-8. (To_DS = off).
This can also simplify the Association:
  Define an Authentication field in the (Re)Association frames.
    This can have the value:
      Pre-authenticate
      Open System
      Or “Shared Key” if not deleted.
    If value is Pre-Authenticate, then an explicit Authentication cycle is needed.
    If value is open Sytem, then Association can proceed as normal.
      Only returning status should show separate authentication failure code.
  Association is reduced to two frames.
  pre-authentication is still possible.
Conclusion:
  Using implicit “authentication only” for Ad-Hoc allows combined Association/Authentication frames without any loss of capability / flexibility.
  Also applies to any traffic with To_DS and From_DS both false
Recommendation: Authentication is not needed for Ad-Hoc. So allow direct data frames (To_DS and From_DS both false) also as Class-1 frame.