Title

| 1 |
| --- |
| mtr | e |

The following changes must be made in order to get the MIB to compile

-- dot11AuthenticationResponseTimeOut must be an Unsigned32, not an INTEGER (out of range)

-- dot11AssociationResponseTimeOut must be an Unsigned32, not an INTEGER (out of range)

-- dot11MaxTransmitMSDULifetime must be an Unsigned32, not an INTEGER (out of range)

-- dot11MaxReceiveLifetime must be an Unsigned32, not an INTEGER (out of range)

-- dot11PrivacyOptionImplemented needs to be type TruthValue

-- dot11PrivacyInvoked needs to be type TruthValue

-- dot11ExcludeUnencrypted needs to be type TruthValue

-- dot11SupportedTxAntenna needs to be type TruthValue

-- dot11SupportedRxAntenna needs to be type TruthValue

-- dot11DiversitySelectionRx needs to be type TruthValue

-- dot11TempType enumerations must begin with a lower-case letter

-- dot11TxPowerLevel5 missing a '.' in SYNTAX

-- dot11CurrentCCAMode enumerations must remove '_' (illegal character)

-- dot11CurrentTxAntenna:  range should be (1..255), not (0..255), since 0 is not a valid index into the corresponding dot11AntennasListTable

-- dot11CurrentRxAntenna:  range should be (1..255), not (0..255), since 0 is not a valid index into the corresponding dot11AntennasListTable

| -- There are several comments referring to "dot11AntennaeListTable", which does not exist. The table is called "dot11AntennasListTable". |
| --- |
| 2 |
| mtr | e |
| -- dot11TempType still has TempType3 |
| 3 |
| mtr | e |

-- compliance section dot11SmtAuthenticationAlgorithms references the no-longer-existent dot11AuthenticationAlgorithmsStatus

-- dot11ManufacturerID needs a DisplayString size

-- dot11ProductID needs a DisplayString size

| -- dot11CurrentCCAMode enumerations must begin with a lower-case letter |
| --- |
| 4 |
| mtr | e |

These two didn't cause it to not compile, but they do correct semantic errors.

--  dot11WEPICVErrorCount needs to be Counter32 instead of Integer32.

-- dot11WEPExcludedCount needs to be Counter32 instead of Integer32.