## Slide 1
Slide 1
Complement to Comparison DATA of QPSK modulation March, 1998 Kazuhiro OKANOUE, Yoshikazu KAKURA, Tomoki OHSAWA NEC Corporation 4-1-1, Miyazaki, Miyamae-ku, Kawasaki, 216-8555, JAPAN Tel: +81 44 856 2255 Fax: +81 44 856 2230 E-mail:{okanoue,kakura,ohsawa}@ccm.CL.nec.co.jp
IEEE P802.11
Wireless LANs
Notes: Month 1998
Page 1
Submission
Abstract
This document complements comparison data described in Doc 98/74r1.

## Slide 2
Slide 2
Requirements for 5GHz Wireless LAN
Large system capacity
Robustness against multipath fading
Implementation (simple and flexible)
Cost
Performance
Scalability
Notes: Month 1998
Page 2
Submission
In order for wireless LAN in 5GHz band to success, we consider that there exist three points, scalability, performance and cost.
As for scalability issue, the wireless LAN system can support a large number of wireless terminals simultaneously. From the point of a system design’s view, it is one solution for the issue to reuse channels in separate places. In order to do this, the wireless LAN system needs to provide as many channels as possible in a limited band bandwidth.
One of important factor to decide wireless LAN system performances is a robustness against multipath fading. In January meeting, many people in 802.11 agreed that the wireless LAN system should work in multipath fading environments with delay spread of 100-150nsec.
It is important for successful wireless LANs to be provided at a competitive cost with wired LAN equipment. Moreover, it is also important to support several kinds of customers. Some customers requires high-end wireless LANs which can work in multipath environments of several hundreds nsec and may be expensive. Some customers use low-end wireless LANs which are low cost but work only in an office. In this way, it is important for standard to be able to provide several kinds of products, which each vender decides.

## Slide 3
TX-RX Power Consumption Balance
Slide 3
Notes: This graph shows a concept of power consumption in transmitter and receiver. Because small backoff of PA is available for single carrier systems, analogue part in transmitter power consumption can be reduced. In digital part, both OFDM and single carrier need transmission power shaping. However, IFFT in OFDM may be impact on power consumption on digital part.
In receiver, both OFDM and single carriers needs coherent detection. Hence, their power consumption can be considered to be almost same. As for the digital part, OFDM and single carrier uses FFT and equalizer, respectively. It is considered to be almost same power consumption.
Page 3
Submission

## Slide 4
Slide 4
Feature of our proposal
Large system capacity
  5 channels for U-NII lower and middle band
  4 channels for U-NII upper band
Robustness against multipath fading
  100nsec delay spread (simple implementation)
  160nsec delay spread (complex implementation)
Implementation (simple and flexible)
  PMA-MLSCE (as an implementation example)
Notes: Month 1998
Page 4
Submission
In order to satisfy the requirements in the previous page, we have submitted doc 98/74r1 as a comparison data of our proposal.

## Slide 5
Slide 5
Equalizer Implementation
delay spread
Implementation complexity
MLSE
DFE
DDFSE
MLSCE
Notes: Month 1998
Page 5
Submission
In our proposal, equalization method is one of important key points. This graph shows a conceptual comparisons of several equalization methods. MLSE has an excellent capability for delay spread. However, implementation is very complex. DDFSE reduces the MLSE’s implementation complexity by effectively using decision results.
On the other hand, DFE can be realized with lower implementation complexity. However, it requires a feed forward filter with many taps to overcome distortions cased by pre-cursor components, which include complex multipliers. Hence, in multipath environments with longer delay spread, the feed forward will dominate its implementation complexity.
In order to realize wireless LANs, an equalizer plotted in a right-down area in the figure is important. We consider that the MLSCE, which we have used to show comparison data is one example of such an equalizer.
In this way, several kinds of equalization methods can be applied to QPSK modulation. We consider this feature can provide venders flexibility of their implementation.

## Slide 6
Slide 6
System Capacity
Notes: Month 1998
Page 6
Submission
This graph shows rough estimation of throughput versus the number of channels in a cell based on our proposed configuration of 25Mbps. Hidden terminals degrade the throughput in a cell larger than 60m.
Our 5 channel configuration can achieve about 11Mbps throughput. We would like to explain mode detail in the next meeting for capacity.

## Slide 7
Slide 7
General Description
Notes: Month 1998
Page 7
Submission
Our proposal supports 25Mbps and 20.3125Mbps. In 20.3125Mbps, we use an expanded BCH codes of (32,26,3).
The channel separation of 18.75MHz realizes no adjacent channel interference with an ideal transmitter and receiver.
Channel allocations of lower, middle and upper bands are described in doc 98/74r1.
We calculated maximum power based on the spectrum mask in the following slide by using 2.5mW/MHz, 12.5mW/MHz and 50mW/MHz for lower, middle and upper band, respectively.
Performance graphs are described in doc 98/74.

## Slide 8
Slide 8
Spectrum Mask for calculation of maximum power
Notes: Month 1998
Page 8
Submission
This figure shows a spectrum mask we used to evaluate maximum transmission power.

## Slide 9
Slide 9
Per-Rate Feature Summary
noise floor of –174 dBm/Hz, +74dB for transmission bandwidth
noise figure +10dB, an implementation margin of +5dB
1) Assumptions:
Notes: Month 1998
Page 9
Submission
As a sensitivity, we assumed the following values:
- noise floor: -174 dbm,
-noise figure +10db
- implementation loss 5db
Performances of CCI, ACI and Alternate channel interference are described in doc 98/74r1.

## Slide 10
Slide 10
Per-Rate Performance Summary (Simple Implementation)
Notes: Month 1998
Page 10
Submission
Doc 98/74r1 includes a performance graphs for the proposed values.

## Slide 11
Slide 11
Per-Rate Performance Summary (Complex Implementation)
Notes: Month 1998
Page 11
Submission
Doc 98/74r1 includes a performance graphs for the proposed values.

## Slide 12
Slide 12
Timing and Overhead related Summary
Notes: Month 1998
Page 12
Submission
Key parameters to decide system throughput are SIFSTime and SlotTime. We calculate them based on the equations in the following slide. The equations have been defined in section 9.2.10 of P802.11D7.0.
As an aAirPropagationTime, we assumed transmission length of 150m.

## Slide 13
Slide 13
SlotTime and SIFSTime
SlotTime=CCATime+RxTxTurnaroundTime+AirPropagationTime+MACProcessingTime
SIFSTime=RxRFDelay+RxPLCPDelay+MACProcessingDelay+RxTxTurnaroundTime
SlotTime=8.9usec
SIFSTime=7.4usec
Notes: Month 1998
Page 13
Submission
SlotTime and SIFSTime have been evaluated based on the above table.