## Slide 1
IEEE 802.11
The Standard to Rely On?
What’s the real difference? What is important?

## Slide 2
Requirements
The indoor Channel multipath
  Delay spread causes “self induced interference”. Frame Error Rates is a user’s and MIS manager’s nightmare!
      10% FER will cause system failures for a significant part of the user community. A small 1000 node system will give 100 support calls! The answer is not “move your notebook into a smaller office!!!
      Without proper attention the standard will be “plug and pray” for the user!

## Slide 3
The Channel Results
TX
RX
-90 dBm sensitivity is achievable! What you get “over a cable”
does not translate into indoor coverage!
The real test is in the practical “radio channel”:

## Slide 4
FER
SNR
The “steeper the slope”
the higher the range.
The Engineering Challenges
Solve the indoor multipath problem
      In the noisy channel
      In the self interference limited channel
PC-Card Format
    (integration and power consumption)
      Keep the processing simple, but effective!
      Pick the best waveform which optimizes the TX and RX current consumption needs.

## Slide 5
The Engineering Challenges
A “System Solution”
    Peak Data Rates
    Maximize # Reuse Channels
Regulations (Spread Spectrum)
      USA (FCC)
        11 chips/symbol +CW test
      Japan (MPT)
        Ratio RF BW/Symbol Rate (need >10 chips/symbol)
      ETSI (Europe)
        Spread Spectrum Power Density

## Slide 6
Spread Spectrum Key?
The Barker Sequence!
  This simple waveform is the key for a low complexity solution to the multipath processing issue!
    Simple means:
      The DSP processor is not “gate limited” (60k Gates and you have excellent results, your multipath headache is gone!)
      The current consumption is very low:
        DSP in CMOS RX <100mA @3.3V. A total PC-CARD solution <300 mA (TX and RX) is not a problem!
t

## Slide 7
Intellectual Property
Clear IP coverage is necessary, we can not make any false assumptions!
A clear “safety net” for all, as part of the IEEE 802 process, due to the PPM IP.

## Slide 8
Summary
PC-Card Form Factor
Low Power Consumption
International Rules
      FCC, ETSI
      MPT (Japan)
Robust Radio in multipath
    Not only for a small office!
Intellectual Property Protection
Integrated unit
< 300mA @3.3 V possible