## Slide 1
Advantages of Code Channelization
Masaharu(Mas) Mori
Clarion Co., Ltd.
Tokyo, Japan
e-mail : masmori@msn.com

## Slide 2
Objectives of the Document
Conventional idea : Code Channelization of the direct sequence system is not useful because of :
  Near-Far problem
  No enough separation
  Complexity of the CDMA system
This document is an introduction to overcome conventional ideas of the channelization and to prove usefulness of Code Channelization.

## Slide 3
Requirement of more frequency channels causes:
Less robustness against multipath because of narrower spreading bandwidth
Less sensitivity because of more bits/symbol
Sometimes amplitude component of the signal, because of more bits/symbol, to consume more power than flat envelope.

## Slide 4
Aspect of the BSA
Reliable BSA area in which acceptable throughput can be guaranteed always and everywhere.
Unreliable BSA area in which the throughput becomes unacceptable depending on time and place.
MIS tries to build WLAN using reliable BSA area.

## Slide 5
Three freq. channels are enough?
This figure shows conceptual BSA arrangement using three frequency channels.
Reliable BSA areas are well separated by frequency channels but unreliable BSA areas overlap reliable BSA areas to cause degradation of performance.

## Slide 6
Undesirable neighbors
3F
2F
1F
My office
SOHO is a very attractive market for WLAN.
It requires many channels in order to avoid interference from neighbors’ WLAN systems.
Management is not available against neighbors.

## Slide 7
Micrilor’s channelization proposal
Two frequency channels are available within 2400 - 2483.5 MHz ISM band.
Eight search-code channels are also available independently to frequency channels.
Sixteen total channels are available by combination of frequency channels and code channels.
Forty-eight data-code channels are also available.

## Slide 8
An example of BSA arrangement by using 16 channels
(f1,C1) (f2.C1) (f1,C2) (f2,C2) (f1,C1)
(f2,C3) (f1,C3) (f2,C4) (f1,C4) (f2,C3)
(f1,C5) (f2,C5) (f1,C6) (f2,C6) (f1.C5)
(f2,C7) (f1,C7) (f2,C8) (f1,C8) (f2,C7)
(f1,C1) (f2.C1) (f1,C2) (f2,C2) (f1,C1)
Four reliable-BSA distance
Four reliable-BSA distance

## Slide 9
Simulation
Throughput for two adjacent BSAs with:
  The same frequency channel and different code channels.
  Same frequency channel and code channel.
Throughput and delay time under interferences from neighbors’ systems.
Using BONeS DESIGNER ver.3.6 by ALTA GROUP of Cedence Design systems, Inc.

## Slide 10
Conditions (1)
(1) The channel access model is based on 802.11 (P802.11D6.1 pp 86-pp 98).
(2) DATA type is INF_DATA and ACK only.
(3) The INF_DATA packets are generated by Poisson distribution.
(4) The radio propagation characteristic is ideal, namely Frame Error is caused by collisions only.
(5) No hidden node is considered.
(6) INF packets consist of same information with fixed length.
(7) Header length not considered.
(8) The positions of STAs are fixed.
(9) Data flow direction : AP to STAs (config. 1 and 2)
STAs to AP (config. 3)

## Slide 11
Conditions (2)

## Slide 12
System Configuration - 1
■ ➡ ❍ ➡ ❍ ➡ ❍ ➡ ❍ ●
BSA-2
BSA-1
■ : An AP belongs to BSA-1 ● : An AP belongs to BSA-2
➡ : Stations belongs to BSA-1 ❍ : Stations belongs to BSA-2
AP1 STA1-1 STA2-4 STA1-2 STA2-3 STA1-3 STA2-2 STA1-4 STA2-1 AP2
0m 2m 4m 6m 8m 10m 12m 14m 16m 18m

## Slide 13
Throughput under config. -1 (INF Length = 4000 bit)
D/U is a parameter of the radio, just the same as -Mj(dB) which is jamming margin.
Solid fine line : Same freq. and code Ch.
Solid thick line: Different freq. channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 14
Baseband Modulation : 16 bit Bi-Orthogonal keying * 16 chips PN sequence
Carrier Modulation : BPSK
Decision Threshold : BER<10-5
Type of Jammer : CW
Average Mj ~ -2.5dB
Jamming margin (Mj) of JX-4000F

## Slide 15
Throughput under config. -1 (INF Length = 12000 bit)
Solid fine line : Same freq. and code Ch.
Solid thick line: Different freq. channels
Dashed line: Same freq. Ch. and Different code channels
CSMA-CA satulation

## Slide 16
Probability of Packet Success under config. -1 (Z0 = -5dB)

## Slide 17
Probability of Packet Success under config. -1 (Z0 = 0dB)
Solid line: Same freq. and code channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 18
Probability of Packet Success under config. -1 (Z0 = 5dB)

## Slide 19
System Configuration - 2
■ ➡ ➡ ➡ ➡ ❍ ❍ ❍ ❍ ●
BSA-2
BSA-1
■ : An AP belongs to BSA-1 ● : An AP belongs to BSA-2
➡ : Stations belongs to BSA-1 ❍ : Stations belongs to BSA-2
AP1 STA1-1 STA1-2 STA1-3 STA1-4 STA2-4 STA2-3 STA2-2 STA2-1 AP2
0m 2m 4m 6m 8m 10m 12m 14m 16m 18m

## Slide 20
Throughput under config. -2 (INF Length = 4000 bit)

## Slide 21
Probability of Packet Success under config. -2 (INF Length = 4000 bit, Z0 = -1dB)
Solid line: Same freq. and code channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 22
Probability of Packet Success under config. -2 (INF Length = 4000 bit, Z0 = 0dB)
Solid line: Same freq. and code channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 23
Probability of Packet Success under config. -2 (INF Length = 4000 bit, Z0 = 1dB)
Solid line: Same freq. and code channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 24
Probability of Packet Success under config. -2 (INF Length = 4000 bit, Z0 = 2dB)
Solid line: Same freq. and code channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 25
Probability of Packet Success under config. -2 (INF Length = 4000 bit, Z0 = 5dB)
Solid line: Same freq. and code channels
Dashed line: Same freq. Ch. and Different code channels

## Slide 26
Prominent applications of code channelization
3F
2F
1F
4F
Code #4
Code #3
Code #2
Code #1
Code Channelization is useful especially in order to obtain floor-to-floor isolation or room-to-room isolation.
The effectiveness has been proved through many applications of Clarion’s SS products in Japan.

## Slide 27
System Configuration - 3
■ ➡ ➡ ➡ ➡
My System
AP STA1 STA2 STA3 STA4
Neighbors’
Systems
Packet Length =
512 bit,
Mean generation period = T_other
My system and neighbors’ systems are being operated by the same frequency channel without code channelization. Signals from neighbors’ systems can be sensed by probability of p. D/U ratio is always enough large to ignore errors by collisions.
Interferences

## Slide 28
Maximum throughput under config. -3 (INF Length = 512bit)
(msec)

## Slide 29
Maximum throughput under config. -3 (INF Length = 12000bit)
T_other (msec)

## Slide 30
Load vs. Throughput under config. -3 INF Length = 512 bit, T_other = 0.01msec (Aggregate Load of interference = 5.12)

## Slide 31
Load vs. Throughput under config. -3 INF Length = 512 bit, T_other = 0.1msec (Aggregate Load of interferences = 0.512)

## Slide 32
Load vs. Throughput under config. -3 INF Length = 12000 bit, T_other = 0.1msec (Aggregate Load of interferences = 0.512)

## Slide 33
Load vs. Throughput under config. -3 INF Length = 512 bit, T_other = 1msec (Aggregate Load of interferences = 0.0512)

## Slide 34
Load vs. Throughput under config. -3 INF Length = 12000 bit, T_other = 1msec (Aggregate Load of interferences = 0.0512)

## Slide 35
Mean Delay under config. -3 INF Length = 512, T_other = 0.1msec (Aggregate Load of interferences = 0.512)

## Slide 36
Mean Delay under config. -3 INF Length = 12000, T_other = 0.1msec (Aggregate Load of interferences = 0.512)

## Slide 37
Mean Delay under config. -3 INF Length = 512, T_other = 1msec (Aggregate Load of interferences = 0.0512)

## Slide 38
Mean Delay under config. -3 INF Length = 12000, T_other = 1msec (Aggregate Load of interferences = 0.0512)

## Slide 39
Conclusion
Code channelization provides better throughput if BSAs are not overlapped.
  To obtain floor-to-floor and room-to-room isolation.
  For unmanaged BSAs (SOHO market).
Substantial overlapping of BSAs causes degradation because of the Near-Far problem.
Next simulation must show system capacity and include interference and leakage (shared capacity) effects.