## Slide 1
IEEE 802.11 Wireless Access Method and Physical Specification
Title: FH Interoperability Addition to Harris HS PHYProposal
Date: March 9, 1998
Author: Dean Kawaguchi
Symbol Technologies, Inc.
2145 Hamilton Ave
San Jose, CA. 95125
Telephone: (408)369-2629
FAX: (408)369-2737
email: DeanK@psd.symbol.com

## Slide 2
FH Backward Interoperability
Backward interoperability with 1/2 Mbps DS PHY is provided for within the Harris High Speed (HS) DS PHY proposal
  Important for maximum range, robustness in severe multipath, minimum collisions (CCA), variety of cost vs performance tradeoff options, and preservation of customer investments
We propose an FH PHY backward interoperability mode as an option for the Harris HS proposal
  This proposal does not modify the basic modulation format, but it assumes the addition of the HS preamble; wraps around the Harris proposal
  Two fundamental changes required for FH interoperability are
1) hopping of the wideband DS signal synchronized to the FH hop sequences
2) using the FH preamble in front of the HS preamble and data
Resulting system is not a hybrid system with regard to FCC rules, but a dual mode radio: an FH mode and a DS mode that also hops

## Slide 3
Why is FH interoperability important?
The same reasons that applied to the DS PHY plus improved reliability, or survivability, in interference limited environments
  Hopping of the wideband HS signal will provide a level of protection against a variety of fixed frequency intereference.
  As a last line of defense, backing down to 1/2 Mbps FH with 79 1 MHz channels will provide the best chance of operating through interference.
Symbol’s experiences in the 900 MHz band since 1990 have shown
  Fixed frequency system will fail in the presence of interference
  Changing channels is slow and often does not work
  Our proprietary format 900 MHz DS system has evolved into a hopping DS system to provide reliable connection in the presence of interference
The 2.4 GHz band may eventually be worse than the 900 MHz band since it is the only unlicensed band available worldwide
  Also, non-802.11 systems in this band are already and will continue to be a significant portion of the usage of this band

## Slide 4
Efficiency of Frequency Plan
Most efficient use of the band would be achieved by frequency planning in a cellular arrangement such as used by DS
  Sharing possible with other 802.11 DS systems
  However, that requires exclusive use of the band which cannot be guaranteed in the unlicensed ISM band
1 MHz FH can perform quite well without control of the band
  Allows more overlapping BSS’s (essentially non interfering) than DS
  More tolerant to non-802.11 devices
The FH interoperability mode achieves a compromise of the best of both formats, achieving both 11 Mbps peak data rates and falling back to 1 MHz FH for maximum reliability in dense environments
  It trades off the efficiency of the cell planning approach for the reliability of frequency hopping and the flexibility of scaling down to a 1 MHz narrow FH signal

## Slide 5
Hop Sequences, Synchronization, and Frequency Plan
Hopping of the HS PHY will be defined and synchronized using the mechanisms contained in the existing 802.11 FH PHY
  The particular 1 MHz channel selected will be associated with a HS PHY channel center frequency
5 HS PHY channels about 22 MHz null to null bandwidth, partially overlapped with a channel spacing of 15 MHz
  Subset of the center frequencies defined in the DS PHY section
  A number of 1 MHz FH channels are assigned to each HS channel
The HS channel that has its center frequency closest to the selected 1 MHz channel is used to transmit and receive HS data
  Maximum offset in center frequency between 1 MHz FH and HS channel is generally +/- 7 MHz except at band edge (-10 to +8 MHz).
  Power and sensitivity would be reduced by several dB at the -10 MHz offset due to filter rejection

## Slide 6
Frequency Plan of HS PHY and FH PHY channels

## Slide 7
Other Frequency Consideration
Consider option of adding new FH hop sequences which improves performance in the mixed HS and FH environments.
  1) By hopping a minimum of 15 MHz instead of 6 would guarantee that the next hop will also hop the wideband channel.
  2a) Reducing the number of channels to 77 by chopping off the bottom 2 channels would limit the frequency offset of the 1 MHz FH channel to +/- 8 MHz from the HS channel center; use 2404 to 2480 MHz
  2b) The minimum number of FH channels specified by the FCC is 75. Chopping off 1 more channel on each end of the band from (2a) would limit the FH to HS channel offsets to +/- 7 MHz; use 2405 to 2479 MHz
Backward interoperability with the DS PHY necessitates turning off the hopping feature since hopping is not part of existing DS PHY
  Turning off the HS hopping of course loses the interference mitigation capabilities of the hopping

## Slide 8
FH Backward Interoperability Header
Proposal uses an FH 1 Mbps preamble and headerprior to the short HS preamble and header
  Provides for 1/2 Mbps FH operation when range, multipath, or backwards interoperability required
  Units that are operating in 1/2 Mbps FH mode only will be able to see the length of the frame and defer for the duration of the frame.
FH Backward Interoperability Frame Format
DS Backward Interoperability Frame Format

## Slide 9
Data Rates in Modified PLCP Signaling Field
The 4 bit FH PLCP Signaling Field will be modified to utilize the reserved bit b0 to expand the data rates from 8 to 16 values
b0 b1 b2 b3 Indicated rate
0 X X X Rates 1 - 4.5 Mbps per existing text
1 0 0 0 5.5 Mbps
1 0 0 1 11 Mbps
1 0 1 0 16.5 Mbps
1 0 1 1 22 Mbps
1 1 0 0 27.5 Mbps
1 1 0 1 33 Mbps
1 1 1 0 38.5 Mbps
1 1 1 1 44 Mbps
To maintain hopping without the FH PHY backward interoperability header, the base rate of the BSS could be set at the high speed rate
  However, to retain the 1/2 Mbps FH rate scaling capability, the 1 Mbps FH header must be added on whenever the rate scaling feature is needed.

## Slide 10
1/11 Mbps Cross Interference and CCA
If there is only one BSS, there will not be excessive collisions with the mixed FH and HS operation
  Everyone will hear the FH interoperability header
When there are more than one BSS, there may be 1/2 Mbps FH traffic at other channels inside the wideband HS channel
  May not see the FH header, but could see the wideband HS header
  The probability of interference of this mixed mode case is in general better than that of two hopping HS BSS’s because adjacent HS channels are less of a problem
Implementation options available to perform CCA on all 1 MHz channels within the wideband HS channel
  These vary from simple RSSI techniques to more complex algorithms implemented mainly at the cost of additional gates

## Slide 11
Rate Switching Algorithms
The algorithms and triggers for rate switching between the rates in the released standard are not specified by 802.11
  This will be the same in the case of 1/2 Mbps FH to HS operation

## Slide 12
Implementation Considerations
Implementation issues need to be addressed in the standards process to validate the practicality of the proposal
The following discussion summarizes an implementation currently in a joint development process between Harris and Symbol
  The resulting chip set, when released, will be widely available from Harris to all interested companies at fair and reasonable terms
The discussion here assumes primarily digital implementation of the FH processing
  Most of the non-digital functions and components are common with that needed for HS processing

## Slide 13
Two modes of FH processing
Wideband mode allows full interoperability with both HS and FH packets
  Use the same bandwidth SAW as the HS signal processing
  Switch instantaneously from narrow FH preamble to wideband HS packet
  However, selectivity will be less than specified in the FH section.
In narrowband mode, FH operation with maximum selectivity performance ensures best possible performance in interference limited environments.
  Use a 1 MHz SAW to achieve the selectivity of an FH compliant device
Both modes needed to achieve the full benefits of the FH interoperability
  Only wideband mode necessary if you only care about backward interoperability

## Slide 14
Transmitter Block Diagram and Spectrum

## Slide 15
Receiver Block Diagram and Signal Spectrum

## Slide 16
Implementation Tradeoffs
The requirements, problems, and tradeoffs encountered in implementation bring up possible changes to the proposal
One example is the necessity to have a high degree of phase and amplitude balance and small DC offsets
  Phase and amplitude imbalance in the transmitter causes images on the other side of DC that will be unattenuated in the wideband mode
  DC offsets in the transmitter causes unmodulated carrier components which would also be unattenuated in the wideband mode
  In the receiver, phase and amplitude imbalance distorts the signal slightly and reduces the selectivity which would be achievable otherwise
One way to achieve receiver balancing is to estimate and correct the imbalances and offsets during the preamble of a receive packet
  When the FH channel is at the same center frequency as the HS channel, the preamble will vary in I/Q space about 60° on the unit circle
  Difficult to separate the I and Q imbalance and offset components

## Slide 17
Implementation Tradeoffs (cont.)
Three options to resolve this problem are:
1) Measure and correct between regular packets
2) Offset LO tuning and process signal at a small frequency offset
3) Select a different center frequency for the wideband signal, i.e., the channel center frequency 5 MHz away. This will increase the number of channels to 13 overlapping channels.
The first two options only affect the implementation, whereas the third one changes the protocol to simplify the implementation. In this particular case, the degree of change to the protocol is probably not warranted.