## Slide 1: FEC (Forward Error Control) is Not Overhead
Chris Heegard & Matthew B. Shoemake
Alantro Communications

## Slide 2: Overhead
Subtracts from the primary goal of transmission:
  reliable conveyance of user information (messages from transmitter to receiver)
Data
Data
Data

## Slide 3: Examples of Overhead
  a frame synchronization in a packet system
  a packet preamble
  a pilot tone
These functions help with higher level objectives or for estimation and tracking of channel parameters

## Slide 4: Redundancy
Adds to the primary goal of transmission
  reliable conveyance of user information
Data
Data
Data

## Slide 5: The Distinguishing Feature
Overhead is independent of the data
  It helps with auxiliary functions, yet subtracts from resources
    Power
    Bandwidth
    Data Rate
Redundancy is a function of the data
  It help with the primary function, it enhances the utilization of resources

## Slide 6: FEC is considered as “overhead” when applied as a “Band-Aid”
A communications system is designed without coding, it is not robust enough
An ECC (error control code) is used to “fix” the system
  improvement of reliability
  loss in rate (“overhead”)
This approach is a mistake in the design of a fresh system!

## Slide 7: How to Correctly Design an FEC
Fix a data rate (user rate) R
Define a large signal set that generates more than 2R*T signals in T seconds
Judiciously select a subset of 2R*T signals from the large set
  Maximize noise immunity
    Keep distinct signal well separated (Energy)

## Slide 8: The “Overhead” of QPSK as a Coding of QAM
Rate = 2 bits/symbol
Overhead = 2 bits/symbol ???

## Slide 9: Uncoded Modulation
Break data stream into small pieces
  map onto independent dimensions
  Noise occasionally causes symbol error ==> data error
Data:
Symbols:

## Slide 10: Coded Modulation
Have each bit of data affect many symbols
Average out the noise with the decoding
Data:
Symbols:

## Slide 11: Making Signals Robust
Maximize energy that differentiates distinct signals
AWGN (Additive White Gaussian Noise)

## Slide 12: Robust Signals
Multipath
  It is intuitively correct that signals that have large energy separation at the input of a filter are better distinguishable at the output of the filter.
Filter