## Slide 1
2.4 GHz High Rate PHY
Harris Submissions
for Comparison Matrix

## Slide 2
11 Bit Barker Word
56
59
65
6A
03
0C
30
3f
8-ary modified Walsh Functions
22 MHz
11 MBps
QMBOK
5.5 MBps
BMBOK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS BPSK
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit encoded to
2 code words
11 chips
1 MSps
2 bits encoded to
4 code words
8 chips
1.375 MSps
4 bits encoded to
16 code words
8 bits encoded to
2x16 code words
8 chips
1.375 MSps
I
Q
I, Q
I
Q
I, Q
Modulation Technique and data rates
Notes: The Harris suggested high rate modulation is a form of M-ary Bi-Orthogonal keying. We propose that both Binary and Quadrature forms of this modulation be used to provide multiple rates for stressed links.

## Slide 3
Pick One
of 8 Walsh
Functions
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
1
QMBOK Modulator Technique for 11 MBps
Notes: This slide shows how to form our suggested modulation type. M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal vectors by the data word. Since the I and Q channels can be considered independent when coherently processed, both can be modulated this way. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 4
Receiver Sensitivity
Data from two different radio units at two data rates
Notes: The sensitivity of two typical real radios was tested and the results shown here. The sensitivity is in line with expected results and shows that the MBOK waveform performs well in thermal noise.

## Slide 5
Reference Submissions
70254 IEEE 802.11 High data rate PHY extensions
70867 Suggested 802.11 High Rate PHY Technique
71447 Proposed 802.11 High Rate PHY Technique
80467B Harris 2.4 GHz short proposal
80477B Harris 2.4 GHz full Proposal
Notes: The Harris technique has been discussed since early in 1997. Harris has also implemented the technique in silicon and thoroughly tested.

## Slide 6
RF/IF Complexity relative to current low rate PHY
Basically uses same RF and IF as existing 802.11 DS PHY
Equalized version replaces the IF limiter with AGC and has more A/D converter bits.
A combined DS/FH mode uses non optimal wideband IF filters with some loss of performance in a crowded environment
Notes: The use of the same RF bandwidth makes the design of the radio more or less the same as the existing low rate PHY. The main change is that to get more delay spread capability, the receiver may be enhanced by equalization and that generally is best performed in a linear receiver. That requires an AGC type of receiver rather than a limiting receiver and more bits of ADC conversion.

## Slide 7
Receiver Structure Description
HFA3624
RF/IF
I/Q LO
I ADC
Q ADC
De-
Spread
De
Rotate
De-
Modulate
Spread,
Rotate
Modulate/
Encode
TX/Rcv
Data I/O
Control
Test I/O
AGC
CCA
Quadrature Modulator
Quadrature Demod
5th Order
Butter-
Worth
Low-Pass
Filters
FH/DS Baseband Processor
Qmodem with AGC
HFA3524 Dual Synthesizer
FLASH EEPROM
RAM
MAC
SYSTEM
INTERFACE
MAC
PROCESSOR
CORE
PHYSICAL
LAYER
PROCESSING
MEMORY
SUBSYSTEM
HFA3925
RF Power
Amp. and Tx/Rx Switch
HFA3424 LNA
VCO
VCO
OSC
44MHz
SW
MAC
SUPPORT
FUNCTIONS
Notes: The overall look of the reference radio design for the new high rates is like the existing and proven PRISM design except for the new baseband processor and MAC.

## Slide 8
Baseband Processing Complexity relative to current low rate PHYs
Addition of high rate without equalizer increases the DS only baseband processor complexity from 23K gates to 33 K gates
Addition of equalizer to increase delay spread from 30 to 100 ns takes an additional 40 K gates
The addition of high rate to FH has not been fully worked out yet
Notes: The complexity of the existing design when stripped to the minimum to support the standard was found to be 23 K gates more or less. To add the high rate capability without the equalizer took 10 K more gates. The equalizer is projected to take an additional 40 K gates. Since many of these will be run at high rates, the power consumption must be carefully managed by selectively turning off sections not needed for the moment.

## Slide 9
DEMODULATOR BLOCK DIAGRAM
CORRELATOR
MAGNITUDE
ADC
CORRELATOR
SUB RATE
SAMPLE
ADC
Iin
Qin
CCA
PSK DEMOD
AVERAGE
PHASE
ERROR
LEAD/LAG
FILTER
NCO
ABS
DIF DECODE
COMPLEX
MULTIPLY
SIN/COS
ROM
SYMBOL
DECISION
DECISION
DIRECTED
PHASE DET
DATA
DESCRAM-
BLER
8
INTEGRATE
& DUMP
32 PHASES
PHASE
DET
SYMBOL
TIMING
SQ1
SQ2
DATA
AGC
AGC
CCA
SIGN
CORRECT
PISO
EQUALIZER AND DUAL
WALSH CORRELATOR
BANKS
SHADED BLOCK ARE THE ADDITIONS TO DS FOR FH AND HIGH RATES
SUM
ED
NCO
LEAD/LAG
FILTER
FH DEMOD
Notes: The added capability blends well with the existing circuitry.

## Slide 10
Antenna Diversity and performance impact
Antenna diversity can improve the performance of the link more cheaply than an equalizer but not as much
The performance impact has shown an improvement of a factor of 2 to 4 in PER in field testing
The negative impact is to require additional time in the preamble on the order of 16 us (already covered by the 802.11 preamble)
Notes: The improvements of antenna diversity depend on the ability of the selected decision metric to discriminate the good antenna. The improvement comes cheap, but is is not as much of an improvement as an equalizer can provide.

## Slide 11
Graph of PER Vs. Thermal Noise (no Multipath).
Notes: The performance of the Root Raised Cosine filtering versus the filtering that Harris used is shown. This is to show the effects of the less than ideal, but very reproducible filtering on the waveform. We find that the loss due to filtering is much less than that due to multipath, so the emphasis must be placed on the channel distortion rather than that of the radio. For all of the following charts, we use the practical filtering in the simulations.

## Slide 12
PER Vs. Multipath Only (No Noise).
Equalized (2 Feedforward and 5 Feedback Taps)
Notes: The use of 2 FF and 5 FB taps with the sliding decision feedback equalization is sufficient to insure that the system meets the desired 100 ns delay spread capability.

## Slide 13
PER Vs. Thermal Noise with Multipath at 10% PER. Eb/No at 20% PER for 64 and 1000 byte packets.
Equalized (2 Feedforward and 5 Feedback Taps)
Notes: The performance in both multipath and thermal noise shows that the system is capable of good performance.

## Slide 14
Required Carrier Frequency Accuracy
The new high rate PHY requires the same carrier frequency accuracy as the existing low rate PHY.
The DS limitation is that the maximum carrier frequency offset should be less than 1/8 Th of the symbol rate of the preamble.
Notes: The requirements are the same as the existing standard.

## Slide 15
BER versus Carrier Offset Performance of HFA 3860
Notes: The PER curves show that the acquisition performance is adequate out to the maximum offset allowed. Once you get out to +100 PPM, the performance degrades substantially. This is because the carrier phase roll gets close to 90 degrees per symbol of the header. Exceeding 90 degrees per symbol makes the phase shift ambiguous and the modem can lock up on a sidelobe.

## Slide 16
Required Data Clock Frequency Accuracy
The new high rate PHY requires the same clock frequency accuracy as the existing low rate PHY.
The limitation is that the maximum data clock offset should drift more than 1/8th of a chip in 128 us.

## Slide 17
BER versus Clock Offset Performance of HFA 3860
Notes: The performance of the Harris implementation is based on the performance of the symbol tracking loops. Our implementation has better tracking on the new high rate modes than on the existing modes. This is due to using 1/8th chip tracking on the high rate modulation and 1/4th chip tracking on the lower rate modulations.

## Slide 18
Preamble Length
Our basic approach is to include the standard DS or FH 802.11 preamble and header
This length includes ample time to do diversity and equalization
For the cases where interoperability is not an issue, a short, high rate header can be used.
Antenna diversity and equalization require a somewhat longer short header than the shortest possible.
Notes: The long, interoperable preamble and header allows ample time to do AGC, diversity selection, and equalizer training along with the normal modem acquisition processing. In the event a shorter preamble and header is desired for maximizing throughput, it must take into account those extra times.

## Slide 19
Slot Times
We propose no change in the DS PHY slot time of 20 us or FH slot time of 50 us.

## Slide 20
CCA mechanism and Co-Channel signal detection time
We measure the correlated signal energy in the preamble over 10 us dwells beginning when the receiver is enabled and compare that to a threshold
FH detection is done on clock energy in similar dwells.

## Slide 21
RX/TX turn around time and SIFS
The transmitter has a 1.3 us processing delay from bits in to bits out the antenna
The receiver has 3.3 us processing delay from bits in the antenna to bits out
The RX/TX turn around time is less than 2 us exclusive of the above delays.
We propose the existing DS 10 us SIFS

## Slide 22
Channelization Scheme
We propose the existing DS channelization scheme.
Three non overlapping channels in the band
A choice of 5 MHz channel centers with 13 channels in the ISM band for the US.

## Slide 23
Adjacent Channel Interference Rejection
8 dB more filter skirt rejection is needed to achieve the same ACI rejection as the existing low rate PHY

## Slide 24
Co Channel Interference Rejection, DS
The ability of the modulation to tolerate other networks in the area was tested. The results are S/J in dB that causes 5% PER
This indicates that the worst case Jammer for 11 MBps is the 1 MBps waveform that spoofs the preamble.
Notes: The ability of the signal to take jamming by a like signal will impact the ability to collocate nets. This set of data shows how the system will tolerate other DS signals of the various rates.
From the data we can see that the 1 Mbps radio is little effected by the higher rates since they are non correlating. On the other hand, the 1 Mbps radio jams the preamble of all the higher rates better than any other.

## Slide 25
S/J where CW jammer gives 10% PER
Data shows that the performance is virtually identical with FSK and CW Jamming
The 20% discard
point is 10.3 dB
Note: channel 1
data is better

## Slide 26
Other Interference Immunity tests, WB Noise Jamming Margin
Note: Processing Gain is measured at the 1.0e-5 BER point
S/J is measured in spread rate bandwidth
PG. = 16.6 + 2 - S/J = 10.9dB

## Slide 27
Other Interference Immunity tests, FH

## Slide 28
Other Interference Immunity tests, FH

## Slide 29
Total Number of Channels in the ISM band
We propose the existing DS channelization scheme.
Three non overlapping channels in the band
A choice of 5 MHz channel centers with 13 channels available. The highest two are not currently used by the existing standard in the US.

## Slide 30
Aggregate Throughput
The 3 non overlapping channels at 11 Mbps will allow 33 MHz total maximum achievable throughput in the ISM band.

## Slide 31
Phase Noise Sensitivity
There is no particular phase noise sensitivity with the proposed waveform. It performs as well in phase noise as any QPSK scheme.
The measured phase noise of our receiver’s LO which performs well is 2 degrees RMS

## Slide 32
RF PA Backoff
The QMBOK waveform needs about 5 dB of PA backoff to insure low regrowth of spectral sidebands.
This is the same as the DS BPSK preamble requires

## Slide 33
DC power consumption
The current, non equalized HFA 3860 QMBOK chip draws 30 mA at 3 VDC.
This represents about 12% of the radio receive power.
The equalizer will probably draw more than this.

## Slide 34
Patent Submissions
The Harris position is that we will only patent techniques having to do with our implementation
Anything likely to be embodied in the standard will be free of license from Harris
The QMBOK waveform is public domain

## Slide 35
Interoperability / Co-existence strategy with current low rate PHYs
Interoperable via use of existing low rate preamble and header, either DS or FH
  In the case of the FH PHY, the low rate preamble and header must be followed by a short high rate header to re-establish antenna diversity and to train the equalizer
Will defer or cause deferral via 802.11 mechanisms currently in place.
Notes: While we originally only suggested a DS low rate interoperability, Symbol has suggested low rate FH techniques.

## Slide 36
Is the proposal Interoperable at the data level?
Yes

## Slide 37
Is the proposal Interoperable at the antenna level?
Yes, the use of the existing preamble and header insures interoperability

## Slide 38
Performance penalty due to Interoperability / Coexistence.
The DS overhead is 192 us Vs about 50 us without interoperability
The FH overhead is 128 + 10 + 50 us or about the same
This amounts to ~20 % on 1K byte packet

## Slide 39
Performance penalty due to Interoperability / Coexistence.
Notes: It is desirable to use long packets to minimize the impact of the long preambles. Users concerned with maximizing throughput will also avoid the RTS/CTS/ACK protocol options.