| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | FMDID assignment using DREG RSP |
| Date Submitted | 2011-09-09 |
| Source(s) | Anil Agiwal, Hyunjeong Kang, Rakesh Taori Samsung Electronics | E-mail: anilag@samsung.com, hyunjeong.kang@samsung.com |
| Re: | Call for Comments on the 802.16p Amendment Working Document , IEEE 802.16p-11/0022 |
| Abstract | This contribution proposes modification to DREG RSP message to assign FMDID |
| Purpose | To be discussed and adopted in IEEE 802.16p-11/0022r1 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

FMDID assignment using DREG RSP

Anil Agiwal, Hyunjeong Kang, Rakesh Taori

Samsung Electronics

# Introduction

The section 6.2.1.3.2 in AWD [1] defines Fixed M2M deregistration ID (FMDID). There is no description on how this FMDID is assigned to M2M device.

Modifications to AAI-DREG-RSP message to assign the FMDID are proposed in this contribution.

# Proposed text with change marks

6.2.3.22 AAI-DREG-RSP message

Table 705—AAI-DREG-RSP message format

Page 12, lines 45-49

| Deregistration ID | 18 | Used to indicate Deregistration ID used to identify the AMS in idle mode 0..218-1 | Present when the S-SFH Network Configuration bit == 0b0 and if the Localized_Idle_Mode_Accepted flag is set to 0 |
| --- | --- | --- | --- |
| Fixed M2M Deregistration ID (FMDID) | 16 | Used to indicate Fixed M2M Deregistration ID used to identify the fixed M2M device in idle mode 0..216-1 | Only present if the Localized_Idle_Mode_Accepted flag is set to 1. |

Page 14, lines 49-53

| Deregistration ID | 18 | Used to indicate Deregistration ID used to identify the AMS in idle mode 0..218-1 | Present when the S-SFH Network Configuration bit == 0b0 and if the Localized_Idle_Mode_Accepted flag is set to 0 |
| --- | --- | --- | --- |
| Fixed M2M Deregistration ID (FMDID) | 16 | Used to indicate Fixed M2M Deregistration ID used to identify the fixed M2M device in idle mode 0..216-1 | Only present if the Localized_Idle_Mode_Accepted flag is set to 1. |

# References

[1] 80216p-11_0022: Enhancements to Support Machine-to-Machine Applications