| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Access Messages for Direct Signaling in the AAS Relay Zone. |
| Date Submitted | 2007-09-19 |
| Source(s) | Dale Branlund, Matt Volpe, Will Sun BRN Phoenix Inc. 2500 Augustine Drive Santa Clara, CA, USA 95054 John Norin, Robert Popoli The DIRECTV Group, Inc. 2250 East Imperial Hwy El Segundo, CA 90245 | Voice: +1-408-572-9703 Fax: +1-408-351-4911 dbranlund@brnphoenix.com Voice: +1-310-964-0717 Fax: +1-310-535-5422 john.norin@directv.com |
| Re: | Working Group Letter Ballot #28, Technical Comments and Contributions regarding IEEE Project P802.16j; Draft Amendment P802.16/D1. |
| Abstract | This contribution describes the Direct Signaling messages transmitted in the access channel of the AAS Relay Zone to accomplish ranging and bandwidth request and grant. |
| Purpose | This document provides the necessary access messaging to properly accomplish ranging and bandwidth request/grant within the AAS Relay Zone for Direct Signaling mode of operation. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

# Access Messages for Direct Signaling in the AAS Relay Zone

# Dale Branlund, Will Sun, Matt Volpe, BRN Phoenix, Santa Clara, CA, USA;
John Norin, Robert Popoli, The DIRECTV Group, Inc., El Segundo, CA, USA

This document describes the access channel messages used within the AAS Relay Zone. These messages support ranging, frequency, power adjustment, code assignment in Direct Signaling mode of operation.  These control messages enable edge-of-cell RS nodes to complete ranging and initial bandwidth request/grant using the beamformed access channel.

## Background

Section 8.4.4.7.2.3 of Draft Amendment P802.16j/D1 describes the AAS Relay Zone access channel but does not full define the access messaging required for managing channel descriptor request, initial bandwidth request/grant, codeword assignment, range/frequency/power adjustment.

## Proposed Solution

The proposed solution is to describe this mechanism and to define the access messages needed for proper operation.

## Detailed Solution

The RLP is an access channel message used to request bandwidth for ranging or transport.  It is used to request either the compact or full channel descriptor as signaled in the RLP type field.(subclause 8.4.4.7.2.3.3).  The RLP Type field signals the purpose of the message.

The following table defines the AAS_RLP Message structure:

.

| RLP Component | Bits | Reps | Slot | Comment |
| --- | --- | --- | --- | --- |
| AAS_RLP Message { |  |  |  |  |
| CID | 16 | 1 |  | Transport CID |
| Queue Depth | 2 | 1 |  | Sized for 4 levels |
| RLP Type | 4 | 1 |  | value 0=Transport BW Request 1=Ranging BW Request 2=Compact Chan Description Req 3=Full Chan Description Req |
| Reserve | 18 | 1 |  | Reserved for Future use |
| CRC | 8 | 1 |  | CRC-8 |
| } |  |  |  |  |
| Total RLP Bits | 48 |  | 1 |  |

The FLP access channel message provides code word assignments during initial ranging and provides bandwidth grant, codeword assignment, supportable MCS for the uplink and downlink, and range time/frequency/power adjustment during message exchange.

The following table defines the AAS_FLP Message structure:

| FLP Component | Bits | Reps | Slot | Comment |
| --- | --- | --- | --- | --- |
| AAS_FLP Message { |  |  |  |  |
| AMC band bitmask | 12 | 1 |  |  |
| UL PwrCtl, | 48 | 1 |  | 2 bits per slot |
| DL MCS level | 3 | 1 |  |  |
| UL MCS | 3 | 1 |  |  |
| UL Range Error | 2 | 1 |  |  |
| UL Frequency Error | 2 | 1 |  |  |
| UL Access PwrCtrl, | 2 | 1 |  |  |
| Assigned Codeword Index | 16 | 1 |  |  |
| Reserve | 0 | 1 |  |  |
| CRC | 8 | 1 |  |  |
| } |  |  |  |  |
| Total FLP Bits | 96 |  | 2 |  |

## Proposed Text Changes

Insert the following subclause:

8.4.4.7.2.3.4 AAS Relay Zone Access Channel Messaging

8.4.4.7.2.3.4.1 Reverse Link Payload Message

The RLP access channel message is used to request bandwidth for ranging or transport.  It is used to request either the compact or full channel descriptor as signaled in the RLP type field.  (subclause 8.4.4.7.2.3.3).  The RLP Type field signals the purpose of the message.

| Syntax | Size | Notes |
| --- | --- | --- |
| AAS_RLP() { |  |  |
| RLP Type | 4 bits | 0x0 = Transport Bandwidth Request 0x1 = Ranging Bandwidth Request 0x2 = Compact Channel Description Request 0x3 = Full Channel Description Request 0x4-0xF = Reserved |
| CID | 16 bits | Transport CID |
| Qdepth | 2 bits | Qdepth level 0b00 = level1 0b01 = level2 0b10 = level3 0b11 = level4 |
| Reserved | 18 bits | Shall be set to zero |
| CRC | 8 bits | CRC-8 |
| } |  |  |

#### RLP Type

The pupose for which the asynchronous access is being requested, including:

0x0 = Transport Bandwidth Request

0x1 = Ranging Bandwidth Request

0x2 = Compact Channel Description Request as described in section 8.4.4.7.2.3.3

0x3 = Full Channel Description Request as described in section 8.4.4.7.2.3.3

### CID

Transport CID for which a bandwidth request is being made

#### Qdepth

Qdepth level of the transport CID that is requesting bandwidth. Four levels can be described.

#### CRC

CRC-8 covers the whole slot

8.4.4.7.2.3.4.2 Forward Link Payload Message

The FLP access channel message provides code word assignments during initial ranging and provides bandwidth grant, MCS selection for UL/DL, and time/frequency/power adjustment during ranging.

| Syntax | Size | Notes |
| --- | --- | --- |
| AAS_FLP() { |  |  |
| AMC band bitmask | 12 bits |  |
| UL Partition Power Adjust | 48 bits | 2 bits encoded adjustment per described slot |
| DIUC | 3 bits |  |
| UIUC | 3 bits |  |
| UL Range Adjust | 2 bits | Encoded step adjustments |
| UL Frequency Adjust | 2 bits | Encoded step adjustments |
| UL Access Power Adjust | 2 bits | Encoded step adjustments |
| Assigned Codeword Index | 16 bits | Defines ACW |
| Reserved | 0 bits | Shall be set to zero |
| CRC | 8 bits | CRC-8 |
| } |  |  |

#### AMC band bitmask

#### UL Power Adjust

Power adjustment for the bearer partitions (up to 6 described in the partition grant control)

### DIUC

### DIUC

### UIUC

UIUC

#### UL Range Adjust

Range Adjustment.

#### UL Access Power Adjust

Power adjustment for the access channel

#### Assigned Codeword Index

#### Assigned ACW index

#### CRC

CRC-8 covers the whole slot