| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposal for DL OL SU-MIMO Transmit Diversity Scheme of Rate 3 |
| Date Submitted | 2008-09-05 |
| Source(s) | Yinggang Du, Hongjie Si, Yin Wei Zhao, Xin Chang, Yang Tang Huawei Takaaki KISHIGAMI, Isamu YOSHII Matsushita Electric (Panasonic) Huiying Fang ZTE Ying Du CATR Jianhua Liu Alcatel-Shanghai Bell | Email: duyinggang@huawei.com + 81-50-3687-6390 kishigami.takaaki@jp.panasonic.com yoshii.isamu@jp.panasonic.com huiying.fang@zte.com.cn duying@mail.ritt.com.cn Jianhua.Liu@alcatel-sbell.com.cn |
| Re: | IEEE 802.16m-08/033 “Call for Contributions and Comments on Project 802.16m System Description Document (SDD)” Target topic: “PHY : MIMO, Call for Detailed Physical Layer Comments” |
| Abstract | This contribution proposes DL OL SU-MIMO schemes |
| Purpose | To develop harmonized SDD text for 802.16m on DL OL SU-MIMO schemes |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposal for DL OL SU-MIMO Transmit Diversity Scheme of Rate 3

Yinggang Du, Hongjie Si, Yinwei Zhao, Xin Chang, Yang Tang

Huawei

Takaaki KISHIGAMI, Isamu YOSHII, Katsuhiko HIRAMATSU

Matsushita Electric (Panasonic)

Huiing Fang

ZTE

Ying Du

CATR

Jianhua Liu

Alcatel-Shanghai Bell

# 1. Introduction

This contribution is to propose DL OL SU-MIMO scheme in response to C802.16m MIMO-08/005r1.  We propose a 4Tx/8Tx antennas rate 3 scheme to be included in the MIMO SDD RG document.

2. Multiplexing scheme with 4 TX antennas and rate 3

# Text Proposal modification to SDD

------------------------------------Begin text proposal------------------------------------

(L19, P68 of 003r4)

# Open-loop SU-MIMO

| NT | Rate | M | NF |
| --- | --- | --- | --- |
| 2 | 1 | 1 | 1 |
| 2 | 1 | 2 | 2 |
| 4 | 1 | 1 | 1 |
| 4 | 1 | 2 | 2 |
| 8 | 1 | 1 | 1 |
| 8 | 1 | 2 | 2 |
| 2 | 2 | 2 | 1 |
| 4 | 2 | 2 | 1 |
| 8 | 2 | 2 | 1 |
| 4 | 3 | 12 | 4 |
| 8 | 3 | 12 | 4 |
| 4 | 4 | 4 | 1 |
| 8 | 4 | 4 | 1 |

Table 5 Matrix dimensions for open-loop SU-MIMO modes

(L8, P70)

# Spatial Multiplexing

The following spatial multiplexing modes are supported for open-loop single-user MIMO:

- Rate-3 spatial multiplexing modes:

  - 4Tx rate-3: rate 3 hybrid STBC and SM

  - 8Tx rate-3: rate 3 hybrid STBC and SM

[Delete the content from L1 to L17 in P71 and Insert the following text in the section 11.8.2.1.1.2 of 80216m-08_003r4.]

For 4Tx antennas rate 3 mode, the input to the MIMO encoder is represented as a 12 ( 1 vector

The output of the MIMO encoder is a 4 ( 4 matrix

Where the number of codeword can be upto 2, i.e., symbol s1 through s6 can belong to one codeword while s7 through s12 belong to another codeword. The output of the precoder is a 4 ( 4 matrix

,

where W is a 4 ( 4 unitary precoder and D is a 4 ( 4 identity matrix ().

When using Antenna Hopping,  is a set of 3 antenna circulation matrices, i.e.,

.

can be changed every pair of tones or symbols.

For 8Tx antennas rate 3 mode, the input to the MIMO encoder is represented as a 12 ( 1 vector

The output of the MIMO encoder is a 4 ( 4 matrix

Where the number of codeword can be upto 2, i.e., symbol s1 through s6 can belong to one codeword while s7 through s12 belong to another codeword. The output of the precoder is a 4 ( 4 matrix

,

where D is a 4 ( 4 identity matrix () and W is defined as follows:

.

is a 8x4 matrix which is implementation specific,  is a 4 ( 4 unitary precoder.

When using Antenna Hopping,  is a set of 3 antenna circulation matrices, i.e.,

.

can be changed every pair of tones or symbols.

------------------------------------End text proposal------------------------------------