| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Synchronous non-adaptive Hybrid ARQ for distributed subcarrier mode |
| Date Submitted | 2008-05-05 |
| Source(s) | Alexei Davydov, Alexander Maltsev Intel Russia, Nizhny Novgorod, Ul. Turgeneva, 30 | E-mail: alexei.davydov@intel.com, alexander.maltsev@intel.com Voice: +7 831 4162444 |
| Re: | IEEE 802.16m-08/016r1 Call for Contributions on Project 802.16m System Description Document (SDD) Topic: Hybrid ARQ (protocol and timing) |
| Abstract | This contribution proposes synchronous non-adaptive HARQ for IEEE 802.16m operating in distributed subcarrier mode |
| Purpose | For discussion and adoption by IEEE 802.16m group |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Synchronous non-adaptive Hybrid ARQ for distributed subcarrier mode

Alexei Davydov, Alexander Maltsev

Intel Corporation

# Introduction

Hybrid Automatic Repeat Request (HARQ) is an effective mean to improve robustness of the system to link adaptation errors caused by channel estimation errors, channel quality information feedback delay, user mobility, etc. When a received packet is found to be in error through the use of Cyclic Redundancy Check (CRC), a retransmission request (or Negative Acknowledgment - NACK) will be sent to the transmitter. The transmitter will then retransmit the same packet or it’s portion until the initial packet is successfully decoded at the receiver or a maximum retransmission limit is reached. The difference with conventional ARQ protocol is that erroneous packets are not discarded by the receiver but stored in a buffer for the following joint demodulation with the next retransmission(s).

# Background

In terms of the retransmission scheduling the HARQ protocols are usually classified in to two groups:

- Synchronous HARQ (S-HARQ)

- Asynchronous HARQ  (A-HARQ)

In the synchronous mode, the retransmissions have to occur at a pre-determined time-frequency instances. Figure 1 shows the example of retransmission allocation in case of S-HARQ. In general, the fact that retransmissions can occur only at a fixed time-frequency instances reduces some flexibility, such as possibility to postpone the retransmission or possibility to use the channel information for more effective allocation of the retransmissions. At the same time S-HARQ provides several benefits over A-HARQ such as reduction of control signalling overhead (the resource allocation control information for the retransmission does not require retransmission and assumed to be the same as in the original transmission).

# Problem Statement

As it was mentioned above for conventional S-HARQ protocol the retransmission does not change from frame to frame and occurs at the same time-frequency allocation as the initial transmission. That means that for applications that require short latencies (comparing to channel coherence time) the channel is almost static across retransmissions. In this case the expected post-processing Signal-to-Noise Ration (SNR) improvement due to retransmission is about 3dB for Chase Combining and provided by time diversity and coherent combining only.

There are a number of applications (e.g. VoIP) where signaling overhead should be carefully managed and kept at low level.  For such applications distributed subcarrier mode will be used as a more efficient for data transmission in terms of lower signaling overhead. In such mode the frequency diversity (additionally to time diversity) may be provided for the each next retransmission thus giving additional efficiency and robustness for the S-HARQ in distributed subcarrier mode.

# Proposed solution

In this section we describe a method for improvement of the efficiency of the conventional S-HARQ for distributed subcarrier mode by means of providing frequency and spatial diversity to the each next retransmission while keeping overhead almost at the same level.

To exploit frequency diversity it is proposed to apply additional predetermined sub channel offset to the original data burst allocation. In this case the fading experienced by specific subcarrier in data burst will change due to change in the burst position (see Figure 2). The new parameter that defines the additional sub channel offset (S-HARQ sub channel offset) may be signalled in control channel during original transmission or specified as a fixed parameter in the system description.

In case of vertical or diagonal MIMO mode the additional robustness for S-HARQ retransmissions may be guaranteed by exploiting the spatial diversity (additionally or separately to the frequency diversity). The spatial streams of the each retransmission may be cyclically rotated. The cyclic rotation of spatial signals ,,…, over spatial streams is illustrated below with rotation offset equal to one for each new retransmission:

.

# Comparative study

To demonstrate the efficiency of the proposed solution a link layer performance analysis for the aforementioned techniques has been performed. The system parameters used in the simulations are summarized in Table 1 [1].

Table 1. Link layer simulation parameters

| Parameter | Value | Notes |
| --- | --- | --- |
| FFT Size | 1024 |  |
| Bandwidth | 10 | MHz |
| Permutation | DL PUSC | Distributed |
| Antenna setting | 1x1/2x2 | 2x2 SM, MMSE |
| TX/RX Ant. Corr. | 0.5/0.5 |  |
| Mobile speed | 3 | km/h |
| Retransmission delay | 10 | ms |
| HARQ | Synchronous | Chase Combining |
| Packet Length | 44 bytes | VoIP active state |

In Figure 3 the generic Packet Error Rate (PER) versus Signal-to-Noise Ratio (SNR) reference curves are shown for the initial transmission for all modulation coding schemes (MCS) in the distributed subcarrier mode. The similar graphs with residual PER performance versus SNR are shown in Figure 4 for the conventional S-HARQ method after first retransmission. It can be seen from the figures that the first packet retransmission and Chase Combining provides about 4dB SNR improvement (3dB coherent combining, 1dB time diversity) comparing to the performance of the initial transmission. Figure 5 demonstrates the efficiency of the proposed S-HARQ with predetermined sub channel rotation in the same scenario. It can be seen that simple predetermined sub channel rotation scheme that require low overhead provides 1-2dB improvement over conventional S-HARQ.

A similar comparison has been conducted for 2x2 vertical STC-B mode. Figure 6 shows the reference PER performance versus SNR for the first 2x2 MIMO transmission. The performance of the conventional S-HARQ and proposed S-HARQ for MIMO systems (with predetermined spatial stream rotation, but without sub channel rotation) are presented in figure 7 and 8 respectively. It can be seen that spatial stream rotation provides 1-2 dB improvement over simple packet retransmission in MIMO mode.

# Text proposal

If synchronous HARQ mode will be adopted as a mandatory mode, insert the following text into SDD Section 10 – Media Access Control Sub-Layer [2]

-------------------------------  Text Start  ---------------------------------------------------

# 10.x Data/Control Plane

# 10.x.x HARQ principles

The HARQ within the MAC sub layer is a synchronous N-channel Stop-And-Wait process with the following characteristics:

- Downlink mode

- default synchronous non-adaptive HARQ

- predetermined data burst rotation for distributed subcarrier mode

- predetermined spatial stream rotation for vertical MIMO

- fixed data burst location for localized subcarrier mode

- Uplink mode

- default synchronous non-adaptive HARQ

- predetermined data burst rotation for distributed subcarrier mode

- predetermined spatial stream rotation for vertical MIMO

- fixed data burst location for localized subcarrier mode

-------------------------------  Text End  ---------------------------------------------------

Insert the following text into SDD Section 10 – Media Access Control Sub-Layer [2]

-------------------------------  Text Start  ---------------------------------------------------

# 10.x Data/Control Plane

# 10.x.x Downlink scheduling

# 10.x.x.x Persistent allocation

The BS may use data bursts rotation within DL persistent allocation region to improve efficiency of HARQ retransmission. In addition in case of vertical spatial multiplexing transmission spatial stream rotation may be used for further improvement. A predetermined data burst rotation offset and spatial stream rotation indicator will be signaled via L1/L2 control channel(s).

# 10.x.y Uplink scheduling

# 10.x.y.x Persistent allocation

The BS may use data bursts rotation within UL persistent allocation region to improve efficiency of HARQ retransmission. In addition in case of vertical spatial multiplexing transmission spatial stream rotation may be used for further improvement. A predetermined data burst rotation offset and spatial stream rotation indicator will be signaled via L1/L2 control channel(s).

-------------------------------  Text End  ---------------------------------------------------

# References

[1] IEEE 802.16m-008/004, “802.16m Evaluation Methodology”

[2] IEEE 802.16m-08/003, “The Draft IEEE 802.16m System Description Document”

Figure 1. Conventional S-HARQ retransmission data resource allocation in time-frequency domain

Figure 2.  Proposed S-HARQ retransmission data resource allocation in time-frequency domain

Figure 3. PER versus SNR for the initial transmission (reference curves)

Figure 4. Residual PER versus SNR after the 1st retransmission for the conventional S-HARQ

Figure 5. Residual PER versus SNR after the 1st retransmission for the proposed S-HARQ

Figure 6. PER versus SNR for the initial vertical MIMO transmission (reference curves)

Figure 7. Residual PER versus SNR after the 1st retransmission for the conventional MIMO S-HARQ

Figure 8. Residual PER versus SNR after the 1st retransmission for the proposed MIMO S-HARQ