| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Handover Enhancements |
| Date Submitted | 2009-02-27 |
| Source(s) | Stavros Tzavidas Motorola | stavros.tzavidas@motorola.com |
| Re: | Change Request on Project 802.16m SDD (IEEE C802.16-08/003r7) TGm SDD: Other (contributions in support of a comment) – MAC |
| Abstract | This contribution proposes corrections to the Handover section of the SDD in order to correctly incorporate the changes introduced by contribution IEEE C802.16m-09/185 as accepted in the previous IEEE meeting (section #59) |
| Purpose | For discussion and adoption by TGm |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Handover Enhancements

Stavros Tzavidas

Motorola

# Introduction

Contribution IEEE C802.16m-09/185 was accepted in session #59 but the proposed edits were incorrectly adopted in the latest SDD version (08/003r7).

More specifically, contribution IEEE C802.16m-09/185 proposes to include in Figure 16 an "HO Indication" message that is sent after the "HO Command" message. However, Figure 16 in the latest SDD draft shows the "HO Indication" message as sent before the "HO Command" message.

HO indication should come after HO command, as per contribution IEEE C802.16m-09/185 which was accepted in the previous session (session #59). This contribution aims to correct this.

# Text Proposal

Replace Figure 16 on page 40 of IEEE C802.16m-08/003r7 with the following figure:

Figure 16 A general call flow for HO