| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed text for wideband CQI feedback in IEEE802.16m Amendment |
| Date Submitted | 2009-04-27 |
| Source(s) | Takaaki KISHIGAMI, Isamu YOSHII Panasonic Corporation | Voice: + 81-46-840-5123 E-mail: kishigami.takaaki@jp.panasonic.com yoshii.isamu@jp.panasonic.com |
| Re: | Category: AWD comments / Area: Chapter 15.3.7 (DL-MIMO) “Comments on AWD 15.3.7.2.6.1 Downlink post-processing CINR measurement feedback” |
| Abstract | We propose the wideband CQI information. |
| Purpose | For 802.16m discussion and adoption |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed text for wideband CQI feedback in IEEE802.16m Amendment

Takaaki KISHIGAMI, Isamu YOSHII

Panasonic Corporation

# Introduction

Current AWD text[1] for the wideband CQI is defined as ‘one average CQI over the whole band’ . Moreover, in 16m system, Fractional frequency reuse (FFR) can be used to reduce inter-cell interferences.

So, the definition of the wideband CQI should be more clarified to adapt to the case that the whole band is frequency-partitioned .

In contribution, we propose the wideband CQI feedback contents considering the frequency partitioning.

# Proposed Text

We propose the following text for the IEEE802.16m Amendment Working Document in Section 15.3.7.2.6.1.

-------------------------------  Start text proposal  ---------------------------------------------------

### 15.3.7.2.6 Feedback mechanisms and operation

### 15.3.7.2.6.1 Downlink post-processing CINR measurement feedback

The reported channel quality indicator has two types: wideband CQI, subband CQI.

The wideband CQI is one average CQI over the whole band as shown in Table x.

Table x – Feedback type and feedback contents

| Feedback information type | Feedback contents (Number of bits) | Description |
| --- | --- | --- |
| Wideband CQI (Effective CINR) | DL average Effective CINR (5 bits) | one average CQI i) over the whole band or ii) over the frequency partitioned band when frequency partitioning is used. |
| Wideband CQI (Physical CINR) | Physical CINR Mean (8 bits) + Physical CINR Standard Deviation (8 bits) (cf. values and coding are defined in 8.4.12.3 [2]). | Physical CINR Mean i) over the whole band or ii) over the frequency partitioned band when frequency partitioning is used. |

The subband CQI is one average CQI over the subband.

For MU-MIMO feedback modes, the CQI is calculated at the MS assuming that the interfering users are scheduled by the serving BS using rank-1 precoders orthogonal to each other and orthogonal to the rank-1 precoder represented by the reported PMI.

-------------------------------  End text proposal  ---------------------------------------------------

# References

[1]IEEE 802.16m-09/0010r1a, “802.16m Amendment Working Document (AWD)”

[2]IEEE Std 802.16 Rev2/D8