| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Performance evaluation of 8Tx codebooks |
| Date Submitted | 2009-05-03 |
| Source(s) | Bruno Clerckx, David Mazzarese, Heewon Kang, Hokyu Choi Samsung Electronics | bruno.clerckx@samsung.com d.mazzarese@samsung.com |
| Re: | Category: AWD comments / Area: Chapter 15.3.7 (DL-MIMO) “Comments on AWD 15.3.7 DL-MIMO” |
| Abstract | The contribution evaluates performance of various 8Tx codebooks |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Performance evaluation of 8Tx codebooks

Bruno Clerckx et al.

Samsung Electronics

# Introduction

Some contributions raised some issues regarding the 8Tx codebook currently accepted in the AWD. Contribution C80216m-09_0941 proposes a new 6-bit codebook for 8Tx. Contribution C80216m-09_0924 claims that a 8Tx codebook previously submitted in the contribution C80216m-09_038r1 outperforms the current AWD codebook. We evaluate the performance of the 6bits codebook of C80216m-09_0924 and the 4bits codebook of C80216m-09_038r1 and compare with performance of current AWD codebook.

# CL SU MIMO

# Figures 1 to 3 evaluates performance of C80216m-09_0924 and AWD codebooks in uncorrelated, correlated and dual-polarized channels. As we can see from those figures, the 6bit codebook proposed in C80216m-09_0924 doesn’t provide any significant gain over the current AWD 4bit codebook. However its complexity in codebook search is significantly larger than the 4bit AWD codebook.

# Figure 1. Performance of C80216m-09_0924 6bits (red) and AWD 4bits (blue) codebooks in 8x2 CL SU MIMO over uncorrelated (4 lambda spacing and 15 degrees angle spread) channels

# Figure 2. Performance of C80216m-09_0924 6bits (red) and AWD 4bits (blue) codebooks in 8x2 CL SU MIMO over correlated (0.5 lambda spacing and 3 degrees angle spread) channels

# Figure 3. Performance of C80216m-09_0924 6bits (red) and AWD 4bits (blue) codebooks in 8x2 CL SU MIMO over correlated (0.5 lambda spacing and 3 degrees angle spread) dual-polarized 45-VH (8dB XPD) channels

# CL MU MIMO

# Figures 4 and 5 evaluates the performance of C80216m-09_038r1 and AWD codebook in correlated channels (0.5 and 0.7 lambda spacing) in 8x2 CL MU-MIMO transmissions with maximum 4 scheduled users. Those simulations confirm that the current AWD 4bit codebook provides significant gain over C80216m-09_038r1 in MU-MIMO.

# Figure 4. Performance of C80216m-09_038r1 4bits (red) and AWD 4bits (blue) codebooks in 8x2 CL MU MIMO over correlated (0.5 lambda spacing and 3 degrees angle spread) channels

# Figure 5. Performance of C80216m-09_038r1 4bits (red) and AWD 4bits (blue) codebooks in 8x2 CL MU MIMO over correlated (0.7 lambda spacing and 3 degrees angle spread) channels

# Conclusions

# The AWD codebook has been shown to provide the best performance. Hence the AWD 8Tx codebook shouldn’t be changed.

# Appendix: Simulation Assumptions

- Channel model: Pedestrian B channel model, 3km/h, linear array

  - Uncorrelated: AS= 15, d/λ=4

  - Correlated: AS= 3, d/λ=0.5 and d/λ=0.7

  - Dual-pol: 45->VH with 8dB XPD

- 10 MHz

- 10 active users

- HARQ (Chase Combining, non-adaptive) with 3 retransmissions

  - Delay first transmission: 8 subframes

  - Delay between re-transmissions: 1 frame (8 subframes)

- CQI, PMI feedback period: every frame (5 ms)

- Link Adaptation (PHY abstraction): QPSK 1/2 with repetition 1/2/4/6, QPSK 3/4, 16QAM 1/2, 16QAM 3/4, 64QAM 1/2, 64QAM 2/3, 64QAM 3/4, 64QAM 5/6

- Ideal channel estimation

- MMSE receiver

- No CQI transmission errors

- ZFBF and SCW CL SU MIMO with rank adaptation

- LLRU (4 PRUs)

- Ideal antenna calibration

- No constraint on PAPR