| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | SN usage in FPEH,FEH and MEH |
| Date Submitted | 2009-07-06 |
| Source(s) | Anil Agiwal, Youngbin Chang, Rakesh Taori, Jungje Son Samsung Electronics | anilag@samsung.com, yb.chang@samsung.com *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | “802.16m amendment working document”: IEEE 802.16m-09/00028r1, “Call for comments on Project 802.16m Amendment Working Document (AWD) IEEE 802.16m-09/00010r2” |
| Abstract | This contribution proposes text changes to modify FPEH/MEH to facilitate polling, ARQ feedback piggybacking and rearrangement to be included in the 802.16m amendment working document. |
| Purpose | To be discussed and adopted by TGm for 802.16m amendment working document. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

SN Usage in FPEH,MEH & FEH

Anil Agiwal, Youngbin Chang, Rakesh Taori, Jungje Son

Samsung Electronics

# Introduction

The description of the ‘SN field in the FPEH, FEH and MEH is not clear.

# Text Proposal for inclusion in the 802.16m amendment working document

---------------------------------------------------------Start of the Text----------------------------------------------------------

[Change 1 - Modify the text in Table 8 in sub clause 15.2.3.2.1, page: 13 as follows]

Table 8 FPEH Fields

| Name | Length (bit) | Description |
| --- | --- | --- |
| SN | 10 | SN is maintained per connection. For non ARQ connection, ‘SN’ represents the MAC PDU Payload Sequence Number and the ‘SN’ value increments by one (modulo 1024) for each MAC PDU. For ARQ connection, ‘SN’ represents the ARQ block sequence number (refer section 15.2.13 for details). |
| FC | 2 | Fragmentation Control bits (encoding shown in Table 9) |
| End | 1 | Indication of more information 0 = Indicating another “Length” and “End” fields are followed 1 = Indicating no more “Length” and “End” fields are followed |
| Length | 11 | This field indicates the length of SDU or SDU fragment. If a payload consists of ‘N’ SDU/SDU fragments, N-1 ‘Length’ fields are present in FPEH. The length of the first SDU or SDU fragment in the payload is indicated by the ‘Length’ field in GMH. |
| Reserved | Variable | Reserved bits are added at the end of FPEH for byte alignment |

[Change2 - Modify the text in Table 15 in sub clause 15.2.3.2.3, page:17, as follows]

Table 15 MEHB Fields

| Name | Length (bit) | Description |
| --- | --- | --- |
| M | 1 | Indication of more MEHB 0 = no more MEHB follows the current MEHB 1 = one or more MEHB follows the current MEHB |
| Flow ID | 4 | Flow ID of the SDU/SDUs fragment identified in the MEHB |
| SN | 10 | SN is maintained per connection. For non ARQ connection, ‘SN’ represents the Sequence number for the payload identified in the MEHB and the SN value increments by one (modulo 1024) for each payload of the connection in a MAC PDU. For ARQ connection, ‘SN’ represents the ARQ block sequence number (refer section 15.2.13 for details). |
| FC | 2 | Fragmentation Control bits (encoding shown in Table 9) |
| Length | 11 | Length of the correspondent SDU/SDU fragment |
| End | 1 | Indication of more information 0 = Indicating another “Length” and “End” fields are followed 1 = Indicating no more “Length” and “End” fields are followed |

[Change3 - Modify the text in Table 10 in sub clause 15.2.3.2.2, page:14, as follows]

Table 10 FEH Format

| Syntax | Size (bit) | Notes |
| --- | --- | --- |
| FEH () { | - |  |
| LAST | 1 | Always set to ‘1’ |
| Type | TBD | FEH type |
| SN | 8 | Type dependent content. Sequence number of the current management message fragment. The SN value increments by one (modulo 256) for each fragment, including unfragmented management message. |
| FC | 2 | Fragmentation control (see Table 9) |
| } | - |  |

---------------------------------------------------------End of the Text----------------------------------------------------------

# Reference

[1] IEEE 802.16m-09/0010r2, “802.16m Amendment Working Document (AWD)”