| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Location update rules |
| Date Submitted | 2009-07-06 |
| Source(s) | Stavros Tzavidas Motorola | stavros.tzavidas@motorola.com |
| Re: | 802.16m amendment working document |
| Abstract | This contribution proposes enhancements to the location update rules in the AWD. |
| Purpose | For review and adoption |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Location Update Rules

Stavros Tzavidas

Motorola

# Introduction

According to the current AWD text, when the AMS leaves its primary paging group it starts a timer and performs a location update after this timer expires.

The benefits of this timer are unclear. It is sufficient to specify that the AMS shall perform a location update when it no longer sees any of the paging groups it has been assigned.

# Text Proposal

----------------------------------------------Start of the text proposal ------------------------------------------------------

Modify section 15.2.17.4.1.1 “Paging group based update” as follows:

15.2.17.4.1.1 Paging group based update

An AMS shall perform Location Update process when an AMS detects a change in the paging groups. The AMS shall detect the change of the paging groups by monitoring the PG IDs, which are transmitted by the preferred ABS during the paging listening interval. If none of the PG ID(s), to which the AMS belongs, is detected, the AMS shall determine that the paging group(s) has changed.

ABSs and Idle Mode AMSs may belong to multiple paging groups. In case an AMS belongs to multiple paging groups, it starts Paging Group Location Update Timer (PG_LU_TIMER) when it leaves primary paging group. An AMS performs the paging group location update when it can no longer detect any of the paging groups to which it belongsafter PG_LU_TIMER and may inform its mobility (slow, medium, fast) to ABS. Based on the AMS mobility information, the ABS may assign new paging group(s) of different size(s) to AMS.

If the AMS returns to the primary paging group before the expiration of PG_LU_TIMER, it releases the timer and does not perform location update.

-------------------------------------------------- End of the text proposal --------------------------------------------------