| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Changes/Refinements to Section 11.13 (Channel Coding and HARQ) of IEEE 802.16m SDD (802.16m-09/0034) |
| Date Submitted | 2009-08-21 |
| Source(s) | Sung-Eun Park, Chiwoo Lim, Jaeweon Cho, Hokyu Choi Samsung Electronics | se.park@samsung.com |
| Re: | Change Request on 802.16m SDD, IEEE 802.16m-09/0034 |
| Abstract | The contribution proposes text changes to the channel coding and HARQ section of the 802.16m SDD, IEEE 802.16m-09/0034 |
| Purpose | To be discussed and adopted by TGm for the 802.16m SDD |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

# Introduction

This contribution proposes text changes to the channel coding and HARQ section of the IEEE 802.16m SDD [1] where the system description requires additional detail. The proposed text is consistent with the 802.16m Draft Amendment [2]. The refined SDD document will be a necessary supplement in the submission of IEEE 802.16m technology description template to ITU-R/WP 5D later this year.

Comments have been inserted to identify the type of change (Editorial/Technical). For technical changes, Draft Amendment [2] text that has been added into the SDD has been identified by page, line and section number. Comments are visible with MS Word markup.

Proposed text has been underlined in blue and deleted text has been struck through in red. Existing SDD text is shown in black.

# References

[1] P802.16m System Description Document, 802.16m-09/0034, July 2009.

[2] IEEE P802.16m/D1, “Draft Amendment to IEEE Standard for Local and Metropolitan Area Networks- Part 16: Air Interface for Broadband Wireless Access Systems,” July 2009.

- - - - - - - - - - - - - - - - - - - - - - - - - - - Begin Proposed Text - - - - - - - - - - - - - - - - - - - - - - - -

## Channel coding and HARQ

### Channel coding

#### Block diagram

Figure 75 shows the channel coding and modulation procedures. The following sections provide more details on the coding and modulation procedures in IEEE 802.16m transmit chain.

Figure 75: Channel coding procedure

- - - - - - - - - - - - - - - - - - - - - - - - - - - End Proposed Text - - - - - - - - - - - - - - - - - - - - - - - - -

# Comments

Block diagram comes from Figure 487 in page 476, line 24 of draft amendment.