| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed E-MBS Zone Specific Pilot Patterns (E-MBS) |
| Date Submitted | 2009-08-28 |
| Source(s) | Jia-Hao Wu, Yu-Tao Hsieh, Pang-An Ting ITRI | Voice : 886-3-5914854 E-mail: yutaohsieh@gmail.com E-mail: jefferywu@itri.org.tw |
| Re: | Re: IEEE 802.16m-09/0037 Call for Contributions on Project 802.16m Amendment Content IEEE P802.16m/D1 E-MBS |
| Abstract | The contribution proposes the text and figures for E-MBS zone specific pilots. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed E-MBS Zone Specific Pilot Patterns

Jia-Hao Wu, Yu-Tao Hsieh, Pang-An Ting

ITRI

# Introduction

In current SDD [1], the basic concept about E-MBS zone specific pilot is described in 11.5.3.2. However, the E-MBS zone specific pilot patterns have not yet been defined. According to current EMD [3], MBSFN channel models for inter-site distance (ISD) 1.5km and 5km have much larger delay spread than ITU-R VA and PB channel. Therefore, we may need to increase pilot density to accommodate severe frequency selectivity. In this contribution, we propose the E-MBS zone specific pilot patterns and corresponding text for AWD [2].

# Proposed E-MBS Zone Specific Pilot Pattern

According to current SDD, the multicast broadcast single frequency network (MBSFN) is supported to enable macro-diversity transmission. Traffic can be transmitted through synchronous ABSs in the same EMBS zone. The AMSs in the served MBSFN zone would receive signal that comes from multiple BSs and the equivalent channel seen from the AMSs will be longer than that in the single-cell transmission. Consequently, it possesses severer frequency selectivity. The MBSFN channel model for ISD equals to 1.5 km and 5km have been defined in current EMD.

In order to facilitate satisfactory channel estimation accuracy in such a long delay spread channel, pilot density may be increased. We propose following E-MBS zone specific pilot patterns and compare it with other proposals by Monte Carlo link level simulation to justify its superiority.

Figure 1 shows the four E-MBS zone-specific pilot patterns in comparison. The pilot overhead of each pattern is different (SDD unicast, Samsung: 11.1%; ITRI: 16.67; Intel: 22.2%).

Table 1 outlines parameters used for conducting simulations. Note that since CP used in simulation is 11.43 us which is shorter than maximum delay spread of MBSFN channel with ISD equal to 5 km (i.e. 24.5 us), this results in inter-symbol interference (ISI) and inter-carrier interference (ICI). In the simulation, we did not assume any ISI or ICI mitigation schemes. In addition, we assume perfect knowledge of channel profile when designing interpolation coefficients of pilot-aided channel estimation.

Table 1. MBSFN pilot simulation parameters

| OFDM Parameters | FFT Size 1024; G = 1/8 (CP length = 11.43 us) Nominal BW = 10 MHz; Carrier frequency = 2.5 GHz |
| --- | --- |
| Channel model | MBSFN ISD = 1.5km/5 km Vehicular speed = 120 kmph |
| CE parameters | 2-D MMSE, Window size = 3PRU, 4-contiguous PRU is assumed SNR, Doppler, Delay spread are assumed known |
| Pilot Pattern | Intel, ITRI, Samsung and SDD 2-stream pilot pattern |
| Data Size | 4 PRU |
| Permutation | Tone-pair Logical DRU |
| MIMO mode | Rate-2 SM [2Tx,2Rx] and Rate-1 SFBC |
| MIMO Detector | Soft MMSE detector |
| MCS | QPSK ½ , 16QAM 1/2, 16QAM 2/3 64QAM 2/3 with LTE CTC |
| Pilot Boosting (over data power) | 5 dB |

Fig. 1 E-MBS zone specific pilot patterns in comparison

Fig. 2 shows the throughput results in MBSFN 1.5km channel cases. Since there is no ISI in this channel model, we could transmit with higher modulation coding order even in rank-2 spatial multiplexing MIMO scheme. ITRI’s pilot pattern has similar performance compared with Intel’s but has lower pilot overhead. In the high SNR region of each modulation coding order, SDD unicast and Samsung’s pilot patterns can support higher throughput due to low pilot overhead. However, ITRI and Intel’s pilot patterns outperform in the intermediate SNR region of each modulation coding order because their ability of acquiring more accurate channel information.

The throughput results in MBSFN 5km channel cases are shown in the figure 3. Since there is severe inter-symbol interference and inter-carrier interference in this large ISD channel, it may be difficult to support rank-2 spatial multiplexing transmission when transmitting high order modulation coding schemes (MCS). In the simulation, we adopt SFBC transmission to increase diversity gain in such a (relatively) low SINR regime. As mentioned before, no any ISI/ICI mitigation technique is applied. It is shown that ITRI and Intel’s higher density pilot patterns have noticeable performance gain compared with SDD unicast and Samsung’s low overhead pilot patterns.

For the case that only single pilot pattern is used in both small or large ISD MBSFN channel, we recommend to adopt ITRI’s zone-specific pilot pattern. For the case that BS can adapt pilot patterns to different inter-site distance in MBSFN, we suggest to use ITRI’s zone specific pilot pattern for large cell size.

Fig. 2 Link level throughput Comparison of E-MBS pilot pattern over ISD=1.5km, 2x2 SM

Fig. 3 Link level throughput Comparison of E-MBS pilot pattern over ISD=5km, 2x2 SFBC

# References

[1] IEEE 802.16m-08/003r9a, “IEEE 802.16m System Description Document.”

[2] IEEE 802.16m-08/0010r2, “IEEE 802.16m Amendment Working Document.”

[3] IEEE 802.16m-07/004r5, “IEEE 802.16m Evaluation Methodology Document.”

[4] IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment.”

# Text proposal for the 802.16m amendment

Insert the following text and figure in IEEE 802.16m/D1 in xxx on page XXX:

============================== Proposed text start ===================================

The E-MBS zone specific pilot pattern for small cell size (e.g. ISD = 1.5km) is the same as unicast pilot pattern shown in Fig. 454. For large cell size such as ISD = 5km, the E-MBS zone specific pilot pattern is shown in Fig. ZZZ.

Fig. ZZZ E-MBS zone specific pilot pattern for large cell size

============================== Proposed text end ===================================