| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text for the location of MIMO midamble (15.3.5.4.2) for the P802.16m/D1 |
| Date Submitted | 2009-08-29 |
| Source(s) | Jinyoung Chun, Jinsam Kwak, Bin-Chul Ihm LG Electronics | jychun03@lge.com |
| Re: | P802.16m/D1 : MIMO midamble (15.3.5.4.2) |
| Abstract | This contribution proposes the location of MIMO midamble. |
| Purpose | For member’s review and adoption into P802.16m/D2 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Text for the Location of MIMO Midamble for the P802.16m/D1

Jinyoung Chun, Jinsam Kwak, Bin-Chul Ihm

LG Electronics

# Introduction

# In current draft (D1), MIMO midamble shall be transmitted every frame on the second last DL subframe. But it’s only considered a few frame structures. We have to make general location of MIMO midamble.

# The problem

# If type-2 DL subframe exists, we can use it for MIMO midamble and the remaining 6 consecutive symbols form a type-2 subframe. If we fix the location of MIMO midamble on the second last DL subframe, we have to make type-1, 2, 3 in some configuration such as 8.75MHz channel bandwidth, etc.

# When the Advanced Air Interface frames support the WirelessMAN-OFDMA for 5, 10, 20MHz channel bandwidths, all subframes in the Advanced Air Interface DL Zone are type-1 subframes. Moreover if Advanced Air Interface DL zone is two subframes, the first frame includes Preamble and MIMO midamble can’t exists on the second subframes. Therefore in this case, MIMO midamble can be located in last subframe.

# Still, we can’t make MIMO midamble in 7MHz TDD with CP 1/8. That’s because all DL subframes form 5 symbol Type-3 subframe.

# Proposed text change

[Add the texts and figures marked in blue and remove the texts and figures marked in red in the P802.16m/D1.]

--------------------------------------  Text Start  --------------------------------------------

[Modify the text in line 54, page 282 (15.3.5.4.2 MIMO midamble) as below.]

15.3.5.4.2 MIMO midamble

MIMO midamble is used for PMI selection in closed loop MIMO. For OL MIMO, midamble can be used to calculate CQI. MIMO midamble shall be transmitted every frame on the second last DL subframe. on the last type-2 DL subframe. If type-2 DL subframe doesn’t exist, MIMO midamble is transmitted every frame on the last type-1 DL subframe. The midamble signal occupies the first OFDMA symbol in a DL type-1 or type-2 sub-frame. For the type-1 subframe case, the remaining 5 consecutive symbols form a type-3 subframe. For the type-2 subframe case, the remaining 6 consecutive symbols form a type-1 subframe.

-----------------------------------------  Text End  ------------------------------------------

# References

[1] Draft Amendment, P802.16m/D1, July 2009.