| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text for AAI_REG-REQ/RSP (15.2.3.6/15.2.3.7) for the IEEE 802.16m/D2 |
| Date Submitted | 2009-11-06 |
| Source(s) | Yuan Zhu, Hujun Yin, Xiangying Yang Intel Corporation | yuan.y.zhu@intel.com Hujun.yin@intel.com |
| Re: | Proposed text changes to P802.16m/D2 15.2.3.6/15.2.3.7 |
| Abstract |  |
| Purpose | To be discussed and adopted by TGm for the 802.16m D3 Draft. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed text for AAI_REG-REQ/RSP (15.2.3.6/15.2.3.7) for the IEEE 802.16m/D2

Yuan Zhu, Hujun Yin, Xiangying Yang

Intel Corporation

- Introduction

This contribution proposes to move “capability negotiation on interference mitigation” section from section 15.2.20.3 of P802.16m/D2 [1] to section 15.2.3.6 and section 15.2.3.7. The text change to delete section 15.2.20.3 is in [2].

# References

[1] Draft Amendment, P802.16m/D2, Oct 2009.

[2] IEEE C802.16m-09/2349 “Proposed Text for AAI_REG-REQ/RSP (15.2.3.6/15.2.3.7) for the IEEE 802.16m/D2”

--------------------------------Start of the text #1----------------------------------------

Add one new row in table 676 section 15.2.3.6 in page 41, line 54 below row Capability for MIMO support

| Capability for Interference mitigation | Bit 0: DL PMI Coordination Bit 1: DL Collaborative multi-BS MIMO Bit 2: DL Closed-Loop multi-BS Macro Diversity Bit 3: UL PMI Combination |
| --- | --- |

------------------------------- End of text # 1  -------------------------------------------

--------------------------------Start of the text #2----------------------------------------

Add one new row in table 677 section 15.2.3.7 in page 43, line 53 below row Capability for MIMO support

| Capability for Interference mitigation | Bit 0: DL PMI Coordination Bit 1: DL Collaborative multi-BS MIMO Bit 2: DL Closed-Loop multi-BS Macro Diversity Bit 3: UL PMI Combination |
| --- | --- |

------------------------------- End of text # 2  -------------------------------------------