| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Scheduling and QoS with Relays (Section 15.2.3, Section 15.6.2.6) |
| Date Submitted | 2009-11-06 |
| Source(s) | Gauri Joshi, Srinadh B, Abhay Karandikar, Prateek Kapadia TICET, IIT Bombay | E-mail: karandi@ieee.org (+91 9820347269) |
| Re: | IEEE 802.16m-09/0057: Letter Ballot Recirc #30a Target topic: P802.16m/D2: Section 15.6.2.6, Section 15.2.3 |
| Abstract | QoS parameters negotiated with the ABS must be used by ARS for scheduling on the access link |
| Purpose | For discussion and inclusion in 802.16m amendment |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Scheduling and QoS with relays

Gauri Joshi, Srinadh B, Abhay Karandikar, Prateek Kapadia

TICET, IIT Bombay, India

Introduction

In Section 15.6.2.6 it is stated that the ABS may impose resource usage constraints on the ARS such as frequency partitions and transmit power. But the QoS parameters of the flow are not specified by the ABS to the ARS. This will result in inefficient resource allocation by ARS for its subordinate AMSs.

Scheduling at ARS

Section 15.2.12 specifies the QoS parameters that the ABS will negotiate with the AMS. Since the ARS independently schedules its subordinate AMSs, the ARS should consider these QoS parameters while scheduling to the AMS.

The AAI_DSA-REQ and AAI_DSA-RSP messages in Section 15.2.3.40 are sent by AMS or ABS to create a new service flow. AAI_DSC-REQ and AAI_DSC-RSP are used to dynamically change the service parameters. These messages between the AMS and ABS will be relayed by the ARS.  We propose that these messages should not be encrypted (section 15.2.3). Thus, when the ARS receives a DSx  message to relay, the ARS can decode and possibly modify the message according to the ARS's own scheduling capabilities.

Proposed Text

Part 1: Add the following lines at Page 566, Line 35 (Section 15.6.2.6)

------------------------------------Start of text ---------------------------------------------------------

The ARS that relays a flow may obtain the flow's QoS parameters by decoding the DSx messages transmitted between AMS and ABS during flow establishment. The ARS can use this information to schedule air link resources to its associated AMSs. The ARS may modify the messages according to its own scheduling capabilities before forwarding them to the AMSs.

-----------------------------------End of text --------------------------------------------------------------------

Part 2: Add the following lines at Page 32, Line 57 (Section 15.2.3)

------------------------------------Start of text ---------------------------------------------------------

DSx messages should not be encrypted.

-----------------------------------End of text --------------------------------------------------------------------