| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Text Change Proposal on DL Subchannelization for Supporting OL Region (16.3.5) |
| Date Submitted | 2009-12-31 |
| Source(s) | Wookbong Lee, HanGyu Cho, Bin-Chul Ihm LG Electronics | wookbong.lee@lge.com *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | Call for comments for Letter Ballot 30b |
| Abstract | Text Change Proposal for subchannelization rule |
| Purpose | For member’s review and adoption into P802.16m_D3 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Text Change Proposal on DL subchannelization for Supporting OL Region (16.3.5)

Wookbong Lee, HanGyu Cho, Bin-Chul Ihm

LG Electronics

# Introduction

In this contribution, we modify current 802.16m draft standard (IEEE P802.16m/D3) so that we can operate OL Region correctly.

# Motivation/Rationale

An open-loop region is defined as a time-frequency resource using same number of pilot pattern and a given open-loop MIMO mode. The open-loop region allows base stations to coordinate their open-loop MIMO transmissions, in order to offer a stable interference environment where the precoders and number of MIMO streams are not time-varying.

Currently there are three kinds of open-loop region, OL region type 0, OL region type 1, and OL region type 2.

The following table shows details of OL region.

Types of open-loop regions

|  | MaxMt | MIMO Mode | MIMO feedback mode | Supported permutation |
| --- | --- | --- | --- | --- |
| OL Region type 0 | 2 streams | MIMO mode 0 MIMO mode 1 (Mt = 2 streams) | 0 | DRU |
| OL Region type 1 | 1 streams | MIMO mode 5 (Mt = 1 stream) | 1 | Miniband based CRU (diversity allocation) |
|  |  |  | 2 | Subband based CRU (localized allocation) |
| OL Region type 2 | 2 streams | MIMO mode 1 (Mt = 2 streams) MIMO mode 3 (Mt = 2 streams) | 5 | Subband based CRU (localized allocation) |

To enable the open-loop region, we need to make sure the resource units assigned for OL region shall be aligned across cells.

Since subbands are already aligned across cells, there is no problem for OL Region type 1 subband mode and OL Region type 2.

However, current subchannelization rule can’t make the OL region alignment across cell for OL Region type 0 and OL Region type 1 miniband mode since different cells have different number of subbands, minibands, or DRU.

Moreover, even though each cell has same number of subbands, minibands and DRU, the location of minibands and DRUs are not aligned due to sector/cell specific CRU/DRU allocation sequence applied for miniband and DRU mapping. (See equation (194) for more details)

This proposal is to make OL region aligned across cells for OL region type 1 miniband mode and OL region type 0.

To minimize additional complexity due to OL region, we propose to reserve number of PRUs for DLRU for subchannelization. The performance of DLRU will be almost maintained since we have another permutation for DLRU (subcarrier permutation).

Here is summary of proposed OL Region operation.

|  | Subchannelization | SCD message | Feedback Allocation/Polling A-MAP IE |
| --- | --- | --- | --- |
| Without any type of OL Region | Reserve PRUs for SLRU and DLRU before CRU/DRU permutation | Indicates there is no OL Region | Indicates measurement shall be done in midamble |
| With OL Region type 1 (SLRU mode) and/or OL Region type 2 |  | Indicates number of subbands for OL Region type 1 (SLRU) and/or OL Region type 2 | Indicates measurement shall be done in OL Region type 2 SLRU to OL MU MS (OL Region type 2) and OL Region type 1 SLRU to CDR MS (OL Region type 1 SLRU) |
| With OL Region type 0 and/or OL Region type 1 (NLRU) |  | Indicates whether OL Region type 0 and/or OL Region type 1 (NLRU) is on or not | Indicates measurement shall be done in DLRU to OL SU MS (OL Region type 0) and minibands to CDR MS (OL Region type 1 NLRU) |

# References

[1] IEEE P802.16m/D3, “DRAFT Amendment to IEEE Standard for Local and metropolitan area networks, Part 16: Air Interface for Fixed and Mobile Broadband Wireless Access Systems”

# Proposed text change

Instruction to editor;

Black text: existing D2 text

Red and strike out text: for deletion

Blue and underline text: for addition

--------------------------------------------------------Text Start -----------------------------------------------------

Modify the text in lines 10-42 in page 329 in 16.3.5.3.1 as follows

The number of DRUs in each frequency partition is denoted by LDRU,FPi, where

LDRU,FPi =FPSi-LCRU,FPi 	for 0≤ i <FPCT 			(192)

And FPSi is the number of PRUs allocated to FPi.

The mapping from PRUFPi to CRUFPi (for 0≤ i <FPCT) is given by:

(193)

where .

s[] is the CRU/DRU allocation sequence defined in Equation (194) and  .

(194)

In Equation (194), PermSeq() is the permutation sequence of length (FPSi-LSB-CRU,FPi-LDRU,FPi) and is determined by SEED = {IDcell*343} mod 210. The permutation sequence is generated by the random sequence generation algorithm specified in 16.3.5.3.3. DL_PermBase is set to preamble IDcell.

The mapping of PRUFPi to DRUFPi is given by:

(195)

where k = s[j + LCRU,FPi -LSB-CRU,FPi].

--------------------------------------------------------Text End -----------------------------------------------------