| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Signaling for Femto ABS Low-Duty Operation Mode (Section 16.4.10) |
| Date Submitted | 2009-12-31 |
| Source(s) | Andreas Maeder, Linghang Fan, Hassan Alkanani, Nader Zein, Tetsu Ikeda NEC | E-mail: andreas.maeder@nw.neclab.eu linghang.fan@eu.nec.com hassan.alkani@eu.nec.com nader.zein@eu.nec.com t-ikeda@ap.jp.nec.com |
| Re: | IEEE 802.16 Working Group Letter Ballot #30b on P802.16m/D3 |
| Abstract | Add signaling for Femto ABS low-duty operation mode. |
| Purpose | To be discussed and adopted by TGm |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Signaling for Femto ABS Low-Duty Operation Mode (Section 16.4.10)

Andreas Mäder, Linghang Fan, Hassan Alkanani, Nader Zein, Tetsu Ikeda

NEC

# Motivation

Low-duty operation mode is designed to minimize interference, power consumption, and at the same time minimize impact on AMS operation.

In order to facilitate scanning, either the Macro ABS or the Femto ABS should signal the Default LDM pattern to the AMS. In the current text in P802.16m/D3, signaling is to be included in the AAI_REG-RSP message. However, this complicates matters if operators want to change the Default LDM patterns of their deployed Femto ABS.

Additionally, the Femto ABS should signal the current operational state to the AMS.

We therefore

- Define a new MAC management message, AAI_LDM-IND, which contains information about the Default LDM pattern used by the Femto ABS.

- Include information about the operational state of the Femto ABS in the P-SFH.

[Remedy 1: Modify the text in Section 16.4.10.2 as following:]

### 16.4.10 Low-duty Operation Mode

#### 16.4.10.1 General description

Besides the normal operation mode, Femto ABSs may support low-duty operation mode, in order to reduce interference to neighbor cells.

The low-duty operation mode consists of available intervals (AI) and unavailable intervals (UAI). During an available interval, the Femto ABSs may become active on the air interface for activities such as paging, transmitting system information, ranging or for data traffic transmission. During an unavailable interval, it

does not transmit on the air interface. Unavailable interval may be used for synchronization with the overlay macro BS or measuring the interference from neighbor cells.

The Femto ABS may enter low-duty operation mode either if all AMSs attached to the Femto ABS are in idle or sleep mode, and if no AMS is in the process of network entry.

The current operational mode of the Femto ABS is indicated in the P-SFH.

#### 16.4.10.2 Default LDM pattern(s)

A Sequence of availability and unavailability intervals forms an LDM pattern. The Default LDM pattern is the iteration of one available interval and one unavailable interval. An available interval for Default LDM pattern begins with the frame including the PA-Preamble. The Default LDM pattern is a subset of the available intervals at the femto ABS.

The Default LDM pattern parameters include:

- Available interval (in units of four frames)

- Unavailable interval (in units of four frames)

- Start superframe number

Once a femto ABS enters low duty mode, the Default LDM pattern of the femto ABS may be activated.

There may be one or more default LDM patterns in a femto ABS deployment. The Default LDM pattern(s) parameters can be pre-provisioned or unicasted to the AMS during initial network entry with the femto ABS in the AAI_REG-RSP message. Changes of the Default LDM pattern can be indicated by the AAI_LDM-IND message.

[Remedy 2: Add the following entry to Table 673 in Section 16.2.3:]

| Message Name | Message Description | Security | Connection |
| --- | --- | --- | --- |
| AAI_LDM-IND | Low-duty mode indication | null | Unicast |

[Remedy 3: Add the following text to Section 16.2.3:]

#### 16.2.3.X AAI_LDM-IND

The AAI_LDM-IND message conveys information about the Default LDM pattern of a Femto ABS.

| Name | Value | Usage |
| --- | --- | --- |
| start_frame_number | Start superframe number of the new Default LDM pattern |  |
| available_interval_length | Length of available interval in units of four frames | Indicates the length of the available interval of the Default LDM pattern |
| unavailable_interval_length | Length of unavailable interval in units of four frames | Indicates the length of the unavailable interval of the Default LDM pattern |

[Remedy 4: Modify Table 799 in Section 16.3.6.5.1.1 as following:]

| Syntax | Size (bit) | Notes |
| --- | --- | --- |
| P-SFH IE format () { |  |  |
| Femto ABS operational mode | 1 | 0b0 = normal mode 0b1 = low-duty mode |
| } |  |  |