| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clarification of Sounding Channel Power Control Offset Value |
| Date Submitted | 2010-04-30 |
| Source(s) | Rongzhen Yang, Hujun Yin, Yang-seok Choi Intel Corp. | Email : Rongzhen.yang@intel.com |
| Re: | Comments on P802.16m/D5 |
| Abstract | This contribution provides the fixed version of sounding power control offset value in sounding power control section. |
| Purpose | To be discussed and adopted into P802.16m/D5 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clarification of Sounding Channel Power Control Offset Value

Rongzhen Yang, Hujun Yin, Yang-seok Choi
Intel Corp.

# Introduction

For sounding channel power control, the offset value is not clarified.

For sounding channel, there is minimum SINR value (soundingSinrMin), gammaIoT, and soudningSinrMax to provide good enough sounding power control. The necessary of offset value cannot be proved. So I suggest setting it as "0" (disabled).

# Text proposal

Instruction to editor;

Black text: existing D5 text

Red and strike out text: for deletion

Blue and underline text: for addition

[Remedy：]

[Change the text from line 60 on the page 729, section16.3.9.4.5 as follows:]

============================== Start of Proposed Text =================================

When calculated sounding SINRTarget is higher than soundingSinrMax, the SINRTarget shall be set to soundingSinrMax.

Offset for sounding channel used in Equation (290) shall be set to 0.

============================== End of Proposed Text =================================