| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Cleanup for E-MBS MAP in IEEE P802.16m (16.3.6.2.3 and 16.3.6.5.3) |
| Date Submitted | 2010-07-09 |
| Source(s) | Eunkyung Kim, Soojung Jung, Jaesun Cha, Sungcheol Chang, Hyun Lee, Chulsik Yoon ETRI 138 Gajeongno, Yusong-gu, Daejeon, 305-700, KOREA | Voice: +82-42-860-5415 E-mail: ekkim@etri.re.kr |
| Re: | “P802.16m/D6,” in response to the IEEE 802.16 Working Group Sponsor Ballot |
| Abstract | Cleanup for the E-MBS MAP supporting E-MBS Operation on IEEE 802.16m Amendment Draft Standard |
| Purpose | To discuss and adopt the proposed text in the next revision of 802.16m draft |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Cleanup for E-MBS MAP in IEEE P802.16m (16.3.6.2.3 and 16.3.6.5.3)

Eunkyung Kim, Soojung Jung, Jaesun Cha, Sungcheol Chang, Hyun Lee, Chulsik Yoon

ETRI

# Instructions

IEEE 802.16m Amendment Draft Standard ‎[1] describes the superframe header transmission with following rules.

- The Primary Superframe Header (P-SFH) shall be transmitted in every superframe.

- The first NP-SFH distributed LRUs of the first AAI subframe are allocated for P-SFH transmission. NP-SFH is 4

- The Secondary Superframe Header (S-SFH) may be transmitted in every superframe

- If the S-SFH is present, the S-SFH shall be mapped to the NS-SFH distributed LRUs following the NP-SFH distributed LRUs.

  - NS-SFH SP1 = 16

  - NS-SFH SP2 = 15

  - NS-SFH SP3 = 12

- NSFH, the number of distributed LRUs which are occupied by SFH, is NP-SFH+NS-SFH

However, E-MBS operation in the dedicated carrier may not support on less than 2 Subbands (i.e., 8 LRUs in an AAI subframe) used for SLRU in 10MHz.

In this contribution, therefore, E-MBS MAP and E-MBS MAP IE are modified to support the transmission of superframe header in the first AAI subframe of the first frame of each superframe.

# Text Proposal for the 802.16m Amendment Draft Standard

Note:

The text in BLACK color: the existing text in the 802.16m Amendment Draft Standard

The text in RED color: the removal of existing 802.16m Amendment Draft Standard Text

The text in BLUE color: the new text added to the 802.16m Amendment Draft Standard Text

[-------------------------------------------------Start of Text Proposal---------------------------------------------------]

[Remedy1: Modify the following text in 16.3.6.2.3 of 802.16m/D6]

16.3.6.2.3 Enhanced Multicast Broadcast Service MAP (E-MBS MAP)

The E-MBS MAP carries configuration information for enhanced multicast broadcast service for one E-MBS Zone. The E-MBS MAP is transmitted in the first several RUs of the E-MBS region in the beginning of the MSI. The parameters of the E-MBS region and the burst size of the E-MBS MAP is transmitted in the AAI_E-MBS-CFG MAC control message described in 16.9.3.1. The first AAI subframe, excluded from the RUs of E-MBS, of each superframe is reserved for superframe header to transmit. AAI_E-MBS-CFG Change Indication indicates any change in the parameters of AAI_E-MBS-CFG MAC Control Message at its next transmission instance.

[Remedy2: Modify the Table 867 in 16.3.6.5.3 of 802.16m/D5]

Table 867—E-MBS DATA Information Elements

| Syntax | Size (bit) | Description/Notes |
| --- | --- | --- |
| E-MBS_DATA_IE () { |  |  |
| No. of E-MBS IDs+FIDs | 8 | Total number of E-MBS streams in the IE |
| For (i=0; i< No. of E-MBS IDs +FIDs,; i++){ |  |  |
| E-MBS ID+FID | 16 | E-MBS ID + Flow ID of an E-MBS stream |
| Isize-offset | 5 | Depends on supported modes, 32modes assumed as baseline |
| MEF | 1 | E-MBS MIMO Encoding Format 0b0: SFBC 0b1: Vertical Encoding |
| If (MEF == 0b1){ |  | Parameters of Vertical Encoding |
| Mt | 1 | Number of streams for transmission for Nt =2, Nt =4, and Nt =8 (Mt <= Nt) 0b0: 1 stream 0b1: 2 streams |
| } |  |  |
| E-MBS AAI subframe offset | Variable | Includes the location of the AAI subframe where the E-MBS data burst ends and the first AAI subframe of the first frame of each superframe is reserved to transmit superframe header, where any E-MBS data burst is not transmitted. MSI == 0b00: 6bits MSI == 0b01: 7bits MSI == 0b11: 9bits |
| E-MBS Resource Indexing | 7 | Includes the location of the SLRU index where the E-MBS data burst ends |
| } | - | - |
| } |  |  |

[-------------------------------------------------End of Text Proposal----------------------------------------------------]

# References

- IEEE P802.16m/D6, “DRAFT Amendment to IEEE Standard for Local and metropolitan area networks; Part 16: Air Interface for Broadband Wireless Access systems; Advanced Air Interface,” May 2010