| Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> |
| --- | --- |
| Title | Simulation Study of the Calibration Assumptions |
| Date Submitted | 2005-05-16 |
| Source(s) | David Huo 67 Whippany Road Whippany, NJ 07981 | Voice: +1 973 428 7787 Fax: +1 973 386 4555 Email: dhuo@lucent.com |
| Re: | Simulation Calibration |
| Abstract | This document provides simulation results of the C/I distributions. |
| Purpose | Discuss and Information |
| Notice | This document has been prepared to assist the IEEE 802.20 Working Group to accomplish the simulator calibration process. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

- Introduction

Contribution [1] proposed a calibration procedure for [2]. In the following some simulation results are presented to investigate its feasibility and the needs of modifications.

- Simulation Assumption

The configuration of the simulation used the following parameters:

- Inter-cell distance is 2.5 km

- Frequency reuse factor is 1

- Path loss model for macro-suburban  with fc=2.GHz is used so that

PL= offset-35*log10(distance)+Gain_Antenna_BS+Gain_Atenna_MS,  where

offset=-28.6- BS_NOISEFIG - LOSS  (up link)

offset=-28.6- MS_NOISEFIG - LOSS (down link)

- A single antenna is used for each sector base station with radiation pattern as specified in [2] and the mobile station uses omni-directional antenna.

- Base station transmit with maximum power of 20 Watt.

- Slow fading is determined by

Z*0.5 + Gauss(sector)*0.5 dB for each sector, where Z= Gauss(network) fixed.

- Fast fading used models  VA120 km/hour and PA 30 km/hour.

- Measurement time 40.ms for the down link and 20. ms for the up link

- Simulation time is 10 seconds, corresponding to 2500 packets for down link and 10000 packets for up link.

Figure 1: Locations of sectors of a 2 tier network; unit is meter.

Figure 2 shows the locations of mobiles stations as given in the attached ascii file, where 10 mobiles per sectors are dropped.

Figure 3  shows the histogram of the transmit power of  mobiles, which is assigned following the following rule:

The mobile with the maximum path and shadowing losses in the a sector is required  to transmit at the maximum power, so that the corresponding long-term average received power at the base station can be  used as the target long-term average received power for all users in the same sector. That is, let PR be the target average received power. The transmit power of user k, PT,k, is given by PT,k = PR/Gk, where Gk is a long-term average channel gain (i.e., excluding short-term fading) of user k.

Figure 3: Histogram of Power Allocation for 10 Fixed Mobiles per Sector

- Results without Fast Fading

Figure 4 shows the histogram of the down link geometry as defined by

,

where PT,B is the (per-sector) base station maximum transmit power, Gi,m is the long-term channel gain (where the long-term channel gain is defined as the average path gain between the mobile and the base station, excluding the short-term fading) between mobile i and sector m,  s(i) indicates the serving sector of mobile i and N is the thermal noise power measured at the mobile.

Figure 5 shows the histogram of the up link geometry based on the above power allocation

Figure 4:  MS transmit power  with 30 MS per sector

Figure 4: Histogram of the Down Link Geometry with 30 MS per Sector

Figure 5: Histogram of  the up link geometry for the give power allocation scheme with 30 MS per sector

- Discussion

- For the fixed location with 10 mobiles per sector the distribution is subject to violent variation due to the small number of random numbers, i.e. the slow fading (57 numbers).  Considering the major purpose of using the fixed location is the bug fix of the programming code, we suggest to run this simulation with zero slow fading, so that the entire result is deterministic and, as such, subject to no variation. The comparison is then performed per location and no histogram is needed.

- The distribution of the geometry is far from smooth and subject to strong variation from drop to drop, indicating that not enough random numbers are involved in the experiment. The two random variables are location (30x57) and slow fading (57). To demonstrate this, we increase the number of sectors, e.g. instead of 2 tiers use a network of 3 tiers and, instead of 30 mobiles use 60 mobiles per sector. By 3 tiers we will have 37x3=111 sectors, i.e. 111 slow fading variables, and by 60 mobiles per sector 60*111=6660 mobile locations. Two drops are shown in Figure 6 and Figure 7, for down and up link, respectively

Figure 6: Histogram of down link geometry for 3 tiers and 60 mobiles per sector

Figure 6:Histogram of up link geometry for 3 tiers and 60 users per sector.

The curves become smoother when more samples are explored. Thus, we recommend to use multiple drops to get the geometry histogram. Figure 7 shows the histogram of the down link geometry for 2 tier, 30 mobiles per sector and 100 drops

Figure 7: Histogram of down link geometry for network of 2 tiers, 30 mobiles per sector and 100 drops.

- Results with Fast Fading

For 19 cells in 2 tiers we have 57 sectors. For 30 mobile for each sector we have 59*30 mobiles.

Figure 8 shows the up link C/I histogram of up link by PA-3km/hr channel, where each sector has 30 mobiles.

Figure 9 shows the down link C/I histogram by VA 120 km/hour channel, where each sector has 30 mobiles.

Figure 8.: Histogram of  Up Link C/I by PA3

Figure 9.: Histogram of  Down Link  C/I by VA120

6. Discussion

Thanks to the variety introduced by the fast fading, the curves of histogram are relative smooth and stable and, as such, allow for comparison.

Reference

[1] C802.20-04-83r6

[2] Evaluation Criteria