## Slide 1
The following are the CSD Responses in relation to the IEEE P802.3xx PAR

## Slide 2
The definition of protocol independent managed objects, to be included in Clause 30 of IEEE Std 802.3, will be part of this project.

## Slide 4
Broad Sets of Applications:
  Recent automotive architectural changes (zonal or central architecture) require automotive Ethernet rates in excess of 10Gb/s.
  High-performance cameras, CPU-to-CPU links, redundant links, sensor aggregation and “flight data recorder” systems require minimum data rates of 25 Gb/s.
Multiple vendors and numerous users:
  At the Call for Interest, 73 individuals from 44 organizations indicated they would support this project. These included automotive OEMS, automotive Tier 1, silicon, infrastructure, cabling, connector, and test equipment vendors.
  Data presented at the CFI indicate a substantial market potential, e.g., the prediction for 2025 is >100 million total ports/year.

## Slide 5
As a PHY amendment to IEEE Std 802.3, the proposed project will remain in conformance with IEEE Std 802, IEEE Std 802.1AC, and IEEE Std 802.1Q.
The proposed amendment will conform to the IEEE 802.3 MAC.
As with other IEEE 802.3 projects, a number of new PHY types will be defined.

## Slide 6
There is no IEEE 802.3 standard that supports electrical Ethernet at rates greater than 10 Gb/s for the requirements of automotive applications.
The project may define multiple PHYs, but will define only a single PHY for each rate, media, and link reach combination.

## Slide 7
The proposed project will build on the array of Ethernet component and system design experience, and the broad knowledge base of Ethernet network operation.
Full-duplex operation over a balanced twisted pair and other media has been proven both technically and operationally in deployments at rates from 2 Mb/s and higher.
Component vendors, including PHY vendors, cabling vendors and systems vendors have presented data on the feasibility of the necessary components for this project. Proposals which leverage existing technologies have been provided.
The reliability of Ethernet components and systems can be projected in the target environments with a high degree of confidence.

## Slide 8
Ethernet interfaces in the target data rate range defined by this project will maintain a favorable cost-performance balance.
The balance of costs between infrastructure and attached stations is not applicable to the automotive environment.
The cost factors for Ethernet components and systems are well known. The proposed project may introduce new cost factors which can be quantified.
Prior experience in the development of other physical layer specifications for Ethernet indicates that the specifications developed by this project will entail a reasonable cost for the resulting performance.
The reduction in the number of legacy networks requiring specialized components, expertise, and gateways in the targeted markets will result in a significant drop in both installation and operational costs.
Overall costs are minimized by introducing Ethernet network architecture, management, and software into the automotive environment.
Migrating automotive networking to Ethernet results in a significant improvement in system price/performance.